## Slide 1: Clarifications for OBSS_PD-based SR parameters
Date: 2016-07-25
Authors:
July 2016
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | laurent.cariou@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Fengming Cao |  |  |  | 

## Slide 11: Authors (continued)
Name | Affiliation | Address | Phone | Email
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com

## Slide 12: Part 1 – OBSS_PD-based SR parameters Motivation
The spec defines a spatial reuse mode that we call here OBSS_PD-based SR for clarification, and which is defined in 25.9.2 and 25.9.3.
In the SFD, we agreed that the TxPower and OBSS_PD can be adjusted based on a proportional rule (shown next slide).
We need to define in the spec:
  Default parameters for this proportional rule
  how to set/adjust the different values in this proportional rule.
This contribution proposes solution for that
July 2016

## Slide 13: OBSS_PD-based SR mode proportional rule
Preserves fairness for the lower power devices
PWRref can be a TBD level (preferred value is 23 dBm)
Class A: TX_PWR=transmit power
Class B: TX_PWR=transmit power+TBD dB
July 2016

## Slide 14: OBSS_PD-based SR mode
3 parameters need to be defined for the equation between TxPower and OBSS_PD:
  OBSS_PDmin
  PWRref
  OBSS_Pdmax
We need to define how to set the values of the parameters
  default values
  Method to change the values of the parameters (set by the AP)
July 2016

## Slide 15: Proposal for default parameters
We propose to define default parameters that are conservative
  In unmanaged environments, OBSS_PD-based SR is still efficient even with conservative parameters, and the impact on legacy is ensured to be limited
  We propose the following default values:
    OBSS_Pdmax should be defined in the spec to -62dBm
    PWRref should be set to a fixed value: 21dBm for STAs or APs with less than 3 SSs, 25dBm for APs with 3 SSs or more
    OBSS_Pdmin should be equal to -82dBm for 20MHz
July 2016

## Slide 16: Default parameters
21dBm
STAs
-62dBm
-72dBm
-82dBm
ETSI ED
Legacy
OBSS_Pdmin_default=-82dBm
OBSS_Pdmax_default=-62dBm
PWRref
OBSS_PD
TX_PWR
25dBm
APs
July 2016

## Slide 17: Allow AP to set these parameters to different values for managed networks
In managed environments, the APs (usually managed by a controller) have a good knowledge of the environment and can define OBSS_Pdmin/max that better suits the environment
  It makes sense to allow APs to set OBSS_Pdmin and OBSS_Pdmax for their BSS in managed environments to maximize spatial reuse gain
Only managed APs should be able to change these parameters
  It is still TBD how we restrict these changes
July 2016

## Slide 18: Illustration of OBSS_Pdmin modifications
25dBm
-62dBm
-72dBm
-82dBm
LAA
Legacy
OBSS_Pdmin=-72dBm (set by managed AP)
PWRref
OBSS_PD
TX_PWR
OBSS_Pdmin_default=-82dBm
OBSS_Pdmax_default=-62dBm
July 2016

## Slide 19: Proposal
the AP can define specific OBSS_PDmin and OBSS_Pdmax values that can be used by its STAs under TBD conditions
    OBSS_PDmin_default <= OBSS_PDmin <= ED threshold
    OBSS_PDmin <= OBSS_PDmax
The parameters OBSS_PDmin and OBSS_PDmax are defined in a new information element, called Spatial Reuse element
  Note: the TBD conditions will define how to apply this only on managed networks

## Slide 20: Part 2 – Disallow flag in HE SIG-A SR field
Specification Framework Document says:
  Include the “SR_disallowed” signaling in HE-SIGA to indicate whether SR operation is allowed or not.
  use a value of Spatial Reuse field to indicate SR is disallowed
  The conditions to disallow SR are TBD
We propose to clarify the operation on “SR disallowed” entry
  There are now 2 SR modes:
    OBSS_PD-based SR
    SRP-based SR
  We should define what SR mode is disallowed
We propose to define conditions to disallow

## Slide 21: Recap on SRP-based SR operation
SR field (in SIG A) for HE Trigger-Based PPDU is defined as follows
  One TBD value for SR Disallow Flag, (under TBD restrictions)
  One TBD value is reserved
  Remaining 14 values for SRP
    SRP = TX PWRAP + Acceptable Receiver Interference LevelAP
SRP-based SR mode:
  SR STA shall back-off its TX power based on
  TX PWRSR STA < SRP –RSSItrigger frame@SR STA
  Other TBD conditions

## Slide 22: Proposal for “SR disallowed” Entry
this “SR disallowed” flag set in SR field in HE-SIGA only disallows SRP-based SR

## Slide 23: Conditions to disallow SRP-based SR
AP should be able to control the setting for “SR_Disallowed” entry in SR field HE-SIGA to disallow the SRP-based SR operation.
AP can request that the STAs associated with it shall set the SR field to the “SR disallowed” entry for all their transmitted PPDUs.
STAs transmitting NDP or FTM frames shall set “SR disallowed” entry in SR field in HE-SIGA.
  NDP(Null Data Packet) is used for sounding for STA to measure the channel quality
  FTM(Fine timing measurement) is used for indoor location
  …

## Slide 24: Conclusion
Part 1
We propose to fill the TBDs in the spec by defining default parameters for OBSS_Pdmin/max and PWRref
We propose for the AP to be able to tune these parameters
Part 2
We propose to clarify that SR_disallow in HE-SIGA only disallow SRP-based SR
We propose some conditions where STAs must disallow SRP-based SR
July 2016

## Slide 25: Straw poll #1
Do you agree to accept the proposed text changes in document “11-16/947r4, Proposed Text Changes for OBSS_PD-based SR parameters”?
  Y/N/A
July 2016