## Slide 1
Consideration on Multi-STA BlockAck Optimization
Date: 2016-09-13
Authors:

## Slide 2: Introduction
In the spec draft, Block Acknowledgement procedures for UL MU and some Ack optimization methods are agreed:
  When receiving frames from more than one STA that are part of an UL MU transmission (see 9.42.2) and that require an immediate acknowledgement an AP may send either multiple BlockAck frames (or Ack(#1408) frames) in an HE MU PPDU, or a Multi-STA BlockAck frame (see 25.4 (Block acknowledgement)).
  If the Ack Type field is 1, then the STA Info field indicates either the acknowledgement of a single MPDU identified by the value of the TID or of all MPDUs carried in the eliciting PPDU, when the TID field is set to 14.
  MPDUs with multiple TIDs that ask for Ack and/or BA acknowledgement and a management frame that asks for Ack acknowledgement may be aggregated in one A-MPDU of MU transmission.
However, more effort for Ack optimization is needed, because Ack mode is not enough in case of many user
In this presentation, we discuss further optimization method for BlockAck as proposed in CID 2389, 2395

## Slide 3: Problem: BA length exceeds EIFS
The duration for BA procedures lasts up to milliseconds
Hidden STAs may send Data frames after EIFS duration, which makes collision

## Slide 4: Recap: Multi-STA BA length selection
In [2] the length of M-BA with fragmentation is decided
  Depending on Fragment Number subfield value, the length of BlockAck bitmap varies from 4 octets to 32 octets

## Slide 5: Recap: Ack/BA mode for Multi-STA BA
In Draft, Ack/BA mode for single MPDU and all MPDUs in multi-TID A-MPDU is agreed
  If the Ack Type(#1408) subfield is (#2185)1 and the TID value of the Per AID TID Info subfield is less than 8 or equal to 15, then the Block Ack Starting Sequence Control and Block Ack Bitmap subfields(#1274) are not present and the Per STA Info subfield(#1141) acknowledges(#Ed) successful reception of a single MPDU indicated by the TID of the Per AID TID Info subfield. (#2414)(#2582)
  If the Ack Type subfield is 1 and the TID subfield of the Per AID TID Info field is 14, then the Block Ack Starting Sequence Control and Block Ack Bitmap are not present and the Per STA Info field acknowledges(#Ed) successful reception of all the MPDUs carried in the eliciting A-MPDU.

## Slide 6: The Ack duration problem
The Ack duration extends up to more than 3ms, even though it assumes 4 octet length in BlockAck bitmap
Also, using Ack Type field is not enough, because in many user cases, it exceeds EIFS even though all of M-BA has 0 in Ack Type field
EIFS excess problem may cause the retransmission of UL STAs due to corrupted BlockAck.
  Ack protection or further Ack optimization is needed

## Slide 7: Additional Ack Optimization method
All STA All Ack
  In case of A-MPDUs from all AIDs are received successfully, AP may use a specific AID in Multi-STA BlockAck frame to indicate the all frames from all triggered STAs are successfully received

## Slide 8: Conclusion
In this presentation, we continued to discuss the Ack optimization method
  There are some methods to reduce the duration of Ack procedure, including adjusting length of Ack Bitamap, Ack/BA mode, and Ack mode M-BA for Multi-TID A-MPDU
However, though all of triggered frame is sent successful, Ack duration exceeds EIFS even though all of M-BA has 1 in Ack Type field for many user case
We present the further optimization method, in case all of triggered STAs’ transmission is successful
  All AID Ack mode with group AID

## Slide 9: Straw Poll 1
Do you agree to add to the spec draft?
  9.3.1.9.7 Multi-STA BlockAck variant
  …
  If the Ack Type subfield is 1, the AID value of the Per AID TID Info field is set to 1ess than 2047, and the TID subfield of the Per AID TID Info field is 14, then the Block Ack Starting Sequence Control and Block Ack Bitmap are not present and the Per STA Info field acknowledges successful reception of all the MPDUs carried in the eliciting A-MPDU. The Ack Type field is not set to 1 when responding to a BlockAckReq frame or an MU-BAR frame. If the ACK Type field is 1, the AID value of the Per AID TID Info subfield is set to 2047 and the TID value of the Per AID TID Info subfield is set to 14, then the Block Ack Starting Sequence Control and Block Ack Bitmap are not present and the single Per STA Info field indicates the acknowledgement of successful reception of all the A-MPDUs of all the STAs elicited by the trigger frame.

## Slide 10: Reference
[1] IEEE P802.11ax D0.4
[2] IEEE 802.11-16/616r2 “BlockAck generation and selection rules”
[3] IEEE 802.11-15/626r1 “Further consideration for Multi-STA BlockAck frame”
[4] IEEE 802.11-15/1065r1 “UL multi-TIDs aggregation”
[5] IEEE 802.11-16/0069r0 “Multi-TID A-MPDU in MU Transmission”
[6] IEEE 802.11-16/868r0 “CIDs for Section 9.3.1.9.7 Multi STA BAs ”