## Slide 1: EDCA rules - follow up 1
Date: 2016-07-28
Authors:

## Slide 2: Introduction
Based on the motion passed in May meeting, The following concepts are present in the TGax SFD[1]
  Allow the AP to choose any access category for contending to send the trigger frame
  • The chosen AC may give to the AP higher priority in accessing the channel
  compared to its associated STAs
There were some further discussions about more details related to the above approved motion should be specified[2, 3]
  How to choose AC for a trigger frame
  How to use different set of EDCA parameter
In this contribution, we would like to discuss about how to choose AC for AP to contend channel sending trigger frames.

## Slide 3: Proposal – option 1
How to choose AC for a trigger frame
  The trigger frame should have the same AC as the outstanding UL MPDU/A-MPDU reported by the STAs in BSR.
    In case of that the trigger frame is going to solicit multiple TID UL MPDU/A-MPDU, the trigger frame may be allowed to choose the highest priority AC among the multiple TID UL MPDU/A-MPDU.

## Slide 4: Proposal – option 1(con’t)
How to choose AC for a trigger frame
  The trigger frame should have the same AC as the outstanding UL MPDU/A-MPDU reported by the STAs in BSR.
    Example: AP may provide
    differentiated priorities using similar
    way of the current EDCA reference
    model for virtual UL transmit queues
    which are based on BSR information.
DL transmit queues with EDCA reference model

## Slide 5: Proposal – option 1(con’t)
How to choose AC for a trigger frame
  The trigger frame should have the same AC as the outstanding UL MPDU/A-MPDU reported by the STAs in BSR.
    Example: AP may provide
    differentiated priorities using similar
    way of the current EDCA reference
    model for virtual UL transmit queues
    which are based on BSR information.
(b) Virtual UL transmit queue with EDCA reference model

## Slide 6: Proposal – option 2
How to choose AC for a trigger frame
  The AP is allowed to always choose the highest AC for sending the trigger frame.

## Slide 7: SP
Which option do you prefer
  Option 1
    The trigger frame should have the same AC as the outstanding UL MPDU/A-MPDU reported by the STAs in BSR.
      In case of that the trigger frame is going to solicit multiple TID UL MPDU/A-MPDU, the trigger frame may be allowed to choose the highest priority AC among the multiple TID UL MPDU/A-MPDU.
  Option 2
    The AP is allowed to always choose the highest AC for sending the trigger frame

## Slide 8: References
11-15-0132-17-00ax-spec-framework, May 2016
11-16-0762-00-00ax-edca-rules-for-sending-trigger-frames, June 2016
11-16-0768-00-00ax-tgax-teleconference-minutes-from-june-to-july-2016