## Slide 1: EDCA rules - follow up 1
Date: 2016-07-28
Authors:

## Slide 2: Introduction
Based on the motion passed in May meeting, The following concept was presented in the TGax SFD[1]
  Allow the AP to choose any access category for contending to send a trigger frame
  • The chosen AC may give to the AP higher priority in accessing the channel
  compared to its associated STAs
There were some further discussions about more details related to the above approved motion should be specified[2, 3]
  How to choose AC for a trigger frame
  How to use different set of EDCA parameters
In this contribution, we would like to discuss about how to choose AC for AP to contend channel sending trigger frames.

## Slide 3: Background
Current EDCA rules

## Slide 4: Proposal – option 1
How to choose an AC for a trigger frame
  The AC of a trigger frame should follow the same EDCA rule for the outstanding UL MPDU/A-MPDU reported in the BSRs of STAs.
    An AP maintains another set of EDCA queues for UL data (UL_EDCA). The information of the outstanding UL data comes from BSRs
    The AP follows the same EDCA rule to transmit data in UL_EDCA queues
    Trigger frames are generated based on the information of the primary queue
    A trigger frame allows to include the secondary AC if there are more UL transmission time and all data in the primary AC are scheduled.

## Slide 5: Proposal – option 1(con’t)

## Slide 6: Proposal – option 2
How to choose AC for a trigger frame
  The AP is allowed to choose the highest AC for sending a trigger frame.

## Slide 7: Proposal – option 3
How to choose AC for a trigger frame
  No need to clarify specification language further
    Allow the AP to choose any access category for contending to send a trigger frame
      The chosen AC may give to the AP higher priority in accessing the channel compared to its associated STAs

## Slide 8: SP
Which option do you prefer
  Option 1: As described in page 4
  Option 2
    The AP is allowed to choose the highest AC for sending the trigger frame
  Option 3
    No need to clarify specification language further

## Slide 9: References
11-15-0132-17-00ax-spec-framework, May 2016
11-16-0762-00-00ax-edca-rules-for-sending-trigger-frames, June 2016
11-16-0768-00-00ax-tgax-teleconference-minutes-from-june-to-july-2016