## Slide 1: EDCA rules - follow up 1
Date: 2016-07-28
Authors:

## Slide 2: Introduction
Based on the motion passed in May meeting, The following concept was presented in the TGax SFD[1]
  Allow the AP to choose any access category for contending to send a trigger frame
  • The chosen AC may give to the AP higher priority in accessing the channel
  compared to its associated STAs
There were some further discussions about more details related to the above approved motion should be specified[2, 3]
  How to choose AC for a trigger frame
  How to use different set of EDCA parameters
In this contribution, we would like to discuss about how to choose AC for AP to contend channel sending trigger frames.

## Slide 3: Background
Current EDCA rules

## Slide 4: Proposal – option 1
How to choose an AC for a trigger frame
  The AC of a trigger frame should be the same as the data which is being solicited by the trigger frame
  The AP may use any set of EDCA parameters that it chooses (baseline)
  The AP uses the same EDCA parameters for trigger frames as for other frames
    If the trigger allows other AC frames in the response, then the AC of the trigger frames corresponds to the primary AC.
    A trigger frame allows responders to include frames belonging to the secondary AC if there is more UL transmission time and all data in the primary AC is scheduled.

## Slide 5: Proposal – option 1(con’t)

## Slide 6: Proposal – option 2
How to choose AC for a trigger frame
  The AP may choose the highest AC for sending a trigger frame, regardless of the AC of the data that the trigger is soliciting. The AP may choose a lower AC than the data that it is soliciting.
  The AP may use any set of EDCA parameters that it chooses (baseline)
  The AP uses the same EDCA parameters for trigger frames as for other frames
    If the trigger allows other AC frames in the response, then the AC of the trigger frames corresponds to the primary AC
    A trigger frame allows responders to include frames belonging to the secondary AC if there is more UL transmission time and all data in the primary AC is scheduled.

## Slide 7: SP
Which option do you prefer to add to TGax draft
  Option 1: As described in page 4
  Option 2: As described in page 6

## Slide 8: References
11-15-0132-17-00ax-spec-framework, May 2016
11-16-0762-00-00ax-edca-rules-for-sending-trigger-frames, June 2016
11-16-0768-00-00ax-tgax-teleconference-minutes-from-june-to-july-2016