## Slide 1: EDCA rules follow up 1
Date: 2016-09-13
Authors:

## Slide 2: Introduction
Based on the motion passed in May meeting, The following concept was presented in the TGax SFD[1]
  Allow the AP to choose any access category for contending to send a trigger frame
  • The chosen AC may give to the AP higher priority in accessing the channel
  compared to its associated STAs
There were some discussions about the proposed text for the approved motion [2, 3]

## Slide 3: Previous proposed text: option 1
An AP is allowed to choose any access category (AC) for contending the channel to send a trigger frame. The chosen AC may give to the AP higher priority in accessing the channel compared to its associated STAs.
  Discussion: in base line, it is specified that “a beamformer may send a VHT NDP announcement frame or Beamforming Report Poll frame using any access category”, which may allow the beamformer to send a VHT NDP announcement frame or Beamforming Report Poll frame with high priority. In the similar sense, we propose the above text to allow AP sending trigger frame with high priority in TGax draft.

## Slide 4: Previous proposed text: option 2
The AC of a trigger frame should be the same as the data which is being solicited by the trigger frame
The AP may use any set of EDCA parameters that it chooses (baseline)
The AP uses the same EDCA parameters for trigger frames as for other frames
note:
  If the trigger allows other AC frames in the response, then the AC of the trigger frames corresponds to the primary AC.
  A trigger frame allows responders to include frames belonging to the secondary AC if there is more UL transmission time and all data in the primary AC is scheduled.

## Slide 5: Previous proposed text: option 3
The AP may choose the highest AC for sending a trigger frame, regardless of the AC of the data that the trigger is soliciting. The AP may choose a lower AC than the data that it is soliciting.
The AP may use any set of EDCA parameters that it chooses (baseline)
The AP uses the same EDCA parameters for trigger frames as for other frames
note:
  If the trigger allows other AC frames in the response, then the AC of the trigger frames corresponds to the primary AC
  A trigger frame allows responders to include frames belonging to the secondary AC if there is more UL transmission time and all data in the primary AC is scheduled.

## Slide 6: Proposal
An AP may send the Trigger frame using any access category and follows the rules defined in 10.22.2 (HCF contention based channel access (EDCA)) for obtaining and sharing the TXOP.

## Slide 7: SP
Do you agree to add the following sentence to the section 25.5.2.2.3 AP access procedures for UL MU operation on page 92 line 31:
  An AP may send the Trigger frame using any access category and follows the rules defined in 10.22.2 (HCF contention based channel access (EDCA)) for obtaining and sharing the TXOP.
Discussion here is also contained in 11-16/0762r1

## Slide 8: References
11-15-0132-17-00ax-spec-framework, May 2016
Draft P802.11ax D0.4
11-16-0762-00ax-edca-rules-for-sending-trigger-frames
11-16-0962-04-00ax-edca-rules-follow-up-1