## Slide 1: EDMG Header-B Encoding and Modulation for SC PHY in 11ay
Date: 2016-07-25
Authors:

## Slide 2: Introduction
This presentation defines the EDMG Header-B encoding and modulation for SC PHY MU-MIMO transmission, [1].
The proposed method is based on the encoding and modulation defined for the legacy SC PHY in 11ad standard, [2].

## Slide 3: EDMG Header-B Format
Proposed Header-B bit content:
  The exact bit content of Header-B is not defined yet;
  It is proposed:
    First 7 bits (b1, b2, …, b7) – define scrambler seed per user (or STA);
    The total header size it is proposed to limit by 64 bits;
  The rest of bits may define the PSDU length in bytes per user;
  EDMG-MCS per user;
  Other parameters;

## Slide 4: EDMG Header-B Encoding
EDMG Header-B encoding steps, [2]:
  Data scrambling:
    b = (b1, b2, …, b64) – input bits of Header-B;
    s = (01, 02, 07, s1, s2, …, s57) – s1, s2, …, s57 are first 57 bits at the output of scrambler with initial seed value (b1, b2, …, b7);
    bs = b × s; × - defines bitwise XOR of two vectors;
  Data encoding:
    c = (bs1, bs2, …, bs64, 01, 02, …, 0440, p1, p2, …, p168) – LDPC codeword;
    HcT = 0 – encoding, H is a 168 x 672 LDPC ¾ parity check matrix;
    c1 = (bs1, bs2, …, bs64, p1, p2, …, p160) – codeword #1, shortening of zero bits, puncturing of tail parity bits;
    c2 = (bs1, bs2, …, bs64, p1, p2, …, p152, p161, p162, …, p168) – codeword #2, shortening of zero bits, puncturing of middle parity bits;

## Slide 5: EDMG Header-B Encoding (Cont’d)
EDMG Header-B encoding steps (cont’d):
  Resulting codeword:
    c = (c1, c2) – codeword of length 448 bits;
  Codeword scrambling:
    s = (01, 02, …, 0224, s1, s2, …, s224) - s1, s2, …, s224 are first 224 bits at the output of scrambler with initial seed value (11, 12, …, 17);
    cs = c × s - bitwise XOR of two vectors;

## Slide 6: Header-B MU-MIMO Transmission
Access Point (AP) transmits one stream per user:
  NSTS – total number of space-time streams;
  “i” – space-time stream index, i=1:NSTS;
  During MU-MIMO transmission each user (or STA) has its own scrambler initial seed value bi = (b1, b2, …, b7)i depending on the space-time stream index “i”;
  If each user has single stream, then the initial seed selection guarantees that each user will have its own unique code vector csi;

## Slide 7: Header-B MU-MIMO Transmission (Cont’d)
If AP transmits N streams per user:
  AP creates more than one codeword per user transmitted in different space-time streams;
  N codewords for N streams are obtained by the bitwise XOR operation applied to the original codeword:
    cs1 = c × s1, cs2 = c × s2, … csN = c × sN;
    c – original code vector introduced above;
    s1 = (01, 02, …, 0224, s1, s2, …, s224) – scrambler vector for stream #1;
    s2 = (s225, s226, …, s672) – scrambler vector for stream #2;
    …
    sN = (s(N-1)*448-224+1, s(N-1)*448-224+2, …, sN*448-224) – scrambler vector for stream #N;
    All bits: s1, s2, …, sN*448-224 are obtained from the output of scrambler with initial seed (11, 12, …, 17);

## Slide 8: Header-B Modulation & Symbol Blocking
Header-B modulation:
  Each codeword csi for space-time stream with index “i” is modulated using π/2-BPSK modulation;
  It provides a SC symbol block blki of length 448 chips for the i-th stream;
  Each block blki is prepended with Guard Interval (GI) which is a Golay Gai64 sequence of length 64 chips;
  {Gai64, i=1:NSTS} – comprises the set of mutually orthogonal Ga Golay sequences;
  This provides a regular SC symbol blocking for the i-th space-time stream as follows:
    [Gai64, blki];

## Slide 9: Symbol Blocking for Channel Bonding
Symbol blocking in case of channel bonding:
  NCB = 2, 3, 4 – channel bonding factor;
  NGI CB = 64 * NCB = 128, 192, 256 – Guard Interval (GI) length in case of channel bonding;
  The symbol block blki is repeated NCB number of times to support different channel bonding factors:
    NCB = 2: [Gai128, blki, blki];
    NCB = 3: [Gai192, blki, blki, blki];
    NCB = 4: [Gai256, blki, blki, blki, blki];

## Slide 10: Conclusions
This presentation defines the EDMG Header-B encoding and modulation for SC PHY.

## Slide 11: Straw Poll #1
Would you agree to insert the following in the SFD:”
  The 11ay specification shall define first 7 bits of EDMG-Header-B for scrambler seed value and define the total number of bits to 64 as in the legacy 11ad header.
  “

## Slide 12: Straw Poll #2
Would you agree to insert the following in the SFD:”
  The 11ay specification shall define encoding and modulation method for EDMG-Header-B as described in the 11-16-0989-00-00ay.
  “

## Slide 13: References
11-15-1358-04-00ay-specification-framework-for-tgay
Draft P802.11REVmc_D5.4