## Slide 1: 2 sets of EDCA parameters
Date: 2016-xx-xx
Authors:
Name | Affiliation | Address | Phone | Email
Laurent Cariou | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | laurent.cariou@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Robert Stacey |  |  |  | robert.stacey@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com
July 2016

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com
July 2016

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com
July 2016

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com
July 2016

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com
July 2016

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com
July 2016

## Slide 7: Authors (continued)
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 
July 2016

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
July 2016

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com
July 2016

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Fengming Cao |  |  |  | 
July 2016

## Slide 11: Authors (continued)
Name | Affiliation | Address | Phone | Email
Minho Cheong | Newracom, Inc. | 9008 Research Dr, Irvine, CA 92618 | +1-949-390-7146 | minho.cheong@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Yongho Seok |  |  |  | yongho.seok@newracom.com
Daewon Lee |  |  |  | daewon.lee@newracom.com
Yujin Noh |  |  |  | yujin.noh@newracom.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
July 2016
Evgeny Khorov | IITP RAS |  |  | khorov@frtk.ru
Anton Kiryanov |  |  |  | ant456@ya.ru

## Slide 12: Motivation: Improving HE STAs UL performance
802.11ax defines UL MU channel access, where AP triggers STAs transmissions
HE STAs can also access the channel with EDCA
To ensure overall improved HE STAs performance, we need to ensure that the access delay for trigger frame transmissions is short and there are no collisions
This can be achieve by the combination of:
  Increasing AP channel access
  Decreasing STAs EDCA access when scheduled
July 2016

## Slide 13: Proposal: Improving HE STAs UL performance
Improved efficiency is obtained by favoring MU transmissions with the following two solutions:
  AP increases its channel access probability to accommodate large set of UL transmissions
    AP channel access should be proportional to traffic load
      AP accesses channel for all HE STAs in UL MU and DL
    HE STAs performance depends on the AP channel access to trigger them in UL MU
  HE non-AP STA lowers EDCA channel access probability, only when they are scheduled by the AP
    The AP and the STAs both contend to access the channel for the same traffic
      This may cause collisions and lower performance
      This has been demonstrated in [1]
In this presentation, we address HE non-AP STAs EDCA only
July 2016

## Slide 14: 2 set of EDCA parameters
We propose to define 2 sets of EDCA parameters:
  One that we call legacy EDCA parameters that are used by legacy STA and HE STA in SU mode
  Another one that we call MU EDCA parameters that are used by HE STA in MU mode and are defined to be more restrictive than legacy EDCA parameters to favor MU transmission.
A set of rules is required for the HE-STAs to choose between two sets of parameters so that the needs of improving efficiency and reducing latency can be satisfied
July 2016

## Slide 15: Set of rules to select the EDCA parameters
The rationale behind the proposed conditions is for a STA:
  to operate with the MU EDCA parameters only when it can trust that the AP will efficiently schedule its traffic with UL MU,
  and to be able to operate with the legacy EDCA parameters when the AP has not been informed and has not yet initiated UL MU scheduling.
July 2016

## Slide 16: Set of rules to select the EDCA parameters
Condition to switch from legacy EDCA parameters to MU EDCA parameters is TBD
  (TBD) EDCA parameter changes can be AC-specific or for all ACs
July 2016

## Slide 17: Set of rules to select the EDCA parameters
Condition to switch from MU EDCA parameters to legacy EDCA parameters
  the STA can switch back to the legacy EDCA parameters if the STA has not been scheduled after a pre-defined TimeOut after the last time the STA was scheduled by Basic variant Trigger frame in UL MU.
    timeout starts from end of basic variant Trigger
July 2016

## Slide 18: Signaling MU EDCA Parameters
What MU EDCA parameters to define:
  CWmin/CWmax, AIFSN: for each AC
  A specific value of AIFSN defines that no EDCA access is possible
How to signal:
  A new IE is introduced to provide MU EDCA parameter set
    It can be called MU EDCA Parameter Set element
July 2016

## Slide 19: Conclusion
We proposed 2 set of EDCA parameters for 11ax.
We propose some rules for the STA to determine which set of EDCA parameters to use.
July 2016

## Slide 20: Straw poll #1
Do you agree that:
  The spec defines 2 sets of EDCA parameters (one being the current legacy EDCA parameters, one new set called MU EDCA parameters) for non-AP HE-STA
  MU EDCA parameters are signaled with a new IE called MU EDCA Parameter Set element:
      This IE includes for each AC the following parameters:
        CWmin/Cwmax, AIFSN
        A specific value of AIFSN defines no EDCA access
Note:
  When scheduling HE STAs in UL MU, the AP can have a more aggressive EDCA access
July 2016

## Slide 21: Straw poll #2
Do you agree that:
  the STA operating with MU EDCA parameters can switch back to the legacy EDCA parameters:
    if the STA has not been scheduled after a pre-defined TimeOut after the last time the STA was scheduled by Basic variant Trigger frame in UL MU.
      timeout starts from end of basic variant Trigger
July 2016

## Slide 22: Reference
[1] 11-16-684r2 Channel access efficiency, Evgeny Khorov (IITP RAS)
July 2016

## Slide 23: Annex
July 2016

## Slide 24: Scenario Description
All nodes are
in the RX range of each other
No hidden STAs
AP
N 802.11ax STAs
N legacy STAs
The AP uses EDCA to access the channel. When the AP wins contention, it grants resources for 11ax associated STAs.
An 11ax STA uses EDCA to access the channel. When it wins contention, it transmits a frame. Apart form that, the STA will transmit a frame after it receives a Trigger frame from the AP.
A legacy STA uses EDCA to access a channel. When it wins contention, it transmits a frame.
All STAs use RTS/CTS.
July 2016

## Slide 25: Scenario Parameters
Parameter | Value
Traffic mode | Saturated
Duration of the EDCA transmission | 4 ms
Duration of Trigger-based transmission initiated by the AP | 4.1ms
СWmin default | 16
СWmax default | 1024
July 2016

## Slide 26: Results with Legacy Parameters: OFDMA TXs are Rarely Used
Chart: Percentage of OFDMA TXs vs Number of STAs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 0.33333 | 0.20023 | 0.14265 | 0.11111 | 0.090558 | 0.077089 | 0.066508 | 0.058976 | 0.052484 | 0.047905
The percentage of OFDMA TXs is low, which degrades efficiency of 11ax networks.
Non-OFDMA TXs result in high overhead for short packets
OFDMA allows using higher MCS by taking into account frequency selective fading and
by increasing power efficiency
To be both efficient and fair, the percentage of OFDMA TXs shall be close to 50 since the number of legacy STAs = the number of 11ax STAs.
Chart: Number of OFDMA TXs per second vs Number of STAs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 81.7563 | 49.2375 | 35.0939 | 27.3297 | 22.2666 | 18.9467 | 16.3387 | 14.4818 | 12.8819 | 11.7529
July 2016

## Slide 27: Results with Legacy Parameters: Percentage of Legacy STAs TXs is Fair
The percentage of legacy TXs is 33%-50% which we call fair.
11ax STAs obtain a bit more channel time than legacy ones because of AP’s Trigger frames. It is not a critical issue.
Percentage of Legacy STAs TXs shall be kept the same.
Chart: Percentage of Legacy STAs TXs vs Number of STAs
| 2 | 4 | 6 | 8 | 10 | 12 | 14 | 16 | 18 | 20
 | 0.33333 | 0.39932 | 0.42796 | 0.44444 | 0.45472 | 0.46254 | 0.46794 | 0.47181 | 0.47236 | 0.47605
July 2016

## Slide 28: Changing CWmin and CWmax for AP, N=1
Total number of transmissions is ~250 which is 100%.
By prioritizing the AP, we can increase percentage of OFDMA TXs up to 100%,
but at the same time we block legacy STAs.
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.0065652 | 0.074228 | 0.18035 | 0.0065778 | 0.076361 | 0.20569 | 0.29884 | 0.0065778 | 0.077392 | 0.21293 | 0.32235 | 0.3852 | 0.0065778 | 0.077533 | 0.21617 | 0.33333 | 0.40742
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 240.2992 | 207.1343 | 155.8943 | 240.2253 | 205.9053 | 143.6561 | 98.5332 | 240.2253 | 205.6028 | 139.8053 | 87.1039 | 56.4419 | 240.2253 | 205.5344 | 138.2335 | 81.7566 | 45.0002
CWmin-CWmax
Target area
Target area
Performance with Legacy parameters
July 2016

## Slide 29: Changing CWmin and CWmax for AP, N=10
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.094813 | 0.25703 | 0.32376 | 0.11389 | 0.30018 | 0.37746 | 0.41144 | 0.12249 | 0.33214 | 0.40167 | 0.43592 | 0.45562 | 0.14563 | 0.401 | 0.45491 | 0.47225 | 0.48288
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
194,9526943 117,1399556 83,44633031 186,4938929 96,35233778 59,13688488 42,76555875 182,3057054 82,51831837 45,77609911 29,20651274 21,45043931 171,0307816 47,79659863 21,79342828 11,60113412 6,451057334 | 194.9527 | 117.14 | 83.4463 | 186.4939 | 96.3523 | 59.1369 | 42.7656 | 182.3057 | 82.5183 | 45.7761 | 29.2065 | 21.4504 | 171.0308 | 47.7966 | 21.7934 | 11.6011 | 6.4511
By prioritizing the AP, we can increase percentage of OFDMA TXs,
but at the same time we block legacy STAs.
The number of OFDMA TXs is too low
Performance with Legacy parameters
July 2016

## Slide 30: Changing CWmin and CWmax for AP, fix CWmin = 64 for 11ax STAs, N=10
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.091002 | 0.33602 | 0.46929 | 0.09864 | 0.39181 | 0.55068 | 0.62139 | 0.10143 | 0.42983 | 0.59086 | 0.66869 | 0.70319 | 0.10419 | 0.50532 | 0.66531 | 0.72493 | 0.75645
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
210,4624175 133,8731016 94,19238237 207,8737781 116,6503765 70,05051472 49,4337766 207,0472621 105,6087376 57,59233917 35,24368008 25,12620179 205,8776516 82,99904805 36,0630794 17,70145305 9,327909461 | 210.4624 | 133.8731 | 94.1924 | 207.8738 | 116.6504 | 70.0505 | 49.4338 | 207.0473 | 105.6087 | 57.5923 | 35.2437 | 25.1262 | 205.8777 | 82.999 | 36.0631 | 17.7015 | 9.3279
By prioritizing the AP and deprioritizing 11ax STAs,
we can increase percentage of OFDMA TXs to the desired level,
while keeping fair percentage of legacy STAs’ TXs.
Values, which meet requirements
Performance with Legacy parameters
July 2016

## Slide 31: Changing CWmin and CWmax for AP, fix CWmin = 128 for 11ax STAs, N=10
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.091002 | 0.33602 | 0.46929 | 0.09864 | 0.39181 | 0.55068 | 0.62139 | 0.10143 | 0.42983 | 0.59086 | 0.66869 | 0.70319 | 0.10419 | 0.50532 | 0.66531 | 0.72493 | 0.75645
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
210,4624175 133,8731016 94,19238237 207,8737781 116,6503765 70,05051472 49,4337766 207,0472621 105,6087376 57,59233917 35,24368008 25,12620179 205,8776516 82,99904805 36,0630794 17,70145305 9,327909461 | 210.4624 | 133.8731 | 94.1924 | 207.8738 | 116.6504 | 70.0505 | 49.4338 | 207.0473 | 105.6087 | 57.5923 | 35.2437 | 25.1262 | 205.8777 | 82.999 | 36.0631 | 17.7015 | 9.3279
By prioritizing the AP and deprioritizing 11ax STAs,
we can increase percentage of OFDMA TXs to the desired level,
while keeping fair percentage of legacy STAs’ TXs.
We can do it by tuning Cwmin, CWmax and/or AIFSN
Performance with Legacy parameters
July 2016

## Slide 32: Changing CWmin and CWmax for AP, fix CWmin = 16 for 11ax STAs, N_ax=10, N_leg=1
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 220.4808 | 141.7558 | 98.548 | 219.1217 | 127.1262 | 75.0634 | 52.0976 | 219.0306 | 115.974 | 62.5816 | 37.6065 | 26.4224 | 218.9731 | 98.457 | 41.7634 | 20.486 | 10.3399
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.0083823 | 0.037338 | 0.05349 | 0.0088842 | 0.044065 | 0.062993 | 0.071577 | 0.0089187 | 0.04698 | 0.068437 | 0.07616 | 0.080298 | 0.0089405 | 0.053524 | 0.07462 | 0.083333 | 0.086231
By prioritizing the AP and deprioritizing 11ax STAs,
we can increase percentage of OFDMA TXs to the desired level,
while keeping fair percentage of legacy STAs’ TXs.
Values, which meet requirements
Performance with Legacy parameters
July 2016

## Slide 33: Changing CWmin and CWmax for AP, fix CWmin = 1024 for 11ax STAs, N_ax=10, N_leg=1
Chart: Number of OFDMA TXs per second
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 239.3538 | 217.163 | 175.8098 | 239.2761 | 216.4517 | 168.6653 | 123.0776 | 239.2753 | 216.4475 | 166.8226 | 114.8648 | 77.0429 | 239.3487 | 216.3807 | 166.6079 | 112.8685 | 68.0771
Chart: Percentage of Legacy STAs TXs
| 2-8 | 4-8 | 8-8 | 2-16 | 4-16 | 8-16 | 16-16 | 2-32 | 4-32 | 8-32 | 16-32 | 32-32 | 2-1024 | 4-1024 | 8-1024 | 16-1024 | 32-1024
 | 0.0066096 | 0.078476 | 0.22858 | 0.0068938 | 0.081061 | 0.25462 | 0.4221 | 0.006895 | 0.081074 | 0.26151 | 0.45202 | 0.59008 | 0.0066174 | 0.081276 | 0.26224 | 0.45941 | 0.62308
By prioritizing the AP and deprioritizing 11ax STAs,
we can increase percentage of OFDMA TXs to the desired level,
while keeping fair percentage of legacy STAs’ TXs.
Values, which meet requirements
Performance with Legacy parameters
July 2016