## Slide 1: P802.1CM Time-Sensitive Networking for Fronthaul
Date: 2016-07-26
Authors:

## Slide 2: Agenda
Fronthaul
IEEE P802.1CM
  Scope, goals
  Collaboration with the Common Public Radio Interface (CPRI) Cooperation
  Current status
Summary

## Slide 3: Simplified 5G Architecture
Radio Base Station (RBS)
backhaul

## Slide 4: Simplified 5G Architecture with Fronthaul
fronthaul
Radio Equipment (RE)
Radio Equipment Control (REC)
backhaul
Radio Base Station (RBS)
baseband

## Slide 5: Fronthaul
Radio Base Station is functionally split into Radio Equipment (RE) and Radio Equipment Control (REC)
The Common Public Radio Interface (CPRI) is the most common radio interface for Fronthaul
RE
Fronthaul, e.g., CPRI
Remote radio site
REC
RE
Fronthaul
REC
Remote radio site
Backhaul
Backhaul

## Slide 6: Use Cases, e.g.,
Main-Remote
Small Cells
  dense Fronthaul network
  indoor deployments too
Centralized RAN (C-RAN)
  extensive Fronthaul network
  indoor deployments too
Fronthaul
Base station site
REC
Small Cell
…
Base station site
REC
Small Cell
Small Cell
Fronthaul
C-RAN site
REC
…
RRU
Remote radio site
RRU
Remote radio site
RE
Remote radio site
Small Cell
…
Small Cell
Small Cell
RE
Base station site
Fronthaul
REC
Remote radio site

## Slide 7: P802.1CM TSN for Fronthaul Project
Develop standard TSN profiles for Fronthaul in order to enable the transport of Fronthaul streams in a bridged network
A Profile is a set of feature and option selections that specifies aspects of bridge and end station operation, and states the conformance requirements for support of a specific class of user applications
  e.g., 802.1BA Audio Video Bridging Systems; also provides architecture
RE1
Bridged network for Fronthaul
REC1
REC2
RE2
RE3

## Slide 8: P802.1CM TSN for Fronthaul Document
Collects requirements for Fronthaul networks
  CPRI functional decomposition requirements
  The different CPRI information flows are supported separate from each other
  CPRI “as is” over Ethernet is NOT in scope
  Placeholder for further Fronthaul requirements
Provides guidance for meeting Fronthaul requirements, which includes
  Selects features, e.g. 802.1 TSN features, in order to build networks capable of transmitting Fronthaul streams, e.g., the requirements of the CPRI information flows
  Describes how the selected features and components can be combined, configured and used in order to meet Fronthaul requirements

## Slide 9: Radio Base Station Split
Current focus of P802.1CM is the functional split specified by CPRI 7.0
It is in scope of 802.1CM to define profile(s) for further split(s)
Current split
PDCP
RLC
MAC
PHY
Radio
PDCP: Packet Data Convergence Protocol
RLC: Radio Link Controller
No split
PDCP
RLC
MAC
PHY
Radio
Further splits are possible
Possible splits – any combinations
Layer 3
Layer 2
Layer 1
Radio
Layer 3
Layer 2
Layer 1
Radio
Layer 3
Layer 2
Layer 1
Radio

## Slide 10: P802.1CM – Current Status
Collaboration with CPRI Cooperation
1st Task Group ballot on D0.4
Gathers requirements for CPRI information flows
  IQ data (IQ: In-Phase and Quadrature modulation)
  Control and Management (C&M)
  Synchronization
Collects bridge and synchronization functions to meet req.
  Possible synchronization approaches
  Bridged network characteristics
  Bridge functions, e.g., frame preemption [802.3br and 802.1Qbu]
Early version of two profiles
  Profile A: strict priority
  Profile B: strict priority and frame preemption
Work in progress!
http://www.ieee802.org/1/pages/802.1cm.html

## Slide 11: Summary
Fronthaul interconnects functionally split components of a Radio Base Station
Current P802.1CM focus is the radio base station split specified by CPRI 7.0
Profile(s) for further splits are also in scope of P802.1CM
P802.1CM specifies packet transport for Fronthaul
  Collaboration with CPRI Cooperation
  Collects Fronthaul requirements
  Specifies architecture for packet transport of Fronthaul, i.e., Ethernet-based