## Slide 1: Control Trailer Clarifications
Date: 2016-07-26
Authors:

## Slide 2: Abstract
This presentation clarifies details about the control trailer modulation and encoding

## Slide 3: Current Status
In January the control trailer design shown above have been presented.
The control trailer has the length of 2 TRN units (2x4992 chips) which is equivalent to 39 bytes (in control PHY) divided into 21 bytes of parity and 18 bytes available for data transfer.
Control trailer is indicated by setting bits 22 and 23 to 1.
PPDU as interpreted by legacy non-EDMG STAs:
PPDU as interpreted by EDMG STAs:

## Slide 4: What needs to be clarified
Details of the frame structure
How are training fields appended to a control PHY packet with a control trailer.

## Slide 5: Details of frame structure
Each TRN-Unit is distributed into two parts: AGC subfields and groups of CE and 4 TRN subfields.
The Control Trailer takes all the parts of the TRN unit. There is no separation between the control trailer and the last LDPC codeword of the packet.
The control trailer behaves as an another LDPC codeword with a length of 39bytes.
  The control trailer encoding is similar to that of the legacy control PHY – 18 bytes of data are padded with zeros to create 504 bits, the rate ¾ LDPC encoder generates 168 bits of parity from the LDPC codewords. The 18bytes and the 168 bits are appended together for transmission
  The spreading (by 32) and modulation is the same as in the data part of the control PHY. The differential encoding continues with no separation from the last bit of the data part of the packet.
The header indicates two TRN units in the TRN length field (if no additional TRN fields)
Preamble
Header LDPC
LDPC2
AGC
CE
CE
TRN + CE
TRN + CE
Preamble
Header LDPC
LDPC2
LDPC3
What legacy see
What 11ay see

## Slide 6: Adding Training Fields
If Training fields are appended to the packet, the number of TRN-Units appended to the packet is increased by 2 to accommodate the control trailer.
The AGC subfields are appended immediately after the control trailer.
The CEF and TRN groups are added of the AGC subfields

## Slide 7: Straw Poll
Do you agree to replace the text in 3.1.1 with the following text: “A Control Trailer may be used in Control mode PPDUs in place of TRN-Units to carry control data. The control trailer is an LDPC codeword with 18 data octets and 168 parity bits, added after the data part of a control PHY packet, using and continuing the control PHY modulation and encoding. If a control trailer is added to a packet, the value of the Training Length field in the L-Header shall be greater than or equal to 2. If the value in the Training Length field in the L-Header is greater than 2, AGC subfields and CE and TRN subfields will be appended after the control trailer.” "

## Slide 8: References
11-16-105-00-00ay-Contorl-Trailer-in-control-mode-PPDU
11-15-1358-04-00ay-specification-framework-for-tgay