## Slide 1: Locationing Protocol for 11az
Date: 2016-07-26
Authors:

## Slide 2: Background – 11az
11az tasked to specify MAC/PHY techniques to enable better positioning
  Requirements:
    improved accuracy
    lower overhead/improved scalability
  Approaches to get there
    angular techniques
    Refined FTM
    passive positioning
    60GHz
    etc
Improving positioning accuracy is inherently a ‘channel estimation problem’
  Resolution of MIMO channels can lead to better location accuracy – range and angle
11az timelines indicate a launch after 11ax and companies will invest in new silicon for 11ax
  Can we leverage 11ax packet structures/sequences to enable improved accuracy positioning with lower overhead?

## Slide 3: Proposal Objectives
Define a sequence that
  Achieves low-overhead MIMO channel estimation for locationing
  Can be embedded in any packet – limiting overhead of a dedicated packet exchange sequence when continuous positioning is required
Define a protocol that
  Supports
    Network-based and STA-side positioning
    Associated and unassociated STA positioning
    Triggered and Contention-based TXOPs
  Improves medium utilization efficiency i.e. limits overhead (eg: can piggyback data)
  Allows Implementation Flexibility – processing time etc

## Slide 4: Channel Estimation Sequence

## Slide 5: Embed a Channel Estimation Sequence in the HE Packet Extension Field
Leverage the HE Packet Extension Field to define a low overhead channel estimation sequence
  11ax does not currently specify the contents of the PE
  11ax allows for a variable length PE – 0/4/8/12/16us
  Tx determines minimum PE length to be used based on Rx capability and rules defined in 11ax
    Tx may additionally add/extend the PE -> as per current 11ax specification
Proposal
  11az specifies at least one mode of operation with transmission of channel-estimation sequences (eg: LTFs) during the PE field
    Use of this mode may be signaled - eg: via HE-SIG field
  Standard specifies an appropriate LTF-mapping (P-matrix) and spatial-mapping Q-matrix
    See next slide
  Standard specifies the sequences that are used for different tx-antenna configurations and PE durations
    See next slide

## Slide 6: Sounding PE Definition
Use a P-matrix – (for example as shown below) that allows for orthogonalization of LTFs from different antennas
Depending on PE duration chosen by Tx, some # of Tx antennas can be supported as shown below
PE is not beam-formed
  Rx may leverage initial AGC gain setting (from Legacy Preamble section to receive the PE)
    Max resolution loss of 1.5bits assuming max beamforming gain with 8 Tx antennas [practical cases would be lower] – Sufficient resolution for channel estimation
  Q-matrix is specified in the standard to be 11az friendly – eg: an I-matrix
PE duration (us)/Tx-antenna | LTF-1 | LTF-2 | LTF-3 | LTF-4
0 | NA | NA | NA | NA
4/1 | +1 |  |  | 
8/1 | 1 | -1 |  | 
8/2 | 1 | 1 |  | 
12/1 | 1 | -1 | Repeat LTF-1 | 
12/2 | 1 | 1 | Repeat LTF-1 | 
16/1 | 1 | -1 | 1 | 1
16/2 | 1 | 1 | -1 | 1
16/3 | 1 | 1 | 1 | -1
16/4 | -1 | 1 | 1 | 1
16/5~16/8 | Repeat 16/1~16/4 with specified CSD |  |  | 

## Slide 7: CIR of 2-antennas using CSD
Example CIR of two antennas multiplexed using CSD

## Slide 8: Locationing Protocol

## Slide 9: Objectives
Leverage 11ax sequences
  Triggered/Scheduled operation
  Contention based TXOP operation
Single TXOP
Implementation flexibility
Define a framework that allows for locationing information to be available at either entity (initiator OR responder)
  Actual information to be shared can be negotiated based on privacy considerations, use-case, compute capabilities etc

## Slide 10: Triggered Frame Exchange
Single TXOP
MU operation MAY be used to sound multiple devices
Use of sounding PE eliminates additional overhead of NDP exchange – allow for piggybacking sounding on data
  Currently specified AMPDU contexts allow for piggybacking data/ack/management transmission
Framework allows device to relax its response-time (critical-path) based on capability
Framework allows flexibility to either entity to perform location computations

## Slide 11: Contention Based Frame Exchange
Simplest 802.11 construct of request/response – limited frame overhead

## Slide 12: Requirements
Method to indicate presence of sounding sequence in PE
  Indicate via a reserved bit in HE-SIG-A
  Sounding Sequence has a unique pattern that can be used to detect presence of sounding PE and number of Tx antennas [Rx would correlate against expected sounding sequence to determine presence and hence # Tx antennas]
  Sounding PE indicated via MAC header
  Sounding PE indicated via a new trigger-type
  Presence of sounding PE pre-negotiated between AP and STA
  …
PE Duration and Antenna Configuration
  PE duration signaled via existing 11ax fields in HE-SIG-A
  Mapping between PE durations and allowed antenna configurations specified by 11az
Note that some of the requirements identified above can be promoted by TGaz as recommended changes to 11ax for better positioning

## Slide 13: Alignment with 802.11ax
Leverage Existing 11ax Sequences
  MU/OFDMA: Trigger -> Data -> DL-ACK
  Contention Based SU: Data -> ACK
Reuse existing fields in 11ax frames for 11az functionality
  Fully backwards compatible with 11ax devices that don’t support 11az
Defined sequence can piggy-back on data exchange – do not need a dedicated exchange for sounding
  Efficient overlay of locationing on data communications
  Enables use-cases for more frequent location updates

## Slide 14: Discussion?
How do we signal presence of locationing sequence in packet extension?
Performance improvements with > 4 antennas?

## Slide 15: Simulation Results

## Slide 16: Simulation Environment
IEEE Channel D-LOS
  K=3dB (default specified for large office environment)
  K = 6, 10dB increased strength of LOS component for additional comparison
  Modifications
    Make K-factor configurable
    Make AoA of the first cluster configurable
    Randomize the AoA of the 2nd and 3rd clusters
Tx (2-antenna) & Rx (4-antenna) are Uniform Linear Arrays with lambda/2 spacing

## Slide 17: Changes to Angular Parameters on IEEE Channel D-LOS for AoA

## Slide 18: Evaluation
Evaluate AoA performance using for 2 antenna Tx/4-antenna Rx using MUSIC for
  Case#1: 2xLTFs separated by CSD of 200ns
    Eg: antenna #1 and #5 using packet extension approach
  Case#2: 2xLTFs orthogonalized by P-matrix codes

## Slide 19: AoA Performance
Both techniques yield similar AoA performance under varying channel conditions

## Slide 20: Straw Polls
Does the group see that a 11az location protocol will define a NEW sequence exclusively for sounding (based on 11ax not 11ac)
  Yes:
  No:
  Abstain:

## Slide 21: Straw Polls
Does the group see leveraging the 11ax Packet-Extension field as a viable approach to improving location accuracy on 11az ?
  Reduced overheads – can be embedded in any/every packet
  Achieve better accuracy through more frequent updates
  Known 11ax sequence – supports MU/OFDMA without need for definition of a new NDP format
  Yes:
  No:
  Abstain: