## Slide 1: Preliminary design of EDMG PHY headers
Date: 2016-07-28
Authors:

## Slide 2: Goals
Propose a preliminary definition for:
SU-MIMO EDMG-header-A
MU-MIMO EDMG-header-A and EDMG-header-B
By including non-controversial fields
L-STF | L-CEF | L-Header | EDMG-Header-A | EDMG-STF | EDMG-CEF | EDMG-Header-B | Data | AGC | TRN
EDMG PPDU format

## Slide 3: SU-MIMO header-A
In SU-MIMO header-A, we propose to include:
Bandwidth information (2.16, 4.32, …) – designed as proposed in doc 954r1
Primary channel allocation – designed as proposed in doc 954r1
SU/MU field (1 bit) - indicates whether the PPDU is a SU PPDU or a MU PPDU. Set to 0 to indicate SU PPDU, set to 1 to indicate MU PPDU
MCS – design TBD
GI/CP length field – 2 bits
PSDU length field – 22 bits
Beamformed field – 1 bit – indicates if the PPDU is beamformed or not – used by the receiver to know if it can do smoothing or not
Short/Long LDPC – 1 bit - if set to 1, indicates LDPC codeword equal to 1344. If set to 0, indicates LDPC codeword equal to 672.
number of SS

## Slide 4: MU-MIMO header-A and header-B
For MU-MIMO, we split the information between header-A (common signaling) and header-B (per-STA per-SS signaling).
In header-A, we propose to include:
Bandwidth information (2.16, 4.32, …)
Primary channel allocation
GI/CP length
Short/Long LDPC
The list of destination AIDs
In header-B, we propose to include:
PSDU length
MCS of the SSs

## Slide 5: Conclusion
We propose to start filling the following headers with non-controversial fields:
SU-MIMO EDMG-headerA
MU-MIMO EDMG-headerA and headerB

## Slide 6: Straw poll #1
Do you agree to add to the SFD the following fields in the EDMG-header A of an EDMG SU PPDU: SU/MU field (1 bit), BW (TBD), primary channel (TBD bits), MCS (TBD), GI/CP length field (2 bits), PSDU length field (22 bits), Beamformed field (1 bit), Short/Long LDPC (1 bit), number of SS (TBD)

## Slide 7: Straw poll #2
Do you agree to add to the SFD the following fields in the EDMG-header A of an EDMG MU PPDU: SU/MU (1 bit), BW (TBD), primary channel (TBD bits), AID for each destination STA (8 bits AID field, 8 destination STAs), GI/CP length field (2 bits), Beamformed field (1 bit), Short/Long LDPC (1 bit)

## Slide 8: Straw poll #3
Do you agree to add to the SFD the following fields in the EDMG-header B for an EDMG MU PPDU: PSDU length field (22 bits), MCS (TBD)