## Slide 1: TG ax A Unified Approach to Spatial Reuse
Date: 2016-08
Authors:

## Slide 2: Background
Three basic Spatial Reuse schemes have been proposed:
Color
  Identify traffic in an OBSS network
TPC
  Adjust the transmit power of a STA based upon the CS/CCA threshold of the STA
  STA can increase CS/CCA threshold if it also reduces TXPWR
DSC
  Adjust the effective CS/CCA threshold of a STA based upon the RSSI of the AP Beacons

## Slide 3: Color and inter-BSS
Inter-BSS packets
  Traffic in an OBSS network to the STA
Intra-BSS packets
  Traffic in the same network as the STA
Basic idea
If packet is identified as inter-BSS, ignore it
  Do not set NAV, Can transmit over it
Color bits in the HE Operation element (6 bits)
  Can also use BSSID
Observation:
  Inter-BSS will not work if OBSS is Legacy, but BSSID can be used.

## Slide 4: TPC
Transmit Power Control
  Reduce transmit power so that interference to OBSS is reduced
Previous
  TPC has been presented in 11k, 11v, 11e, 11h, 11aa, 11ac and now 11ax
Observation:
  TPC works great if all STAs do it.

## Slide 5: TPC 16/945
Couples TPC with OBSS_PD
  OBSS_PD is CS/CCA for inter-BSS packets
OBSS_PDthres = OBSS_PD min + (TXPWRref - TXPWR)
And OBSS_PDmin <= OBSS_PDthres <= OBSS_PDmax
Recommended
-83 dBm <= OBSS_PDthres <= -62 dBm
Sets relationship between the inter-BSS CCA and TXPWR.
No description of how STA decides the balance of TXPWR and

## Slide 6: DSC
Dynamic Sensitivity Control (13/1012)
  Adjust STA effective CS/CCA threshold based upon RSSI of beacon from AP
  CCAeff = MIN (Upper Limit, RSSI beacon ) – Margin
Observation:
  DSC is the converse of TPC, in place of reducing TXPWR, increase effective CCA threshold (or reduced RX sensitivity)_

## Slide 7: Linking TPC with DSC
Presentations on reducing TXPWR with increased CCA threshold for 11ax include:
  14/523 Laurent Cariou (Orange) “MAC simulation results for Dynamic sensitivity control (DSC - CCA adaptation) and transmit power control (TPC)
  15/1069 James Wang (MediaTek, et al) “Adaptive CCA and TPC”

## Slide 8: TPC and DSC
14/523
DSC (CCA control):
  each STA adjust CCA to CCA = Useful Rx Power – Margin
TP control:
    each receiver requests transmitter to adjust TP so that it receives the Useful Rx Power at Margin dB above classical CCA (-82dBm)
15/1069
  Adjusted_TX_Pwr = TX_Pwrnominal –RSSIAP +constant 1
  Adjusted_OBSS_PD = OBSS_PDnominal + RSSIAP + constant 2
Limits the OBSS_PD threshold to be
  -82dBm<Adj_CCA<-62 dBm
In both 14/523 and 15/1069, the CCA formulas are identical to DSC with a fixed DSC Upper Limit.

## Slide 9: Proposal
Link DSC, Adaptive (A)TPC, and inter-BSS
  DSC calculates the effective CCS Threshold based upon the beacon RSSI (or distance to the AP) CCAeff = MIN (Upper Limit, RSSI beacon ) – Margin
  ATPC calculates the TXPWR CCAeff = CCAmin+ (TXPWRref - TXPWR) (TXPWR - TXPWRref )= CCAmin – CCAeff
  The CCAeff is only used on Inter-BSS packets OBSS_PD thres = CCAeff

## Slide 10: Parameters
DSC parameters:
  DSC Margin
  DSC Upper Limit
ATPC parameters:
  ATPC CCA Min ≤ CCAeff ≤ ATPC CCA Max
  ATPC CCA Min
    Set to -82 dBm for 20 MHz (agrees with Std)
  ATPC CCA Max
    Set to DSC Upper Limit – DSC Margin (maximum CCAeff)
  TXPWRref
    21 dBm (<3 SS), 23dBm (3+ SS) as proposed by 16/945
OBSS_PD
  OBSS_PDthres = CCAeff

## Slide 11
AP
STA
TXPWRref = 21 dBm DSC Upper Limit = -40 dBm DSC Margin = 20 dB
ATPC CCA Min = -82 dBm ATPC CCA max = -60 dBm (-40–20)

## Slide 12: Summary – Unified Proposal for Spatial Reuse
Color Based CCA
  No change
  Inter-BSS packet can be ignored
DSC may be used to determine effective CCA threshold, CCA eff
ATPC may be used to determine TXPWR
CCAeff may be used only on inter-BSS packets
Satisfies all conditions as described in various presentations

## Slide 13: Adaptive CCA, ATPC and inter-BSS
Full text on this unified approach is in 16/1063

## Slide 14: Motion
Incorporate text in 16/1063 into the 11ax Draft.