## Slide 1: TG ax A Unified Approach to Spatial Reuse
Date: 2016-10
Authors:

## Slide 2: Background
Three basic Spatial Reuse schemes have been proposed:
Color/inter-BSS
  Identify traffic in an OBSS network, inter-BSS packets
  Ignore inter-BSS packets if below an OBSS_PD value
TPC
  Adjust the transmit power of a STA based upon the CS/CCA threshold of the STA
    i.e. STA can increase CS/CCA threshold if it also reduces TXPWR
DSC
  Adjust the effective CS/CCA threshold of a STA based upon the RSSI of the network AP Beacons
Revision 0 posted August 2016.

## Slide 3: Inter-BSS, Intra-BSS and OBSS_PD
Inter-BSS packets
  Traffic in an OBSS network to the STA
Intra-BSS packets
  Traffic in the same network as the STA
Basic idea
If packet is identified as inter-BSS, ignore it if below a certain signal level, OBSS_PD
  Do not set NAV, Can transmit over it

## Slide 4: TPC
Transmit Power Control
  Reduce transmit power so that interference to OBSS is reduced
  Adjust OBSS_PD level in conjunction with Transmit power
From 16/1233r6

## Slide 5: TPC and OBSS_PD
Couples TPC with OBSS_PD
  OBSS_PD is CS/CCA for inter-BSS packets
OBSS_PDthres = OBSS_PD min + (TXPWRref - TXPWR)
And OBSS_PDmin <= OBSS_PDthres <= OBSS_PDmax
Recommended
-82 dBm <= OBSS_PDthres <= -62 dBm
Sets relationship between the inter-BSS CCA and TXPWR
TXPWR = TXPWRref + OBSS_PDmin – OBSS_PDthres
“A STA can select an OBSS_PD level during its operation under SR mode. This level can be dynamically adjusted or can be static.”

## Slide 6: DSC
Dynamic Sensitivity Control (13/1012, etc)
  Adjust STA effective CS/CCA threshold based upon RSSI of beacon from AP
  CCAeff = MIN (Upper Limit, RSSI beacon ) – Margin
  CCAeff min = -82 dBm for 20 MHz.

## Slide 7: Linking TPC with CS/CCA (DSC)
Presentations on reducing TXPWR with increased CCA threshold for 11ax first suggested in:
  14/523 Laurent Cariou (Orange) “MAC simulation results for Dynamic sensitivity control (DSC - CCA adaptation) and transmit power control (TPC)
  15/1069 James Wang (MediaTek, et al) “Adaptive CCA and TPC”
At the moment the CCA setting is left open.

## Slide 8: TPC and DSC
14/523
DSC (CCA control):
  each STA adjusts CCA to CCA = Useful Rx Power – Margin
TP control:
    each receiver requests transmitter to adjust TP so that it receives the useful Rx Power at ‘Margin’ dB above classical CCA (-82dBm)
15/1069
  Adjusted_TX_Pwr = TX_Pwrnominal –RSSIAP +constant 1
  Adjusted_OBSS_PD = OBSS_PDnominal + RSSIAP + constant 2
Limits the OBSS_PD threshold to be
  -82dBm<Adj_CCA<-62 dBm
In both 14/523 and 15/1069, the CCA formulas are identical to DSC with a fixed DSC Upper Limit.

## Slide 9: Proposal
Link DSC, Adaptive (A)TPC, and inter-BSS
  DSC STA calculates the effective CCA Threshold based upon the beacon RSSI (i.e. distance to the AP) CCAeff = MIN (Upper Limit, RSSI beacon ) – Margin CCAeffmin = -82 dBm
  ATPC STA calculates the TXPWR CCAeff = CCAmin+ (TXPWRref - TXPWR) (TXPWR - TXPWRref )= CCAmin – CCAeff
  The CCAeff is only used on Inter-BSS packets OBSS_PD thres = CCAeff
  Everything is optional
  NOTE: TPC as proposed in 16/1223 is left alone. ATPC is the scheme where the CCAeff is used and the TX power set accordingly. Same relationship is kept.

## Slide 10: Proposed Parameters and unification
DSC parameters:
  DSC Margin Set both to 0 for DSC prohibited
  DSC Upper Limit
ATPC parameters:
  ATPC CCA Min
    Set to -82 dBm for 20 MHz (agrees with Std and min CCAeff)
  ATPC CCA Max
    Set to DSC Upper Limit – DSC Margin (maximum CCAeff)
    Set both to zero for ATPC prohibited
  TXPWRref
    21 dBm (<3 SS), 23dBm (3+ SS) as proposed by 16/945, 16/1223
OBSS_PD
  OBSS_PDthres = CCAeff

## Slide 11
AP
STA
TXPWRref = 21 dBm DSC Upper Limit = -40 dBm DSC Margin = 20 dB
ATPC CCA Min = -82 dBm ATPC CCA max = -60 dBm (-40–20)
Result is as was envisaged by 15/1069 James Wang

## Slide 12: Summary – Unified Proposal for Spatial Reuse
DSC may be used to determine effective CCA threshold,
  CCA eff
ATPC may be used to determine TXPWR
  based upon CCA eff
  (TXPWR - TXPWRref )= OBSS_PDmin – CCAeff
Inter-BSS packets may be ignored if below OBSS_PD
  OBSS_PD may be set to CCA eff
Satisfies all conditions as described in various presentations
Provides a standardized method for setting OBSS_PD.
    Enables spatial reuse to be simulated

## Slide 13: Adaptive CCA, ATPC and inter-BSS
Full text on this unified approach is in 16/1063

## Slide 14: Motion
Incorporate text in 16/1063 into the 11ax Draft.