## Slide 1: An Update on Spatial Sharing Enhancement for MIMO Operation
Date: 2016-09-12
Authors:

## Slide 2: Background
It has been agreed in 11ay SFD [1] that
  The EDMG spatial sharing mechanism shall enable an EDMG STA to perform concurrent measurements employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA based on the same measurement configuration.
This contribution addresses how EDMG STA reports measurement results after performing concurrent measurements employing multiple RX antenna configuration.

## Slide 3: Recap: Multi-Antenna Spatial Sharing [2]
  EDMG PCP/AP sends an enhanced Directional Channel Quality Request to EDMG STA to request it to perform multiple measurements concurrently employing multiple RX antenna configurations as are used for receiving multiple streams from the target EDMG STA.
    Each of multiple RX antenna configurations corresponds to a specific RX antenna.
    All of concurrent measurements are based on the same measurement configuration (e.g., Measurement Method, Measurement Start Time, Measurement Duration, Number of Time Blocks, etc.).

## Slide 4: Proposal
    Measuring STA sends an enhanced Directional Channel Quality Report to PCP/AP, which shall report results of concurrent measurements according to one of the two following measurement report methods:
  Method 1: The results of concurrent measurements during each measurement time block are individually reported.
  Method 2: The average of the results of concurrent measurements during each measurement time block is reported.
Compared with Method 1, Method 2 has a much shorter measurement report. But Method 1 is able to provide more detailed measurement results.

## Slide 5: Example Frame Format
 | Measurement Report Method | Reserved
Bits: | 1 | 7
 | Operating Class | Channel Number | AID | Reserved | Measurement Method
Octets: | 1 | 1 | 1 | 1 | 1
 | Measurement Start Time | Measurement Duration | Number of Time Blocks | Optional Subelements
Octets: | 8 | 2 | 1 | Variable
Modifying the measurement request field format for Directional Channel Quality request (Clause 9.4.2.21.16 in P802.11REVmc D8.0) as follows:
  The Measurement Report Method field indicates the method that is to be used by the requested STA to report the results of concurrent measurements in the measurement report.
    If this field is set to 0, it indicates that the results of concurrent measurements during each measurement time block are individually reported.
    If this field is set to 1, it indicates that the average of the results of concurrent measurements during each measurement time block is reported.

## Slide 6: Example Frame Format (cont.)
 | Number of RX Antenna Configurations | Measurement Report Method | Reserved
Bits: | TBD | 1 | 5
 | Operating Class | Channel Number | AID | Reserved | Measurement Method | Measurement Start Time
Octets: | 1 | 1 | 1 | 1 | 1 | 8
 | Measurement Duration | Number of Time Blocks (N) | Measurement for Time block 1 | … | Measurement for Time block N | Optional Subelements
Octets: | 2 | 1 | 1 |  | 1 | Variable
Modifying the measurement report field format for Directional Channel Quality report (Clause 9.4.2.22.15 in P802.11REVmc D8.0) as follows:
  The Number of RX Antenna Configurations field indicates the number of RX antenna configurations used by the STA to perform concurrent measurements.

## Slide 7
 | Subelement ID | Length | Data
Octets: | 1 | 1 | Variable
 | Measurement for Time Block 1 | … | Measurement for Time Block N | … | Measurement for Time Block 1 | … | Measurement for Time Block N
Octets: | 1 |  | 1 |  | 1 |  | 1
Extended Measurement Report subelement
Example Frame Format (cont.)
  The Measurement Report Method field indicates the method used by the STA to report the results of concurrent measurements.
    If this field is set to 0, it indicates that the results of concurrent measurements during each measurement time block are individually reported.
      Measurement results corresponding to one of RX antenna configurations are carried in the Measurement for Time Blocks fields of Measurement Report field.
      Measurement results corresponding to the remaining RX antenna configurations are carried in an Extended Measurement Report subelement of Measurement Report field.
    If this field is set to 1, it indicates that the average of the results of concurrent measurements during a measurement time block is reported.
N*(Number of RX antenna configurations-1) fields

## Slide 8: Reference
11-15-1358-05-00ay-specification-framework-for-tgay.doc
11-16-0295-02-00ay-spatial sharing enhancement for MIMO.pptx

## Slide 9: Straw Poll
Do you agree to insert the following text into 11ay SFD?
  The EDMG spatial sharing mechanism shall enable an EDMG STA to report the average of the results of concurrent measurements using multiple RX antenna configurations in order to reduce the overhead of the measurement report.
  Yes:
  No:
  Abstain: