## Slide 1: Multi-Stage, Multi-Resolution Beamforming Training for 802.11ay
Date: 2016-09-12
Authors:

## Slide 2: Introduction
In 802.11ay, enhancements to the 802.11ad beamforming training procedures have been agreed on for complexity reduction, efficiency and to enable MIMO BF training [1][2][3][4].
In this contribution, we propose a multi-stage, multi-resolution beamforming training (BFT) framework to further increase the BF training efficiency in scenarios with high resolution beams.
The scheme also has advantages that enable more efficient beam tracking.

## Slide 3: Current BF Agreements
The following agreements have been made to improve BF training in 802.11ay [4]:
  The 11ay beamforming protocol shall
    enable TX and RX training using the same BRP frame.
    enable simultaneous BF training of transmit DMG antennas.
    support simultaneous RX antenna training.
    provide the means to enable TX sector down selection as part of beamforming training.
    support, for STAs with antenna pattern reciprocity, RX sector down selection as part of beamforming training.
    support a mode of operation in which, in a single phase, the initiator trains its transmit antennas/sectors and multiple responders train their receive antennas/sectors.
    The 11ay beamforming protocol supports multi-beamforming for multiple array antennas. Multi-beamforming means that a transmitter simultaneously sends SSW frames in multiple polarized directions.

## Slide 4: Multi-Stage, Multi-Resolution BFT
To further increase the efficiency of the beamforming training procedure with high resolution beamforming, we propose that 802.11ay support the use of a multi-stage, multi-resolution beamforming framework [5].
  In this framework, beams of increasing angular resolution can be used at different stages of the sector sweep, beam refinement or tracking procedure.
To support this scheme in 802.11ay, signaling should be added to indicate the capability to perform multi-stage, multi-resolution BFT and to signal resolution information such as the maximum and current beam resolutions.

## Slide 5: Multi-Stage, Multi-Resolution BFT
L0: Sector Level Sweep: Identify Sector of angular spread 90 degrees
L1: BFT Level 1:
  4 beams per sector with angular spread 22.5 degrees
L2: BFT Level 2:
  4 beams per beam Level 1 or 16 beams per sector with angular spread 5.625 degrees
L3: BFT Level 3/ Non-hierarchical BRP:
  4 beams per beam Level 2 or 64 beams per sector with angular spread 1.046 degrees.

## Slide 6: Example
Multi-stage, Multi-resolution beam sweep: 12 beam sweeps and 3 feedback frames
Beam = Sector 1, L1:beam 2, L2:beam 1, L3:beam 3
Single Resolution beam sweep : 64 beam sweeps and 1 feedback frame
Beam = Sector 1, beam 19

## Slide 7: BFT Protocol
Single Resolution BF Training
Multi-stage, Multi-Resolution BF Training

## Slide 8: Advantages of Multi-Stage, Multi-Resolution BFT
The overall number of training beams transmitted for a narrow beam system can be reduced. This is important especially in MIMO scenarios where multiple transmit-receive pairs are needed.
  Connection between the transmitter-receiver pair can be made at any stage without the need for a long wait.
  The procedure can also be combined with beam down-selection.
The initiator or responder can request training at a particular resolution level and dynamically trade-off BFT efficiency and beam accuracy.
A node can request for BFT with a resolution fallback in case of a change in the channel which is advantageous for beam tracking

## Slide 9: Conclusion
Multi-stage Multi-resolution BFT offers improvements in BF training efficiency and beam tracking for high resolution beams.
Signaling should be added to 802.11ay to indicate the capability to perform multi-stage, multi-resolution beam tracking and to signal information such as the maximum and current beam resolutions

## Slide 10: Straw Polls
Do you agree to add the following text into the 802.11ay SFD?
  11ay shall support multi-stage, multi-resolution beamforming training as part of the beamforming training procedure

## Slide 11
References
IEEE 802.11-16/0100r3, MIMO BF Training Enhancements, Wang et. al., Jan 2016
IEEE 802.11-16/0316r0, Low Complexity Beamtraining for Hybrid MIMO, Fellhauer et. al., March 2016
IEEE 802.11-16/0420r1, BF Training for SU MIMO, Huang et. al., March 2016
IEEE 802.11-15/1358r5, Specification Framework for TGay, Cordeiro, August 2016
Noh, Song, Michael D. Zoltowski, and David J. Love. "Multi-Resolution Codebook Based Beamforming Sequence Design in Millimeter-Wave Systems." 2015 IEEE Global Communications Conference (GLOBECOM). IEEE, 2015.