## Slide 1
MAC Capabilities Info. in HE Capabilities IE
Date: 2016-09-11
Authors:

## Slide 2: Overview
An HE STA declares that it is an HE STA by transmitting HE Capabilities element
  This element advertises PHY and MAC capabilities of an HE STA
Current definition of MAC-related capabilities subfields in the HE Capabilities element is incomplete in [1]
  Certain capabilities are missing (E.g., All Ack, etc.)
In these slides we propose to define
  Missing MAC capabilities subfields of HE Capabilities Information subfield, including their bit width and respective values

## Slide 3: HE Capabilities IE - Overview
PHY
 | B0 | B1 | B2 | B3 B4 | B5 B7 | B8 B9 | B10 B11
 | PPE Thresholds Present | TWT Requester Support | TWT Responder Support | Fragmentation Support | Maximum Number of Fragmented MSDUs | Minimum Fragment Size | Trigger Frame MAC Padding Duration
Bits: | 1 | 1 | 1 | 2 | 3 | 2 | 2
 | B12 B14 | B15 B16 | B17 | B18 | B19 | B20 B31
 | Multi-TID Aggregation Support | Largest Constellation With DCM | Maximum Nss With DCM | UL MU Response Scheduling Support | A-BSR Support | Reserved
Bits: | 3 | 2 | 1 | 1 | 1 | 12
 | B20 | B21 B22 | B23 | B24 | B25 | B26 | B27 | B28 | B29 | B30
 | +HTC-HE Support | HE Link Adaptation | All Ack Support | 32 bit BA Bitmap Support | MU Cascading Supported | Broadcast TWT Supported | Ack-enabled Multi-TID Aggregation Support | Group Addressed Multi-STA BlockAck In DL MU Support | OMI A-Control Support | OFDMA RA Support
Bits: | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
LEGEND:
Already present in D0.3
For discussion
Related to PHY Cap (out of scope for this deck)

## Slide 4: Present in TGax D0.3
Subfield | Definition | Encoding
PPE Thresholds Present | Indicates if the PPE Thresholds field(#1330) is present or not. | Set to 0 if the PPE Thresholds field is not present. Set to 1 if the PPE Thresholds is present.
TWT Requester Support | Indicates support by an HE STA for the role of TWT requesting STA as described in 10.44 (Target wake time (TWT)). | Set to 1 if dot11TWTOptionActivated is true and the STA supports TWT requester STA functionality (see 10.44 (Target wake time (TWT))). Set to 0 otherwise.
TWT Responder Support | Indicates support by an HE STA for the role of TWT responder STA as described in 10.44 (Target wake time (TWT)). | Set to 1 if dot11TWTOptionActivated is true and the STA supports TWT responder STA functionality (see 10.44 (Target wake time (TWT))). Set to 0 otherwise.
Fragmentation Support | Indicates the level of dynamic fragmentation that is supported by a STA. | Set to 0 if no support for dynamic fragmentation. Set to 1 if support for dynamic fragments that are contained within a VHT single MPDU, no support for dynamic fragments within an A-MPDU. Set to 2 if support for up to one dynamic fragment for each MSDU and each MMPDU within a single AMPDU or multi-TID A-MPDU. Set to 3 if support for multiple dynamic fragments for each MSDU within an A-MPDU or multi-TID AMPDU and up to one dynamic fragment for each MMPDU in a multi-TID A-MPDU.
Maximum Number of Fragmented MSDUs | Indicates the maximum number of fragmented MSDUs that can be concurrently received by a STA. | The maximum number of fragmented MSDUs, Nmax, defined by this field is Nmax = 2Maximum Number Of F-MPDUs, except for a value of the Maximum Number of Fragmented MSDUs equal to 7 which indicates that there is no restriction.

## Slide 5: Present in TGax D0.3
Subfield | Definition | Encoding
Minimum Fragment Size | Indicates the minimum payload size, in octets, for the first fragment of an MSDU that is supported by a STA. | Set to 0 for no restriction in the minimum payload size. Set to 1 for 128 octets restriction in the minimum payload size. Set to 2 for 256 octets restriction in the minimum payload size. Set to 3 for 512 octets restriction in the minimum payload size.
Trigger Frame MAC Padding Duration | Indicates the additional amount of time defined as MinTrigProcTime, in microseconds, needed for a non-AP STA to process a received Trigger frame. | Set to 0 to indicate no additional processing time. Set to 1 to indicate 8 us of processing time. Set to 2 to indicate 16 us of processing time. Remaining values are reserved.
Multi-TID Aggregation Support | Indicates the number of TIDs minus 1 of QoS Data frames that an HE STA can aggregate in a multi-TID A-MPDU as described in 25.10.4 (A-MPDU with multiple TIDs). | Set to 1 when dot11AMPDUwithMultipleTIDOptionImplemented is true. Set to 0 otherwise.
UL MU Response Scheduling Support | Indicates support for receiving an MPDU that contains an UL MU Response Scheduling A-Control field. | If +HTC-HE Support is 1: Set to 1 if the STA supports reception of the UL MU Response Scheduling A-Control field. Set to 0 otherwise. Reserved if +HTC-HE Support is 0.
A-BSR Support | Indicates support by an AP for receiving an MPDU that contains a BSR A-Control field and support by a non-AP STA for generating an MPDU that contains a BSR A-Control field. | If +HTC-HE Support is 1: Set to 1 if the STA supports the BSR A-Control field functionality. Set to 0 otherwise. Reserved if +HTC-HE Support is 0.

## Slide 6: Missing Capabilities
Subfield | Definition | Encoding
+HTC-HE Support | Indicates if the STA supports the reception of an HE variant HT Control field carried in a QoS Data, QoS Null, or Management frame. | Set to 1 if the STA supports reception of an HE variant HT Control field. Set to 0 otherwise.
HE Link Adaptation Capable | Indicates whether the STA supports link adaptation using the HE variant HT Control field. | If +HTC-HE Support is 1: Set to 0 (No Feedback) if the STA does not provide HE MFB. Set to 2 (Unsolicited) if the STA provides only unsolicited HE MFB. Set to 3 (Both) if the STA can provide HE MFB in response to HE MRQ and if the STA provides unsolicited HE MFB. The value 1 is reserved. Reserved if +HTC-HE Support is 0.
All Ack Supported | Indicates whether the STA supports reception of a Multi-STA BlockAck frame under the all ack context (see 25.4.2) | Set to 1 if the STA supports reception of a Multi-STA BlockAck frame under the All-Ack context. Set to 0 otherwise.
32 bit BA Bitmap Support | Indicates whether the STA supports reception of a Multi-STA BlockAck frame that has a 32 bit BlockAck Bitmap intended to it. | Set to 1 if the STA supports reception of a Multi-STA BlockAck frame that has a 32 bit BlockAck Bitmap field that is intended to it. Set to 0 otherwise.
MU Cascading Supported | Indicates whether the STA supports participating in an MU Cascading sequence (see 25.5.3 (MU cascading operating). | Set to 1 if the STA supports MU cascading operation. Set to 0 otherwise.

## Slide 7: Missing Capabilities
Subfield | Definition | Encoding
Broadcast TWT Supported | Indicates support by an HE non-AP STA for the role of TWT scheduled STA and by an AP for the role of TWT scheduling STA as described in 25.7.3 (Broadcast TWT operation). | Set to 1 when the STA supports broadcast TWT functionality. Set to 0 otherwise.
Ack-enabled Multi-TID Aggregation Support | Indicates support by a STA to receive a multi-TID A-MPDU that can solicit either Ack or BlockAck, or both, as described in 25.10.4 (A-MPDUs with multiple TIDs). | Set to 1 when the STA supports reception of a Ack-enabled multi-TID A-MPDU. Set to 0 otherwise.
Group Addressed Multi-STA BlockAck In DL MU Support | Indicates support by a non-AP STA for the reception of a group-addressed Multi-STA BlockAck frame that is sent in a DL MU PPDU in a non-broadcast RU. | Set to 1 when the non-AP STA supports its reception. Set to 0 otherwise. This field is reserved for an AP.
OMI A-Control Support | Indicates support for receiving an MPDU that contains an OMI A-Control field. | If +HTC-HE Support is 1: Set to 1 when the non-AP STA supports reception of the OMI A-Control field. Set to 0 otherwise. Reserved if +HTC-HE Support is 0.
OFDMA RA Support | Indicates support for a non-AP STA to follow the OFDMA random access procedure and for an AP to send Trigger frames that allocate random RUs (see 25.5.3.6 (UL OFDMA-based random access). | Set to 1 when the STA supports UL OFDMA-based random access procedure. Set to 0 otherwise.

## Slide 8: Further optionality considerations
Multiple frame types are allowed to be combined in an A-MPDU for 11ax[1]
  As part of multi-TID aggregation,
  As part of soliciting trigger-based PPDUs in response to DL MU PPDUs
  As part of a cascading MU sequence, etc.
We propose to specify that:
  The reception of Action (ACK) frame aggregated with Data is optional.
  The reception of acknowledgement frames (ACK, BA, M-BA) aggregated with Data is optional (indicated via MU Cascading Supported bit).
  The reception of Basic variant Trigger frame aggregated with Data is mandatory.

## Slide 9: Straw Poll 1
Do you agree to add the subfields below to the HE Capabilities IE?
 | +HTC-HE Support | HE Link Adaptation | All Ack Support | 32 bit BA Bitmap Support | MU Cascading Supported | Broadcast TWT Supported | Ack-enabled Multi-TID Aggregation Support | Group Addressed Multi-STA BlockAck In DL MU Support | OMI A-Control Support | OFDMA RA Support
Bits: | 1 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 10: Straw Poll 2
Do you support that:
  The reception of Action (ACK) frame aggregated with Data is optional.
  The reception of acknowledgement frames (ACK, BA, M-BA) aggregated with Data is optional (indicated via MU Cascading Supported bit).
  The reception of Basic variant Trigger frame aggregated with Data is mandatory.

## Slide 11: References
[1] IEEE802.11ax D0.4