## Slide 1: Tx Quality Requirements
Date: 2016-09-12
Authors:
Name | Affiliation | Address | Phone | Email
Daewon Lee | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | daewon.lee@newracom.com
Yujin Noh | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | yujin.noh@newracom.com
Bin Tian | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Lin Yang | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Ilan Sutskover | Intel |  |  | ilan.sutskover@intel.com
Ran Leviev | Intel |  |  | ran.leviev@intel.com
Shahar Gross | Intel |  |  | shahar.gross@intel.com

## Slide 2: Authors (continued)
Name | Affiliation | Address | Phone | Email
Yongho Seok | Newracom | 9008 Research Dr. Irvine, CA 92618 |  | yongho.seok@newracom.com
Young Hoon Kwon |  |  |  | younghoon.kwon@newracom.com
Reza Hedayat |  |  |  | reza.hedayat@newracom.com
Minho Cheong |  |  |  | minho.cheong@newracom.com
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 3: Authors (continued)
Name | Affiliation | Address | Phone | Email
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Feng Jiang |  |  |  | feng1.jiang@intel.com

## Slide 4: Authors (continued)
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 5: Authors (continued)
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 6: Authors (continued)
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 7: Authors (continued)
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Aon Mujtaba |  |  |  | mujtaba@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 8: Authors (continued)
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 9: Authors (continued)
Name | Affiliation | Address | Phone | Email
Jinmin Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | Jinmin1230.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
JayH Park |  |  |  | Hyunh.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com

## Slide 10: Authors (continued)
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp
Akira Yamada | NTT DOCOMO | 3-6, Hikarinooka, Yokosuka-shi, Kanagawa, 239-8536, Japan | +81 46 840 3759 | yamadaakira@nttdocomo.com

## Slide 11: Authors (continued)
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Fengming Cao |  |  |  | 

## Slide 12: Authors (continued)
Name | Affiliation | Address | Phone | Email
Sungeun Lee | Cypress Semiconductor Corporation |  |  | sungeun.lee@cypress.com
Saishankar Nandagopalan |  |  |  | snan@cypress.com
Stephane Baron | Canon |  |  | stephane.baron@crf.canon.fr
Pascal Viger |  |  |  | pascal.viger@crf.canon.fr
Patrice Nezou |  |  |  | patrice.nezou@crf.canon.fr

## Slide 13: Open or Missing TX Quality Requirements
Full bandwidth masks – defined
  RBW/VBW missing
OFDMA signals quality requirements– open
Spectral flatness – open
Frequency and symbol clock error – open
Time of departure accuracy – open
LO leakage level – defined
  80+80 MHz requirement missing

## Slide 14: Tx Clock Error
Proposal:
  Transmit subcarrier frequency and symbol clock error
    Same as 11ac (+/- 20ppm) except for trigger-based PPDU
  Time of departure accuracy
    Same as 11ac

## Slide 15: RBW and VBW for Tx Mask
11ac specification
  RBW
    11a/n/ac: 100kHz
  VBW
    11 a/n/ac: 30kHz
Proposal:
  RBW
    11ax: 25kHz due to ¼ carrier spacing
    Narrower RBW may also help in mask compliance
  VBW
    11ax: 7.5kHz
      Same ¼ scaling as the RBW
      Smaller VBW leads to better averaging. Benefit 11ax which may boosted STF/LTF and changing BW between pre-HE and HE portion

## Slide 16: Spectral Mask
Spectral mask
  Measuring total out-of-band emission power (orthogonal and non-orthogonal interferences)
  Good for controlling the adjacent channel interference impact to a non-synchronized receiver (like OBSS receiver)
  Not the be best tool for inter-RU interference control
Proposal:
  Every packet type should conform to the full bandwidth mask, to avoid excess leakage to adjacent channels
    Additional requirements to be put on narrowband OFDMA and preamble puncturing (i.e. non-contiguous channel bonding)
    Spectral flatness required is discussed later in this contribution

## Slide 17: Whole BW Mask for OFDMA
In UL OFDMA, narrow band data comes along with wideband (at least 20MHz) preamble
  For compliance testing, better testing the whole packet instead of using special testing mode with HE portion only
  Preamble power is proportional to RU bandwidth and packet duration
    Preamble PSD level is at least 10*log10[(Preamble BW)/(RU BW)] lower than the HE portion which makes it easy to meet the mask

## Slide 18: Spectral Flatness
Spectral flatness is required to ensure that mask compliance is not achieved by power boosting a subcarrier beyond reasonable level
Proposal:
  Spectral flatness should be tested as in 11ac, with the following exceptions:
    Used RUs only to be considered
    RU boosting and BF should not be used when measuring spectral flatness
  Spectral flatness should have same +4/-6 dB limit (as in 11ac)
  Note: spectral flatness is tested after GI removal and uses FFT output

## Slide 19: 11ax 20/40/80/160MHz Spectral Flatness
Propose to have same maximum deviation requirement as 11ac, re-calculate the tone indices for averaging, based on 11ax numerology
  For 20MHz: use same indices as 11ac 80MHz
  For 40MHz: outer most INNER subcarrier = 84*244/122 = 168
  For 80MHz: outer most INNER subcarrier = floor(168*500/244) = 344
  For 160/80+80MHz: outer most INNER subcarrier = floor(168*1012/244) = 696
  Inner most INNER subcarrier = (1024-696)/2+2 = 166

## Slide 20: 11ax Spectral Flatness Table Proposal
Transmission BW(MHz) | Averaging subcarrier indices (inclusive) | Tested subcarrier indices (inclusive) | Maximum Deviation (dB)
20 | -84 to -2 and +2 to +84 | -84 to -2 and +2 to +84 | ±4
 |  | -122 to -85 and +85 to +122 | +4/-6
40 | -168 to -3 and +3 to +168 | -168 to -3 and +3 to +168 | ±4
 |  | -244 to -169 and +169 to +244 | +4/-6
80 | -344 to -3 and +3 to +344 | -344 to -3 and +3 to +344 | ±4
 |  | -500 to -345 and +345 to +500 | +4/-6
160/80+80 | -696 to -515, -509 to -166, +166 to +509, and +515 to +696 | -696 to -515, -509 to -166, +166 to +509, and +515 to +696 | ±4
 |  | -1012 to -697, -165 to -12, +12 to +165, and +697 to +1012 | +4/-6

## Slide 21: TX EVM for Full BW (Except for Full BW UL-MIMO)
Proposal:
  Non DCM:
    MCS0 to 9 the same as 11ac
    MCS 10 and 11 already motioned
  DCM + MCS0, DCM + MCS1:
    Same as MCS0
  DCM + MCS 3:
    Same as MCS 1
  DCM + MCS 4:
    Same as MCS 2
For trigger based full BW MU-MIMO PPDU, further investigation is needed for the impact of EVM to cross-stream interference

## Slide 22: Used Tone EVM for UL OFDMA Transmissions
The definition of used tone EVM is the same as the full BW EVM except that EVM is computed for the transmitted RU
The transmitted RU shall conform to its own EVM requirement
  EVM requirement is per MCS
  No more than one RU used in a triggered UL PPDU, but multiple RUs in DL OFDMA for example
In order to control the interference to other RUs, for non full bandwidth OFDMA transmission, EVM for UL OFDMA may require some changes compared with full BW cases.
  Details are TBD
Note Appendix contain information on how LTE regulates UL OFDMA transmission

## Slide 23: Tx EVM for DL OFDMA
Proposal:
  EVM shall be computed for each transmitted RU separately and is subject to the EVM limit associated with the MCS of that RU

## Slide 24: Controlling Maximal Interference Outside of the Transmitted RU
Full BW mask is useless (see picture)
Adjacent RX tests are highly complicated and not too informative
  Test equipment is both TX and RX
Mask-like test is less recommended
  Insensitive to MCS, whereas MCS selection is a primary tool of the AP – so loses information
We propose to use EVM-like test
  MCS dependent

## Slide 25: TX EVM for UL OFDMA
For UL OFDMA, EVM concept can be expended to ensure the quality of UL OFDMA transmission
  Used tone EVM: control maximal distortion level in the transmitted RU
  Unused tone EVM: control maximal interference level outside of the transmitted RU, inside the PPDU bandwidth
    Only the HE part is to be controlled by the requirements
    Only important cases: (1) triggered uplink packets, (2) non-contiguous channel bonding

## Slide 26: Unused Tone EVM for UL OFDMA Transmissions
Unused subcarriers carry interference to other RUs in triggered UL transmission
The “unused EVM” of a subcarrier outside the RU is essentially calculated as the linear average power of that subcarrier normalized to the linear average power per subcarrier of the transmitted RU
  This is equivalent to EVM with respect to “origin” constellation
  Since “unused tone EVM” does not include normalization by estimated channel, it is in general SNR-like, and thus ~3dB lower than “used tone” EVM

## Slide 27: Unused tone EVM for UL OFDMA Transmissions (cont.)
To avoid frequency selective variations of the unused tone EVM propose averaging over frequency intervals
  Recommended averaging over 26 subcarriers (2MHz)
  Whether to perform a interval based averaging or moving filter averaging is TBD
Generally speaking, unused tone EVM is worst case when adjacent to the transmitted RU
Prefer “simple” – one unused tone EVM limit for all the unused tones and independent of RU size

## Slide 28: Unused tone EVM Proposal
Proposal:
  Non full bandwidth UL-OFDMA transmissions shall comply with a maximum unused tone EVM limit.
  Unused tone EVM is defined as unused subcarrier power normalized by the average power per subcarrier of the transmitted RU, and averaged over 26 tones in linear domain
  Unused Tone EVM limit is set at TBD(s) below Used Tone EVM limit

## Slide 29: EVM Testing: LO Leakage
For trigger-based PPDU, LO leakage may affect the EVM results and shall be excluded from the computation of both used or unused tone EVM
    Limit today is -32dBc, which for 52 tones is equal to -32+17=-15dBr
    Much higher than EVM levels typically
LO leakage can show up in
  Center frequency of the PPDU tone plan and its +/- 3 tone neighbor
    Digital correction may be used for frequency precorrection for trigger based PPDU
  20MHz operating devices: center of primary20 of the PPDU tone plan and +/- 3 tones
  40MHz operating devices: center of the primary40 of the PPDU tone plan and +/- 3 tones
  Outside of the PPDU BW: e.g. 80MHz capable devices transmits 20MHz or 40MHz PPDU. Doesn’t affect used tone and unused EVM
Test equipment, not knowing exact LO location, can search for the worst used and unused EVM tone in the above possible LO locations and treat it is potential LO
  Exclude this tone from used or unused tone EVM measurement
  Apply LO leakage level requirement on this tone

## Slide 30: EVM Testing: Time Correction
802.11ax is more sensitive to ICI due to timing error
  Longer OFDM symbols (4X) allow bigger timing drift to develop
  Higher MCSs require lower levels of EVM, which are more sensitive to timing errors
The 802.11ac text specifies
  d) Symbols in a PPDU shall be derotated according to estimated frequency offset
Proposal: add timing error correction
  d) Symbols in a PPDU shall be derotated according to estimated frequency offset. Sampling offset drift shall also be compensated.

## Slide 31: EVM Testing: Amplitude Compensation
Background:
  Some implementation may additionally compensate amplitude on top of phase compensation for long packets.
  11n/11ac EVM testing procedure does not explicitly enforce or discourage amplitude compensation in the test procedure.
Issue:
  If test equipment tracks the PA’s amplitude drift (cabled with each Tx path) for long packets especially with multi-streams (where different PA’s hooked to different antennas may drift differently), good EVM will show up on the test equipment even though the intended receiver (over the air) sees bad EVM
Proposal:
  Discourage a bad external PA implementation by adding a explicit text to not to compensate for amplitude drift during EVM testing

## Slide 32: LO Leakage Requirement for 80+80MHz
11ac LO leakage requirement for 80+80MHz was subject to spectral mask requirements.
  “For an 80+80 MHz transmission where the RF LO falls outside both frequency segments, the RF LO shall additionally met the spectral mask requirements as defined in Transmit spectrum mask.”
Proposal:
  Add the same LO leakage requirement for 80+80MHz as in 11ac

## Slide 33: STRAWPOLLS

## Slide 34: Straw Poll #1
Do you agree to the following?
  Limit subcarrier frequency error and symbol clock error at +/-20ppm, except for trigger-based PPDU.
  Keep time of departure accuracy same as in 802.11ac.
Y/N/A

## Slide 35: Straw Poll #2
Do you agree that full bandwidth masks for HE PPDUs are tested with RBW=25kHz and VBW=7.5kHz?
Y/N/A

## Slide 36: Straw Poll #3
Do you agree that every 11ax PPDU is compliant with the full PPDU bandwidth mask?
Y/N/A

## Slide 37: Straw Poll #4
Do you agree that Spectral Flatness is tested for HE PPDUs similarly to 11ac, with the following modifications?
  RU boosting and beamforming shall not be applied during test
  Only non-zero RUs participate in the flow
  Note: spectral flatness is measured on the HE portion only, after GI removal and uses FFT output
Y/N/A

## Slide 38: Straw Poll #5
Do you prefer which of the following spectrum flatness requirement
  Same as 11ac except tone index adjusted for 11ax tone plan as shown in Slide #19
Y/N/A

## Slide 39: Straw Poll #6
Do you agree that following EVM requirements for full BW transmission except for the HE triggered MU-MIMO PPDU?
  Non DCM: MCS0 to 9 the same as 11ac;
  DCM+MCS0 and DCM+MCS1 the same as MCS0 no DCM
  DCM+MCS3 the same as MCS1 no DCM
  DCM+MCS4 the same as MCS2 no DCM
  HE triggered MU-MIMO PPDU EVM requirements are TBD
Y/N/A

## Slide 40: Straw Poll #7
Do you agree that for an DL OFDMA PPDU, EVM shall be computed for each transmitted RU separately and is subject to the EVM limit associated with the MCS of that RU?
Y/N/A

## Slide 41: Straw Poll #8
Do you agree that non full bandwidth UL OFDMA transmissions shall comply with a maximum unused tone EVM limit?
  Maximum unused tone EVM limit is defined as unused subcarrier power normalized to the average power per subcarrier of the transmitted RU and averaged over 26 tones
  Unused tone EVM limit is set at TBD(s) below used tone EVM limit
Y/N/A

## Slide 42: Straw Poll #9
Do you agree that for trigger based PPDU LO leakage shall be excluded from used tone and unused tone EVM computation?
  The LO leakage exclusion method is described in slide #28
Y/N/A

## Slide 43: Straw Poll #10
Do you agree to add the following to EVM test procedure?
  Sampling offset drift shall also be compensated
Y/N/A

## Slide 44: Straw Poll #11
Do you agree to add the same LO leakage restriction for 80+80MHz transmission as 11ac to 11ax?
  For an 80+80 MHz transmission where the RF LO falls outside both frequency segments, the RF LO shall additionally met the spectral mask requirements as defined in X.X.X.X (Transmit spectrum mask).
Y/N/A

## Slide 45: Straw Poll #12
Do you agree to add the following to EVM test procedure?
  Amplitude drift shall not be compensated by the testing instrument
Y/N/A

## Slide 46: Straw Poll #13
Do you agree to accept the proposed text changes in comment resolution document “11-16-xxxx-00-00ax comment-resolution-for-cids-on-phy-transmit-spec”?
Y/N/A

## Slide 47: References
[1] 11-16-xxxx-00-00ax comment-resolution-for-cids-on-phy-transmit-spec

## Slide 48: Appendix

## Slide 49: Simulated Measurements of Unused Tone EVM (1/3)
Simulation Model
  Measurement:
    Not an actual measurement
    Power measure after GI removal and FFT
    Based on models and tested on Matlab
  Non-linearity Modeling:
    AM-AM and AM-PM distortion of PA modeled
  LO leakage: -35dBc
  Residual CFO: >0.01ppm
  I-Q imbalance: >±0.1dB amplitude, >±0.1 degree phase
  Tx IPN: -36dBc
  PPDU BW: 80MHz
  RUs Under Test: 26-Tone RU #6 and 242-Tone RU #2

## Slide 50: Simulated Measurements of Unused Tone EVM (2/3)

## Slide 51: Simulated Measurements of Unused Tone EVM (3/3)

## Slide 52: Summary of Simulated Measurements
 | EVM @ approx. -34dB |  | EVM @ approx. -22dB |  | EVM @ approx. -14dB | 
 | Gap Between EVM and Max Unused Tone Power [dB] | Gap Between EVM and Max Unused 26-Tone Power [dB] | Gap Between EVM and Max Unused Tone Power [dB] | Gap Between EVM and Max Unused 26-Tone Power [dB] | Gap Between EVM and Max Unused Tone Power [dB] | Gap Between EVM and Max Unused 26-Tone Power [dB]
26 Tone RU | 5.7 | 11.2 | 3.0 | 7.4 | 2.6 | 7.0
52 Tone RU | 4.9 | 10.5 | 2.8 | 5.78 | 2.5 | 5.5
242 Tone RU | 4.9 | 7.8 | 3.7 | 4.9 | 4.3 | 5.5
484 Tone RU | 6.9 | 9.0 | 9.8 | 10.6 | 9.5 | 10.2
Observation:
A constant ~5 dB gap between EVM and maximum unused tone power with excellent EVM (i.e. low EVM)
A variable 2 ~ 10dB gap between EVM and maximum unused tone power depending on RU under test with poor EVM (i.e. high EVM)

## Slide 53: Relationship of Interference to Noise Floor
The interference closest to the used spectrum is equal to noise floor plus a constant
  The term G is that 2.5dB~5dB difference between inband EVM and “unused EVM” Assumed first unused subcarrier EVM is equal to last used subcarrier EVM
  For AWGN and a typical device, the constant is around -5dB
  Noise floor is shared for all uplink OFDMA receptions and it includes the noise figure and therefore valid for all RX power levels (all AGC levels at AP)

## Slide 54: Controlling maximal interference level outside of the transmitted RU
Each UL RU contributes interference of about 7dB below AP’s noise floor
  In OFDMA, contribution into RU may be the outcome of multiple RUs, and in particular the two adjacent ones
    With 2 adjacent RUs of similar conditions (SNR and MCS), contributed interference is ~4dB below noise floor; The self interference is ~8dB below noise floor (5dB + 3dB of C.E.)
Not much can be done about it – requiring tighter unused EVM limit will reduce transmit power and accordingly SNR and will keep S/I at similar level

## Slide 55: Tx Requirement for LTE (1/5)
Tx EVM
  Not a function of MCS (only modulation).
    This is because, the exact code rate for LTE system can vary depending on allocated resource units (called resource blocks), number of transmit antennas, etc.
Parameter | Average EVM Level | EVM [dB]
QPSK or BPSK | 17.5 % | -15 dB
16QAM | 12.5 % | -18 dB
64QAM | 8 % | -22 dB

## Slide 56: Tx Requirement for LTE (2/5)
Unused Subcarrier Requirement
Parameter description | Unit | Limit (NOTE 1) |  | Applicable Frequencies
General | dB | Max{ -25 -10 log10(NRB/LCRB), 20log10EVM - 3 -5 (¦ΔRB¦-1)/LCRB, -57dBm/180kHz - PRB} |  | Any non-allocated (NOTE 2)
IQ Image | dB | -25 | Image frequencies when carrier center frequency ≥ 1 GHz | Image frequencies (NOTES 2, 3)
Carrier leakage | dBc | -25 | Output power > 10 dBm and carrier center frequency ≥ 1 GHz | Carrier frequency (NOTES 4, 5)
 |  | -25 | 0 dBm ≤ Output power ≤10 dBm | 
 |  | -20 | -30 dBm ≤ Output power ≤ 0 dBm | 
 |  | -10 | -40 dBm £ Output power < -30 dBm | 
NOTE 1: An in-band emissions combined limit is evaluated in each non-allocated RB. For each such RB, the minimum requirement is calculated as the higher of PRB - 30 dB and the power sum of all limit values (General, IQ Image or Carrier leakage) that apply. PRB is defined in NOTE 10. NOTE 2: The measurement bandwidth is 1 RB and the limit is expressed as a ratio of measured power in one non-allocated RB to the measured average power per allocated RB, where the averaging is done across all allocated RBs. NOTE 3: The applicable frequencies for this limit are those that are enclosed in the reflection of the allocated bandwidth, based on symmetry with respect to the centre carrier frequency, but excluding any allocated RBs. NOTE 4: The measurement bandwidth is 1 RB and the limit is expressed as a ratio of measured power in one non-allocated RB to the measured total power in all allocated RBs. NOTE 5: The applicable frequencies for this limit are those that are enclosed in the RBs containing the DC frequency if NRB is odd, or in the two RBs immediately adjacent to the DC frequency if NRB is even, but excluding any allocated RB. For UE of UL Category M1, the applicable frequencies shall also be the centre frequency of the supported 6RBs additionally. NOTE 6: LCRB is the Transmission Bandwidth (see Figure 5.6-1). NOTE 7: NRB is the Transmission Bandwidth Configuration (see Figure 5.6-1). NOTE 8: EVM is the limit specified in Table 6.5.2.1.1-1 for the modulation format used in the allocated RBs. NOTE 9: ΔRB is the starting frequency offset between the allocated RB and the measured non-allocated RB (e.g. ΔRB =1 or ΔRB =-1 for the first adjacent RB outside of the allocated bandwidth. NOTE 10: PRB is the transmitted power per 180 kHz in allocated RBs, measured in dBm. |  |  |  | 

## Slide 57: Tx Requirement for LTE (3/5)
Unused Subcarrier Power Limit
Max{ -25 -10 log10(NRB/LCRB), 20log10EVM - 3 -5 (|ΔRB|-1)/LCRB, -57dBm/180kHz - PRB }
  In units of resource blocks (RB) (i.e. 180kHz)
  NRB: number of RB in the system (in 20MHz, 100 RB)
  LCRB: number of RB allocated to user
  ΔRB: distance between measurement RB and allocated RB to user. (ΔRB = +/-1, is the RBs right next to the allocated RBs)
  PRB: transmitted power per 180 kHz in allocated RBs, measured in dBm

## Slide 58: Tx Requirement for LTE (4/5)
Low MCS, Small RU Case
QPSK 3/4: EVM -13dB
26-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 12)
106-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 46)
LTE 26 RU
EVM: -13 [dB]
-34.21 [dB] (= -25-10log10(100/12))
Example1: Low MCS, Small RU Case
QPSK 3/4: EVM -13 [dB]
26-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 12)
106-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 46)
EVM
-13 [dB]
Slope starting at -16 [dB]
LTE for 106 RU
-28.37 [dB] (= -25-10log10(100/46))
Note: LTE specifies additional exceptions for IQ-imbalance, and LO Leakage
LTE only requires to meet the maximum value
Proposed Unused Tone EVM
-13 - Margin [dB]

## Slide 59: Tx Requirement for LTE (5/5)
High MCS, Small RU Case
256 QAM 5/6 EVM -32 dB
26-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 12)
106-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 46)
LTE for 26 RU
EVM: -32 [dB]
-34.21 [dB] (= -25-10log10(100/12))
Example 2: High MCS, Small RU Case
256 QAM 5/6 EVM -32 dB
26-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 12)
106-Tone RU (e.g. 2MHz) (NRB = 100, LCRB = 46)
EVM
-32 [dB]
Slope starting at -35 [dB]
LTE for 106 RU
-28.37 [dB] (= -25-10log10(100/46))
LTE only requires to meet the maximum value
Note: LTE specifies additional exceptions for IQ-imbalance, and LO Leakage
Proposed Unused Tone EVM
-32 - Margin [dB]