## Slide 1
MAC Clarifications
Date: 2016-09-11
Authors:

## Slide 2: Overview
We propose to clarify the following:
  Soliciting UL MU Ack in response to DL MU PPDU
  DL MU NAV setting rules

## Slide 3: Trigger variant in DL MU PPDU
This discussion is related to 11-16-1186-00-00ax-A-MPDU content
  Proposes to have Basic variant Trigger allowed in A-MPDU context
    i.e., other variants of Trigger are not allowed in the A-MPDU context
We propose to solve an issue under this context:
  Basic variant Trigger + QoS Data frame(s) can be aggregated in an A-MPDU and solicit immediate UL MU ACK/BA/M-BA[1]
  However, the non-AP STA can also send other QoS Data along with the UL MU ACK which would need immediate ACK as well.
    Not desirable since AP would lose control of sequences within its TXOP
    E.g., the following sequence would not be possible
STA 2
STA 1
STA 3
DL MU PPDU
STA 1 (BA)
SIFS
STA 2 (BA)
STA 5
STA 4
STA 2
DL MU PPDU
STA 4 (BA)
SIFS
STA 5 (BA)
SIFS
STA 2 (BA)

## Slide 4: Proposal fix
Enable the AP to indicate to the STAs in the Basic variant Trigger frame that they are not allowed to aggregate frames that would solicit immediate responses in a response Trigger-based PPDU
  Allocate value 0 of TID Aggregation Limit subfield of User Info field for this purpose.
  Remaining values of the TID Aggregation Limit subfield indicate the maximum number of TIDs that can be aggregated by a STA in a multi-TID A-MPDU
Proposed spec changes to 9.3.1.23.1 of TGax D0.4:
  The TID Aggregation Limit subfield indicates the maximum number of TIDs minus 1 that can be aggregated by a STA in a multi-TID A-MPDU carried in the responding HE trigger-based PPDU.
  NOTE– A value of 7 in the TID Aggregation Limit subfield indicates to the STA that it can aggregate QoS Data frames from any number of different TID values in the multi-TID A-MPDU
Proposed spec changes to 25.5.2.2.2 of TGax D0.4:
  The AP shall set the value in the TID Aggregation Limit subfield in the Type dependent Per User Information field to 0 or 1 for an HE STA with STA that has indicated a zero value in the Multi-TID Aggregation Support field of the HE Capabilities element it transmits and is identified by the AID12 subfield of the User Info field of a Basic Trigger variant Trigger frame (see 9.3.1.23 (Trigger frame format)).(#2669)

## Slide 5: Straw Poll 1
Do you support to instruct the TGax Editor to make the following changes:
TGax Editor: Change the paragraph below of 9.3.1.23.1 of D0.4 as follows:
  The TID Aggregation Limit subfield indicates the maximum number of TIDs minus 1 that can be aggregated by a STA in a multi-TID A-MPDU carried in the responding HE trigger-based PPDU.
  NOTE– A value of 7 in the TID Aggregation Limit subfield indicates to the STA that it can aggregate QoS Data frames from any number of different TID values in the multi-TID A-MPDU.
TGax Editor: Change the paragraph below of 25.5.2.2.2 of D0.4 as follows:
  The AP shall set the value in the TID Aggregation Limit subfield in the Type dependent Per User Information field to 0 or 1 for an HE STA with STA that has indicated a zero value in the Multi-TID Aggregation Support field of the HE Capabilities element it transmits and is identified by the AID12 subfield of the User Info field of a Basic Trigger variant Trigger frame (see 9.3.1.23 (Trigger frame format)).(#2669)

## Slide 6: NAV update rules for DL MU PPDU
Currently the following NAV rule is specified in D0.4:
  When the received frame's RA is equal to the STA's own MAC address, the STA shall not update its intra- BSS NAV or regular NAV with the information from the Duration field.”
Which applies to DL MU PPDUs as well. However,
  This may cause issues because not all receivers are solicited a response
If a set of RXs are not solicited an immediate response but also do not set their NAV then they can content for the medium
  Which can result in collision with trigger-based PPDUs containing the responses
    See example in the next slide

## Slide 7: NAV issue: Example
AP sends DL MU PPDU to STA 1-3
  Soliciting immediate response from STA 1
  Setting Ack policy for STA 2 and 3 to BlockAck
STA 1 sends immediate response in SIFS
STA 2 and STA 3 contend for the medium using EDCA
  They have not updated their NAV and STA 1 is not within range of STA 3
Transmission of STA 2 collides with that of STA 1
STA 2
STA 1
STA 3
DL MU PPDU
STA 1 (BA)
SIFS
STA 2 (Data)
AIFS
…

## Slide 8: Proposal
We propose to remove the following sentence from the D0.4:
  “When the received frame's RA is equal to the STA's own MAC address, the STA shall not update its intra- BSS(#1465) NAV or regular NAV with the information from the Duration field.”
And add spec text that is inline with the following rule:
  “A STA shall update its NAV, irrespectively of whether it is the intended receiver of an MPDU contained in the received PPDU, except that it shall ignore the NAV if the PPDU solicits an immediate response from the STA.”
Refer to 11/16/1173r0 Comment Resolution on Two NAVs - Part II for the proposed spec text change that accounts for this update.

## Slide 9: Straw Poll 2
Do you support the following NAV update rule:
  A STA shall update its NAV, irrespectively of whether it is the intended receiver of an MPDU contained in the received PPDU, except that it shall ignore the NAV if the PPDU solicits an immediate response from the STA.

## Slide 10: References
[1] IEEE802.11ax D0.4