## Slide 1
MAC Clarifications
Date: 2016-09-11
Authors:
Name | Affiliation | Address | Phone | Email
Alice Chen | Qualcomm | 5775 Morehouse Dr. San Diego, CA, USA |  | alicel@qti.qualcomm.com
Albert Van Zelst |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | allert@qti.qualcomm.com
Alfred Asterjadhi |  | 5775 Morehouse Dr. San Diego, CA, USA |  | aasterja@qti.qualcomm.com
Bin Tian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | btian@qti.qualcomm.com
Carlos Aldana |  | 1700 Technology Drive San Jose, CA 95110, USA |  | caldana@qca.qualcomm.com
George Cherian |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gcherian@qti.qualcomm.com
Gwendolyn Barriac |  | 5775 Morehouse Dr. San Diego, CA, USA |  | gbarriac@qti.qualcomm.com
Hemanth Sampath |  | 5775 Morehouse Dr. San Diego, CA, USA |  | hsampath@qti.qualcomm.com
Lin Yang |  | 5775 Morehouse Dr. San Diego, CA, USA |  | linyang@qti.qualcomm.com
Lochan Verma |  | 5775 Morehouse Dr. San Diego, CA USA |  | lverma@qti.qualcomm.com
Menzo Wentink |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | mwentink@qti.qualcomm.com
Naveen Kakani |  | 2100 Lakeside Boulevard Suite 475, Richardson TX 75082, USA |  | nkakani@qti.qualcomm.com
Raja Banerjea |  | 1060 Rincon Circle San Jose CA 95131, USA |  | rajab@qit.qualcomm.com
Richard Van Nee |  | Straatweg 66-S Breukelen, 3621 BR Netherlands |  | rvannee@qti.qualcomm.com

## Slide 2
Robert Stacey | Intel | 2111 NE 25th Ave, Hillsboro OR 97124, USA | +1-503-724-893 | robert.stacey@intel.com
Shahrnaz Azizi |  |  |  | shahrnaz.azizi@intel.com
Po-Kai Huang |  |  |  | po-kai.huang@intel.com
Qinghua Li |  |  |  | quinghua.li@intel.com
Xiaogang Chen |  |  |  | xiaogang.c.chen@intel.com
Chitto Ghosh |  |  |  | chittabrata.ghosh@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Yaron Alpert |  |  |  | yaron.alpert@intel.com
Assaf Gurevitz |  |  |  | assaf.gurevitz@intel.com
Ilan Sutskover |  |  |  | ilan.sutskover@intel.com
Name | Affiliation | Address | Phone | Email
Rolf De Vegt | Qualcomm | 1700 Technology Drive San Jose, CA 95110, USA |  | rolfv@qca.qualcomm.com
Sameer Vermani |  | 5775 Morehouse Dr. San Diego, CA, USA |  | svverman@qti.qualcomm.com
Simone Merlin |  | 5775 Morehouse Dr. San Diego, CA, USA |  | smerlin@qti.qualcomm.com
Tevfik Yucek |  | 1700 Technology Drive San Jose, CA 95110, USA |  | tyucek@qca.qualcomm.com
VK Jones |  | 1700 Technology Drive San Jose, CA 95110, USA |  | vkjones@qca.qualcomm.com
Youhan Kim |  | 1700 Technology Drive San Jose, CA 95110, USA |  | youhank@qca.qualcomm.com

## Slide 3
Name | Affiliation | Address | Phone | Email
Hongyuan Zhang | Marvell | 5488 Marvell Lane, Santa Clara, CA, 95054 | 408-222-2500 | hongyuan@marvell.com
Yakun Sun |  |  |  | yakunsun@marvell.com
Lei Wang |  |  |  | Leileiw@marvell.com
Liwen Chu |  |  |  | liwenchu@marvell.com
Jinjing Jiang |  |  |  | jinjing@marvell.com
Yan Zhang |  |  |  | yzhang@marvell.com
Rui Cao |  |  |  | ruicao@marvell.com
Sudhir Srinivasa |  |  |  | sudhirs@marvell.com
Bo Yu |  |  |  | boyu@marvell.com
Saga Tamhane |  |  |  | sagar@marvell.com
Mao Yu |  |  |  | my@marvel..com
Xiayu Zheng |  |  |  | xzheng@marvell.com
Christian Berger |  |  |  | crberger@marvell.com
Niranjan Grandhe |  |  |  | ngrandhe@marvell.com
Hui-Ling Lou |  |  |  | hlou@marvell.com

## Slide 4
Name | Affiliation | Address | Phone | Email
Jayh Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | hyunh.park@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Eunsung Park |  |  |  | esung.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sungeun Lee | Cypress Semiconductor Corporation |  |  | sungeun.lee@cypress.com
Saishankar Nandagopalan |  |  |  | snan@cypress.com
Stephane Baron | Canon |  |  | stephane.baron@crf.canon.fr
Pascal Viger |  |  |  | pascal.viger@crf.canon.fr
Patrice Nezou |  |  |  | patrice.nezou@crf.canon.fr

## Slide 5
Joonsuk Kim | Apple |  |  | joonsuk@apple.com
Guoqing Li |  |  |  | guoqing_li@apple.com
Jarkko Kneckt |  |  |  | jkneckt@apple.com
Eric Wong |  |  |  | ericwong@apple.com
Chris Hartman |  |  |  | chartman@apple.com
Name | Affiliation | Address | Phone | Email
Jianhan Liu | Mediatek USA | 2860 Junction Ave, San Jose, CA 95134, USA | +1-408-526-1899 | jianhan.Liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
ChaoChun Wang |  |  |  | chaochun.wang@mediatek.com
James Wang |  |  |  | james.wang@mediatek.com
Tianyu Wu |  |  |  | tianyu.wu@mediatek.com
Russell Huang |  |  |  | russell.huang@mediatek.com
James Yee | Mediatek | No. 1 Dusing 1st Road, Hsinchu, Taiwan | +886-3-567-0766 | james.yee@mediatek.com
Alan Jauh |  |  |  | alan.jauh@mediatek.com
Frank Hsu |  |  |  | frank.hsu@mediatek.com

## Slide 6
Name | Affiliation | Address | Phone | Email
David X. Yang | Huawei | F1-17, Huawei Base, Bantian, Shenzhen |  | david.yangxun@huawei.com
Jiayin Zhang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai | +86-18601656691 | zhangjiayin@huawei.com
Jun Luo |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | jun.l@huawei.com
Yi Luo |  | F1-17, Huawei Base, Bantian, Shenzhen | +86-18665891036 | Roy.luoyi@huawei.com
Yingpei Lin |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | linyingpei@huawei.com
Jiyong Pang |  | 5B-N8, No.2222 Xinjinqiao Road, Pudong, Shanghai |  | pangjiyong@huawei.com
Zhigang Rong |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | zhigang.rong@huawei.com
Jian Yu |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  | F1-17, Huawei Base, Bantian, Shenzhen |  | ming.gan@huawei.com
Yuchen Guo |  | F1-17, Huawei Base, Bantian, Shenzhen |  | guoyuchen@huawei.com
Yunsong Yang |  | 10180 Telesis Court, Suite 365, San Diego, CA 92121 NA |  | yangyunsong@huawei.com
Junghoon Suh |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | Junghoon.Suh@huawei.com
Peter Loc |  |  |  | peterloc@iwirelesstech.com
Edward Au |  | 303 Terry Fox, Suite 400 Kanata, Ottawa, Canada |  | edward.ks.au@huawei.com
Teyan Chen |  | F1-17, Huawei Base, Bantian, Shenzhen |  | chenteyan@huawei.com
Yunbo Li |  | F1-17, Huawei Base, Bantian, Shenzhen |  | liyunbo@huawei.com

## Slide 7
Bo Sun | ZTE | #9 Wuxingduan, Xifeng Rd., Xi'an, China |  | sun.bo1@zte.com.cn
Kaiying Lv |  |  |  | lv.kaiying@zte.com.cn
Yonggang Fang |  |  |  | yfang@ztetx.com
Ke Yao |  |  |  | yao.ke5@zte.com.cn
Weimin Xing |  |  |  | xing.weimin@zte.com.cn
Brian Hart | Cisco Systems | 170 W Tasman Dr, San Jose, CA 95134 |  | brianh@cisco.com
Pooya Monajemi |  |  |  | pmonajem@cisco.com
Name | Affiliation | Address | Phone | Email
Ron Porat | Broadcom |  |  | rporat@broadcom.com
Sriram Venkateswaran |  |  |  | 
Matthew Fischer |  |  |  | mfischer@broadcom.com
Zhou Lan |  |  |  | 
Leo Montreuil |  |  |  | 
Andrew Blanksby |  |  |  | 
Vinko Erceg |  |  |  | 
Thomas Derham |  |  |  | 
Mingyue Ji |  |  |  | 

## Slide 8
Name | Affiliation | Address | Phone | Email
Fei Tong | Samsung | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434633 | f.tong@samsung.com
Hyunjeong Kang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-31-279-9028 | hyunjeong.kang@samsung.com
Kaushik Josiam |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7437 | k.josiam@samsung.com
Mark Rison |  | Innovation Park, Cambridge CB4 0DS (U.K.) | +44 1223 434600 | m.rison@samsung.com
Rakesh Taori |  | 1301, E. Lookout Dr, Richardson TX 75070 | (972) 761 7470 | rakesh.taori@samsung.com
Sanghyun Chang |  | Maetan 3-dong; Yongtong-Gu Suwon; South Korea | +82-10-8864-1751 | s29.chang@samsung.com
Yasushi Takatori | NTT | 1-1 Hikari-no-oka, Yokosuka, Kanagawa 239-0847 Japan | +81 46 859 3135 | takatori.yasushi@lab.ntt.co.jp
Yasuhiko Inoue |  |  | +81 46 859 5097 | inoue.yasuhiko@lab.ntt.co.jp
Shoko Shinohara |  |  | +81 46 859 5107 | Shinohara.shoko@lab.ntt.co.jp
Yusuke Asai |  |  | +81 46 859 3494 | asai.yusuke@lab.ntt.co.jp
Koichi Ishihara |  |  | +81 46 859 4233 | ishihara.koichi@lab.ntt.co.jp
Junichi Iwatani |  |  | +81 46 859 4222 | Iwatani.junichi@lab.ntt.co.jp

## Slide 9
Name | Affiliation | Address | Phone | Email
Masahito Mori | Sony Corp. |  |  | Masahito.Mori@jp.sony.com
Yusuke Tanaka |  |  |  | YusukeC.Tanaka@jp.sony.com
Yuichi Morioka |  |  |  | Yuichi.Morioka@jp.sony.com
Kazuyuki Sakoda |  |  |  | Kazuyuki.Sakoda@am.sony.com
William Carney |  |  |  | William.Carney@am.sony.com
Sigurd Schelstraete | Quantenna |  |  | Sigurd@quantenna.com
Huizhao Wang |  |  |  | hwang@quantenna.com
Narendar Madhavan | Toshiba |  |  | narendar.madhavan@toshiba.co.jp
Masahiro Sekiya |  |  |  | 
Toshihisa Nabetani |  |  |  | 
Tsuguhide Aoki |  |  |  | 
Tomoko Adachi |  |  |  | 
Kentaro Taniguchi |  |  |  | 
Daisuke Taki |  |  |  | 
Koji Horisaki |  |  |  | 
David Halls |  |  |  | 
Filippo Tosato |  |  |  | 
Zubeir Bocus |  |  |  | 
Parag Kulkarni |  |  |  | 

## Slide 10: Overview
We propose to clarify the following:
  Soliciting UL MU Ack in response to DL MU PPDU
  DL MU NAV setting rules

## Slide 11: Trigger variant in DL MU PPDU
This discussion is related to 11-16-1186-00-00ax-A-MPDU content
  Proposes to have Basic variant Trigger allowed in A-MPDU context
    i.e., other variants of Trigger are not allowed in the A-MPDU context
We propose to solve an issue under this context:
  Basic variant Trigger + QoS Data frame(s) can be aggregated in an A-MPDU and solicit immediate UL MU ACK/BA/M-BA[1]
  However, the non-AP STA can also send other QoS Data along with the UL MU ACK which would need immediate ACK as well.
    Not desirable since AP would lose control of sequences within its TXOP
    E.g., the following sequence would not be possible
STA 2
STA 1
STA 3
DL MU PPDU
STA 1 (BA)
SIFS
STA 2 (BA)
STA 5
STA 4
STA 2
DL MU PPDU
STA 4 (BA)
SIFS
STA 5 (BA)
SIFS
STA 2 (BA)

## Slide 12: Proposal fix
Enable the AP to indicate to the STAs in the Basic variant Trigger frame that they are not allowed to aggregate frames that would solicit immediate responses in a response Trigger-based PPDU
  Allocate value 0 of TID Aggregation Limit subfield of User Info field for this purpose.
  Remaining values of the TID Aggregation Limit subfield indicate the maximum number of TIDs that can be aggregated by a STA in a multi-TID A-MPDU
Proposed spec changes to 9.3.1.23.1 of TGax D0.4:
  The TID Aggregation Limit subfield indicates the maximum number of TIDs minus 1 that can be aggregated by a STA in a multi-TID A-MPDU carried in the responding HE trigger-based PPDU.
  NOTE– A value of 7 in the TID Aggregation Limit subfield indicates to the STA that it can aggregate QoS Data frames from any number of different TID values in the multi-TID A-MPDU
Proposed spec changes to 25.5.2.2.2 of TGax D0.4:
  The AP shall set the value in the TID Aggregation Limit subfield in the Type dependent Per User Information field to 0 or 1 for an HE STA with STA that has indicated a zero value in the Multi-TID Aggregation Support field of the HE Capabilities element it transmits and is identified by the AID12 subfield of the User Info field of a Basic Trigger variant Trigger frame (see 9.3.1.23 (Trigger frame format)).(#2669)

## Slide 13: Straw Poll 1
Do you support to instruct the TGax Editor to make the following changes:
TGax Editor: Change the paragraph below of 9.3.1.23.1 of D0.4 as follows:
  The TID Aggregation Limit subfield indicates the maximum number of TIDs minus 1 that can be aggregated by a STA in a multi-TID A-MPDU carried in the responding HE trigger-based PPDU.
  NOTE– A value of 7 in the TID Aggregation Limit subfield indicates to the STA that it can aggregate QoS Data frames from any number of different TID values in the multi-TID A-MPDU.
TGax Editor: Change the paragraph below of 25.5.2.2.2 of D0.4 as follows:
  The AP shall set the value in the TID Aggregation Limit subfield in the Type dependent Per User Information field to 0 or 1 for an HE STA with STA that has indicated a zero value in the Multi-TID Aggregation Support field of the HE Capabilities element it transmits and is identified by the AID12 subfield of the User Info field of a Basic Trigger variant Trigger frame (see 9.3.1.23 (Trigger frame format)).(#2669)

## Slide 14: NAV update rules for DL MU PPDU
Currently the following NAV rule is specified in D0.4:
  When the received frame's RA is equal to the STA's own MAC address, the STA shall not update its intra- BSS NAV or regular NAV with the information from the Duration field.”
Which applies to DL MU PPDUs as well. However,
  This may cause issues because not all receivers are solicited a response
If a set of RXs are not solicited an immediate response but also do not set their NAV then they can content for the medium
  Which can result in collision with trigger-based PPDUs containing the responses
    See example in the next slide

## Slide 15: NAV issue: Example
AP sends DL MU PPDU to STA 1-3
  Soliciting immediate response from STA 1
  Setting Ack policy for STA 2 and 3 to BlockAck
STA 1 sends immediate response in SIFS
STA 2 and STA 3 contend for the medium using EDCA
  They have not updated their NAV and STA 1 is not within range of STA 3
Transmission of STA 2 collides with that of STA 1
STA 2
STA 1
STA 3
DL MU PPDU
STA 1 (BA)
SIFS
STA 2 (Data)
AIFS
…

## Slide 16: Proposal
We propose to remove the following sentence from the D0.4:
  “When the received frame's RA is equal to the STA's own MAC address, the STA shall not update its intra- BSS(#1465) NAV or regular NAV with the information from the Duration field.”
And add spec text that is inline with the following rule:
  “A STA shall update its NAV, irrespectively of whether it is the intended receiver of an MPDU contained in the received PPDU, except that it shall ignore the NAV if the PPDU solicits an immediate response from the STA.”
Refer to 11/16/1173r0 Comment Resolution on Two NAVs - Part II for the proposed spec text change that accounts for this update.

## Slide 17: Straw Poll 2
Do you support the following NAV update rule:
  A STA shall update its NAV, irrespectively of whether it is the intended receiver of an MPDU contained in the received PPDU, except that it shall ignore the NAV if the PPDU solicits an immediate response from the STA.

## Slide 18: References
[1] IEEE802.11ax D0.4