## Slide 1: Intra-PPDU Power Save for a Multiple BSSID Set Case
Date: 2016-09-12
Authors:

## Slide 2: Abstract
The draft spec defines the intra-PPDU power save operation [1].
This contribution proposes a condition to enter the doze state for power saving using the intra-PPDU power save operation.

## Slide 3: Intra-PPDU Power Save for a Multiple BSSID Set Case
An HE STA is not able to transmit/receive a PPDU to/from the associated AP during the transmission of the BSS of a multiple BSSID set that the STA’s associated BSS belongs to.
Therefore, the STA may enter the doze state during the PPDU.
Preamble | (A-)MPDU
BSSID(0)
BSSID(1)
STA0
STA1
PPDU
(associated)
(STA1 receives a PPDU from AP of BSSID(0)
MAC header | 
MPDU
Including BSSID(0)
STA1’s state
Awake
Doze
(Multiple BSSID set)

## Slide 4: Conclusions
Additional power save condition would be helpful.
  An HE STA can determine if a received frame is from a BSS of a multiple BSSID set that the STA’s associated BSS belongs to.
  The STA may enter the doze state during the frame.

## Slide 5: References
[1] Draft P802.11ax D0.4

## Slide 6: Straw Poll
Do you agree to adopt the spec text change as shown in doc 11-16/1205r0?
  Y
  N
  A