## Slide 1: EDMG dynamic channel BW signalling
Date: 2016-09-11
Authors:

## Slide 2: Abstract
Solution for BW signaling at TXOP establishment

## Slide 3
Purpose and definitions
The purpose of this presentation is to provide solution for BW signaling at TXOP establishment

## Slide 4
Tx Sequence in multiple channels BW allocation from 2016-TECH-Intel-0031-01-NG60 channel bonding more details r1
STA A decides not to use secondary channel due to CCA busy and still use primary channel to utilize opportunity to deliver data
RTS/CTS provides BW indication
Energy is detected by STA A in Secondary channel
TXOP initiator is able to change Tx BW at the time it issues RTS in response to conditions changes
TXOP responder is able to receive frame sent not in full BW
Tx Sequence in multiple channels BW allocation

## Slide 5
Two types of multiple channel accesses - channel bonding and channel aggregation may be supported in parallel in the same BSS
Associated STA’s know widest channel allowed to be occupied and primary channel number in advance, communicated by beacon, action frame, “Grant”, and so on
Actual BW is decided by a TXOP initiator instantly at RTS transmission
Actual channel signaled in RTS and DMG CTS may be any valid channel that includes current primary channel and subset of secondary channels
Indicating channel bandwidth relatively to known primary channel and known widest allowed channel is enough to align channel occupation between TXOP initiator and TXOP responder
Assumptions and requirements

## Slide 6
Channel BW indication from 11-15-1358-09-00ay-11ay Spec Framework

## Slide 7
B22, B23 of PHY Header | Desired channel bandwidth | Channels occupation Number of 2.16GHz channels that establish 4x2.16GHz channel in increasing order |  |  |  | Setting of Scrambler Initialization field to encode BW | 
 |  |  |  |  |  | B0 | B1, B2, B3
 |  | n | n+1 | n+2 | n+3 |  | 
11 | 1 | u | NA | NA | NA | 1 | 0
 |  | NA | u | NA | NA |  | 
 |  | NA | NA | u | NA |  | 
 |  | NA | NA | NA | u |  | 
 | 2 | u | u | NA | NA |  | 1 Lower channel-even
 |  | NA | NA | u | u |  | 
 | 2 | u | u | NA | NA |  | 2 Lower channel-odd
 |  | NA | NA | u | u |  | 
 | 3 | u | u | u | NA |  | 3
 | 3 | NA | u | u | u |  | 4
 | 4 | u | u | u | u |  | 5
 | Aggregated two 2.16 GHz channels | u | NA | u | NA |  | 6
 |  | NA | u | NA | u |  | 
 | Aggregated two 2.16 GHz channels | u | NA | NA | u |  | 7
Proposed signaling
Notation: u- channel is use, NA-channel not in use

## Slide 8: Straw polls
Do you support the encoding of bonded channels codes 0-5 as presented in slide 7?

## Slide 9: References