## Slide 1: WUR-based Broadcast Reference Signal
Date: 2016-09-12
Authors:

## Slide 2: Introduction
In 802.11 network, AP broadcasts periodic Beacon frame
  STAs receive BSS operation information
  STAs can monitor the connectivity status between AP
WUR-based power saving STAs, during when there is no wake-up packet transmission
  STAs cannot monitor the connectivity status between AP
  STAs do not know whether they are within the WUR coverage of the AP
We propose that WUR AP to periodically broadcast a reference signal for WUR STAs
WUR AP
WUR STA
WUR
802.11 TR
802.11 TR
802.11 Transceiver
Wake Up Radio
Beacon
/ Data
Wakeup
Packet

## Slide 3: WUR-based Broadcast Reference Signal
WUR AP may periodically broadcast the reference signal
  In scenarios where WUR-based sleeping STAs are required to monitor the WUR connectivity between AP
  The signal’s transmission period can be set much longer than the Beacon transmission period
  The length of the signal can be shorter than normal wake-up packets, only required to contain the transmitter information
WUR-based STAs can monitor the reference signal
  Measure the signal strength and monitor WUR connectivity with its AP
  Power consumption of the reference signal reception would not be much higher than that of the idle listening
WUR
Ref
Sig
802.11 TR
802.11
Beacon
Frame
802.11
Beacon
Frame
802.11
Beacon
Frame
WUR
Ref
Sig

## Slide 4: Scenario 1: WUR RX sensitivity control
A
WUR range
In scenarios where WUR STAs want to minimize their idle listening power consumptions
Without WUR reference signal:
  STAs cannot measure the relative distance to its AP, thus maintain their WUR with the maximum RX sensitivity
  Maintaining better RX sensitivity consumes more power in WUR [2]
With WUR reference signal:
  STA A receives the signal with very high RSSI, adjusting its WUR RX sensitivity to reduce power consumption
  STA B receives the signal with low RSSI, adjusting its WUR RX sensitivity to better receive wake-up packets
B

## Slide 5: Scenario 2: WUR coverage monitoring before sleep
WUR range
A
Data range
In scenarios where a certain STA has different connectivity range between WUR and 802.11 with the associated AP
Without WUR reference signal:
  STA A can falsely enter WUR-based power save mode in locations where it can not receive wake-up packets
With WUR reference signal:
  STA A monitors the reference signal, and decides to enter WUR-based power save mode only when the signals are stably received

## Slide 6: Scenario 3: WUR coverage monitoring during sleep
WUR range
B
A
In scenarios where STAs have mobility during sleep
Without WUR reference signal:
  STAs cannot measure the distances to its AP, thus do not handle the coverage lost [3]
With WUR reference signal:
  STA A receives AP’s reference signal with very low RSSI, may notify to its 802.11 transceiver
  STA B does not receive the reference signal for a certain time, should notify to its 802.11 transceiver
mobility

## Slide 7: Scenario 4: Network discovery during sleep
WUR range
In scenarios where STAs want to discover nearby 802.11 network without turning on their 802.11 transceiver
Without WUR reference signal:
  STAs do not know the availability of network until they turn on 802.11 transceiver
With WUR reference signal:
  STAs receive the reference signal from nearby AP, thus may wake-up 802.11 transceiver to notify network availability
  To minimize unnecessary wake-up of 802.11 TR, WUR may limit the wake-up with pre-defined conditions

## Slide 8: Conclusions
WUR should enable STAs to remain low-power state without sacrificing instant reachability
WUR AP may periodically broadcast reference signal
  WUR STAs can periodically monitor connectivity status between AP
  The length of the signal would be shorter than normal wake-up packets
  Small increase in the signal decoding overhead and channel occupancies with tradeoff of other benefits
Benefits for WUR STAs
  STAs can adjust their RX sensitivity to reduce idle power consumptions
  STAs can monitor WUR coverage before/during sleep state
  STAs can discover nearby BSSs with minimal power consumptions

## Slide 9: References
  [1] 11-16/0605r3, Proposal for LP-WUR Study Group
  [2] N. Seyed Mazloum and O. Edfors, “Performance Analysis and Energy Optimization of Wake-Up Receiver Schemes for Wireless Low-Power Applications”, IEEE Trans. on Wireless Communications, Vol. 13, No. 12, pp. 7050-7061, 2014.
  [3] 11-16/0931r0, Demand on Roaming for WUR, ZTE