## Slide 1
MU mode EDCA control
Date: 2016-09-14
Authors:

## Slide 2: Background
EDCA operation after trigger frame reception has been discussed and specified
  When an HE STA successfully receives the corresponding acknowledgement frame in response to the MPDU sent in HE trigger based PPDU, the backoff for the associated EDCAF resumes the backoff counter countdown. [1][2]
  An HE non-AP UL MU capable STA that receives a Basic variant Trigger frame that contains a Per User Info field with the AID of the STA, and that receives an immediate response from the AP for the transmitted Trigger-based PPDU, shall:[3]
    update its CWmin[AC], CWmax[AC], AIFSN[AC], state variables to the values contained in the most recently received MU EDCA Parameter Set element sent by the AP to which the STA is associated, for all the ACs from which QoS Data frames were transmitted in the trigger-based PPDU.

## Slide 3: New EDCA set for MU opportunity
New EDCA set[4]
  MU EDCA set is a new EDCA parameter set that it lowers STAs’ channel access opportunity
  MU EDCA set could be used for enhancing 11ax efficiency
  When MU EDCA is indicated, HE non-AP STAs shall use MU EDCA parameters for its SU channel access
  MU EDCA indication might be performed by Trigger Frame
    For some HE STAs or all the HE STAs
    For each AC or all ACs
    SU EDCA indication is possible, also (Return to conventional EDCA)
  As a result of MU EDCA set, STAs would transmit HE trigger-based PPDUs rather than other SU PPDUs

## Slide 4: MU mode EDCA from new EDCA set
If UL MSDU is arrived after EDCA mode change indication (by Trigger Frame), MU EDCA parameters for the MSDU can be applied - No problem

## Slide 5: Issue for MU mode EDCA
Does retransmission count affect its new back-off procedure of MU EDCA?
  If retransmission occurred, how new EDCA CW would be applied to its exist channel access procedure?(CW_MU_min? or more larger one? or doubled CW of SU EDCA parameter?)

## Slide 6: Issue for MU mode EDCA
Similar to MU Mode initiation, procedure after MU MODE expiration need to be considered
  After MU Mode truncation or MU EDCA timer expiration, procedures for the existing back-off timer and retransmission timer need to be considered as well as its MU Mode initiation procedure

## Slide 7: Possible solutions for MU mode EDCA
Option 1-1 (Reset back-off and CW doubling)
  Reset its back-off number based on a changed EDCA set
  Retransmission history is not considered(CWmin_mu for ReTx)
Option 1-2 (Reset back-off but CW based on # of ReTx)
  Reset its back-off number based on a changed EDCA set
  Using CW value considering retransmission(2^(n-1)* CWmin_mu)
Option 2-1 (Sustain back-off for last frame)
  Sustain last EDCA procedure until transmission success or retransmission limit (MU mode is applied after EDCA procedure of last frame)
Option 2-2 (Sustain back-off for last frame once)
  Sustain last EDCA procedure only once
  Whether the transmission is success or not, next transmission follows option 1(Do not reset back-off number but applying new CW immediately)

## Slide 8: Conclusions
Because TG determined “EDCA back-off value is not changed after its trigger frame reception and transmission of HE Trigger based PPDU”, we prefer to apply this concept for MU mode EDCA, too.
In other words, we prefer option 2 rather than option 1.
Retransmission contention windows need to be considered
  We prefer first option of retransmission
As a result, we prefer option 2-1

## Slide 9: Straw poll
Do you agree to add the following text to Spec Draft?
  25.2.2 Obtaining an EDCA TxOP for UL MU capable STAs
    When the HEMUEDCATimer of an HE non-AP STA reaches 0, the backoff for the associated EDCAF resumes the backoff counter countdown and legacy EDCA parameters shall not be applied until the EDCAF initialization
      Never changes existing back-off value
      Gets a retransmission back-off counter from doubled CW value originated from MU_CW_min after the timer expire
    Red colored text is not the suggested Draft Text

## Slide 10: References
[1] Draft P802.11ax_D0.4
[2] 11-16/0880r2 “UL MU Transmission Rules - EDCA backoff”
[3] 11-16/1180r0 “Proposed spec text for MU EDCA parameters”
[4] 11-16/0998r1 “2 sets of EDCA parameters”