## Slide 1
UL OFDMA-based Random Access Parameter Set (RAPS) element
Date: 2016-09-12
Authors:
Chittabrata Ghosh, Intel
Name | Affiliation | Address | Phone Number | E-mail
Chittabrata Ghosh | Intel Corporation |  | +1-415-244-8904 | chittabrata.ghosh@intel.com
Robert Stacey | Intel Corporation |  |  | 
Kiseon Ryu | LGE |  |  | 
Jeongki Kim | LGE |  |  | 
Jayh Park | LGE |  |  | 
Yunbo Li | Huawei |  |  | 

## Slide 2: Abstract
In this contribution, we propose an element for signaling of parameters needed for the operation of UL OFDMA-based random access
Chittabrata Ghosh, Intel

## Slide 3: Goal of the presentation
The IEEE SFD 11-15/0132r15 mentions about the following mechanism to be defined:
  An AP indicates the value of OCWmin used by all STAs for the random RU allocation process for the next UL MU OFDMA transmissions. The value of OCWmin is transmitted through a dedicated field in the beacon frame.
Chittabrata Ghosh, Intel

## Slide 4: Proposed Comment Resolution
CID |  | Page Number | Line Number | Comment | Proposed Change
600 | 25.10.3 | 60 | 48 | The standard shall provide a mechanism to change Trigger-based Random access contention parameters on the fly | Either introduce a new information element or extend the format of the trigger frame
2384 | 25.10.3 | 47 | 3 | OCWmin is used by STA, but the mechanism of delivering OCWmin to STA is not defined. | Define
Propose to define the parameters for UL OFDMA-based random access in Random Access Parameter Set (RAPS) element
Chittabrata Ghosh, Intel

## Slide 5: Proposed Random Access Parameter Set element format
Element ID | Length | Element ID Extension | OCW Range
We propose the Random Access Parameter Set element (RAPS) with the following subfields
  Element ID: Defined as in baseline REVmc_6.0
  Length: Defined as in baseline REVmc_6.0
  Element ID Extension: Defined as in baseline 11ax Draft 0.4
  OCW Range: This field indicates the minimum and maximum values of the OCW
The RAPS element is carried in Beacon and Probe Response frames
Octets 1 1 1 1
Chittabrata Ghosh, Intel

## Slide 6: Definition of the OCW Range Field in RAPS element
EOCW_min: This subfield indicates the minimum value of OCW for first HE Trigger-based PPDU transmission using UL OFDMA-based random access
EOCW_max: This subfield indicates the maximum value of OCW for retransmission attempts using UL OFDMA-based random access
The values in the EOCWmin and EOCWmax subfields encode the values of OCWmin and OCWmax, respectively, in an exponent form and defined as:
    OCWmin = 2EOCWmin – 1
    OCWmax = 2EOCWmax – 1
Chittabrata Ghosh, Intel
EOCW_min | EOCW_max
Bits 4 4

## Slide 7: Conclusion
We proposed the signaling mechanism by defining the RAPS element for operation of UL OFDMA-based random access
We have provided the comment resolution to the comments received with respect to the signaling mechanism
September 2016
Chittabrata Ghosh, Intel