## Slide 1: Location Measurement Protocol for Unassociated STAs
Date: 2016-09-13
Authors:

## Slide 2: Abstract
In this presentation we describe how UL OFDMA-based random access protocol may be used for setting and allocating resources for location measurements by unassociated HE STAs

## Slide 3: Related Functional Requirements:
From the accuracy and coverage protocol section:
The location protocol shall support positioning measurement of unassociated and associated STAs in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent positioning measurements of multiple STAs, in both associated and unassociated states in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of an AP in HE operation mode. The same requirement shall also apply to VHT operation mode.

## Slide 4: UL MU Operation for Unassociated Mode Support
11ax UL MU mode is TF based, where STAs are identified and assigned resources using an 11 bit identification (AID 12 subfield in Per User Info field):
  AP needs to be able to allocate DL and UL resources (medium for sounding and possibly measurement reporting).
  STA needs to know its identification (e.g. AID or Pre-AID)
  Required for STA identification for both NDP (to reuse the TF)

## Slide 5: UL OFDMA-based Random Access Metrics in 802.11ax
Random access RU
  An RU allocated to AID 0 signaled in Trigger frame
  TFR is a Trigger frame (TF) with at least one RU assigned to AID 0
OCW
  Contention Window for OFDMA
OCWmin, OCWmax
  Min and max values for OCW
OBO (OFDMA Backoff Count) counter
  A counter maintained by the STA that determines the random access RU the STA utilizes

## Slide 6: Recap: HE UL OFDMA-based Random Access Procedure in 802.11ax
Illustration of random access (RA) using 3 STAs with initial OBO values 1, 3, and 4, respectively
  STAs 1 and 2 initiate RA in the first Trigger frame with RA RUs assigned to AID 0
  STA 3 initiates RA in the second Trigger frame with RA Rus assigned to AID 0
STA 2 counts down to 0 in first Trigger frame and selects RU 2 for its HE Trigger-based UL PPDU
STA 1 resumes countdown and decrements its OBO count to 0 in second Trigger frame and selects RU 1 for its HE Trigger-based UL PPDU
STA 3 with a non-zero OBO counter waits for the next Trigger frame with RA RUs

## Slide 7: Frame exchange flow description
Similar to an FTM session as defined in REVmc, the proposed mechanism is composed of 3 stages:
  Service negotiation phase
    Capability exchange and supportive location information exchange with adaptation to support MIMO operation and HE MU mode
      LCI and CIVIC IEs (same as REVmc)
      Location supported modulation and BW (same as REVmc)
      Number of Tx and Rx chains (to support MIMO – extension of the REVmc)
      Location or Location offset of additional Tx chains (to support MIMO – extension of the REVmc)
      Possibly information related to scheduling (e.g. how frequent location measurement executed).
    Resource negotiation and assignment
      In REVmc, this was used to allocate resource at the AP for the STA’s location context (e.g., token ID associated with the FTM session)
      For HE STAs, STA AIDs are indicated (Pre-AID for unassociated STAs) and resource allocation (random access RUs) information
    The Multi-STA BA (M-BA) is used for Pre-AID assignment and ACK to unassociated STAs and ACK to FTM requests from associated STAs
  Measurement exchange
  Termination (can be implicit or explicit, to be discussed at a later time)

## Slide 8: Proposed Service Negotiation Phase
TF Service Request
FTM Request
Responding STA
Initiating STA(s)
FTM
Propose that the TF Service Request frame solicits one or multiple Initial FTM Request frame(s) from initiating STA(s) allowing capability exchange
The responding STA sends an M-BA in response to the FTM Request frames
Finally, the responding STA sends an FTM to complete the service negotiation phase
  Reuse legacy FTM frame and add 11az IEs
  Legacy STAs skip the 11az IEs
SIFS
M-BA
SIFS
Same as REVmc
(<= 10ms recommended)
SIFS
Ack

## Slide 9: Recap: Existing Per STA Info Subfield Format in M-BA in 11ax
Per AID TID
Info
Block ACK Starting Sequence Control
Block ACK Bitmap
B0-B11: The AP indicates the STA AID for which the Block ACK Bitmap is included
ACK Type: The AP indicates ACK of single MPDU or all MPDUs when B11=0 and when B11=1, the Block ACK bitmap indicates reception of multiple MPDUs in an A-MPDU
TID: This field indicates the TID value of MPDUs for which the Block ACK Bitmap is included;
AID
ACK Type
TID
Per AID TID Info subfield
Per STA Info subfield
Bits B0 B10 B11 B12 B15

## Slide 10: Proposed Per STA Info Subfield in M-BA Frame for an unassociated STA using Random Access
We propose the following modified sub-fields in the Per STA Info subfield
  B0-B10: Un-association ID (UID) value (e.g., 11111111111) used as an unassociated STA identifier (11ax draft mentions this subfield to be an AID)
  B11: The value is always set to ACK when B0-B10 is an UID (identical to 11ax draft)
  TID Value: The AP sets this value to 1111 when B0-B10 is an UID and B11 is set to ACK (identical to 11ax draft for a management frame)
  RA: This field indicates the MAC address of the transmitter (unassociated STA) as identified from the A2 Address field of UL management frame (new proposal not in 11ax draft)
  Pre-AID: A random value assigned by the AP to the unassociated STA identified by the MAC address
    This value is selected from a set of AIDs not assigned to associated STAs (new proposal not in 11ax draft)
Un-association ID (UID) | ACK | TID Value = 1111
Bits 16 16 48 11 5
B0 B10 B11 B12 B15
Per AID TID Info | Reserved | RA | Pre-AID | Reserved
Per STA Info subfield

## Slide 11: Pre-Association Exchange Procedure with Random Access
A STA parses the value in the B0-B10 subfield as follows:
  If the value is equal to an AID, and the STA is an associated STA, it parses the remaining subfields as in the baseline 11ax specification
  If the value is equal to an AID, and the STA is an unassociated STA, it skips the 10 octets following the Per TID Info subfield
  If the value is equal to an UID, and the STA is an associated STA, then it skips the 10 octets following the Per TID Info subfield
  If the value is equal to an UID, and the STA is an unassociated STA, it parses the MAC Address and the pre-AID subfields
The AP uses the pre-AID in order to schedule RUs in the following Trigger frame(s) to the unassociated STA uniquely identified by the value in the MAC Address subfield in the M-BA frame

## Slide 12: Is a Negotiation Phase Required?
Any measurement protocol would require a client to know the LCI and antenna location
  Calculating location distance/range measurement is required
Any measurement protocol would require a client to know the following:
  CIVIC information
  Civic location is used for dispatch address
  Format and bandwidth (same as REVmc)
  Other Radio capabilities – e.g., # of antennas
  Resource allocation and identification assignment (e.g., pre-AID) – e.g. interval between measurements

## Slide 13: Proposed Measurement Exchange
Following the service negotiation phase, the AP allocates resources for UL sounding (NDP) indicating AIDs and Pre-AIDs;
  UL sounding is followed by DL sounding
The 2nd TF allocates resources for STA to provide location measurement report (LMR) to AP
  Followed by reciprocal report from AP to STA (Location Measurement Report)
TF (Sounding)
NDP
AP
STA(s)
LMR (AP to STA)
SIFS
NDP
SIFS
SIFS
LMR (STA to AP)
SIFS
SIFS
TF

## Slide 14: Protocol properties
The UL NDPs may be staggered in time or spatial domain and are 11az NDP; format of NDP is TBD
Adapting the FTM protocol to 11ax scheme
Based on the 11ax scheduling infrastructure with STAs 1 to n
Constant interval between measurement and report
Possibly reusing the previously proposed VHT protocol to the 11ax
Power efficient – completes within a single TxOP
Location measurement exchange part
UL sounding
part
SIFS
Tx OP
NDP n (sound)
:
:
NDP 1 (sound)
TF
SIFS
SIFS
SIFS
AP2STA LMR
part
AP2STA
STA n
(LMR)
:
:
AP2STA
STA 1
(LMR)
SIFS
STA2AP LMR
part
STA2AP
STA n
(LMR)
:
:
STA2AP
STA 1
(LMR)
TF
SIFS
DL sounding
part
DL
NDP
~100us

## Slide 15: Conclusion
In this contribution, we have shown how FTM negotiation can be performed for both associated and unassociated modes using UL OFMDA-based Random Access mechanism
We have further proposed the negotiation phase using M-BA frame assigning the Pre-AID to an unassociated STA

## Slide 16: Straw poll 1
Do you support the proposed service negotiation phase as illustrated below for HE STAs?
TF Service Request
FTM Request
Responding STA
Initiating STA(s)
FTM
SIFS
M-BA
SIFS
Same as REVmc
(<= 10ms recommended)
SIFS
Ack