## Slide 1: Uplink Training for Downlink Multi-User MIMO
Date: 2016-09-12
Authors:

## Slide 2: Introduction
Training with Tx/Rx beam sectorization is the current training method for DL MU-MIMO in 802.11ay
This method is transparent to any uplink-downlink channel differences
Problems: time consuming (as much training as number of sectors), beam accuracy can be low (more accuracy -> more training overhead)
This method is presented as Myth #3 in [1]: it does not exploit the full potential of Massive MIMO systems

## Slide 3: Introduction
Alternative approach: perform uplink training
Pros: Less training overhead, superior beam accuracy, not sensitive to LOS assumption
Cons: UL/DL channel reciprocity not guaranteed -> possibly requires calibration

## Slide 4: Calibration for Channel Reciprocity
AP has Tx and Rx chain gain imbalances and (diagonal matrices)
AP calibration estimates
AP calibration is well-known and well-studied, and it works [2]
Calibration of STAs not necessary for DL transmission

## Slide 5: Uplink Training Procedure
Assuming calibration has been performed
AP transmits an uplink training trigger frame to a specific group of STAs
Each STA in the group transmits a training packet
AP estimates (jointly) the received channel (or any transformation of the channel)
AP uses the estimated channel for downlink transmission

## Slide 6: Uplink Training Procedure
AP
STA 1
STA 2
Trigger
Frame
Training
Packet
Training
Packet
Beamformed
Data
Estimate CSI
These packets are short!

## Slide 7: Massive MIMO Deployment (2.3 GHz)
0.5 m between UEs, 40-50 m between BS and UE, 8 m linear array

## Slide 8: Performance
TDD significantly better than hybrid beamforming and FDD

## Slide 9: Summary
Proposed an uplink training procedure for beamforming construction
Pros: Significantly less training overhead, enables superior beamforming
Cons: Possibly calibration assumptions (although verified in practice to work)

## Slide 10: References
[1] E. Björnsson, E. G. Larsson, T. Marzetta, ”Massive MIMO: Ten Myths and One Critical Question”, IEEE Comm. Mag., Feb. 2016
[2] J. Vieira et. al., ” Reciprocity Calibration for Massive MIMO: Proposal, Modeling and Validation”, IEEE Trans. Wire. Comm., 2016

## Slide 11: Straw Poll
Do you believe the uplink training mechanism presented here is worth considering for further study?
Y/N/A:

## Slide 12: Mathematical Derivation
Let be the (physical) uplink channel between STA and the AP – this channel is reciprocal
Let be the transmit antenna imbalance at STA
Define
AP receives , where is the pilot matrix
After CSI estimation, AP obtains an estimate of

## Slide 13: Mathematical Derivation
The downlink signal vector is
is the precoder
can be removed due to calibration
Since AP has an estimate of , the precoder can be tailor-suited to
What remains is the diagonal matrix which has no impact on receiver performance
Hence, no calibration is necessary at the STAs