## Slide 1: MU MIMO beamforming protocol proposal
Date: 2016-11-02
Authors:

## Slide 2: Purpose
This presentation describes a consolidated BF training protocol for use during the DTI period of the beacon interval
Slide 2

## Slide 3: Protocol
Protocol is comprised of the following phases, executed in this order:
  Phase 1: SISO phase (mandatory)
  Phase 2: MIMO phase (mandatory)
Gap in between phases is TBD
  Need to take implementation complexity into account
Whether an EDMG STA is required to support this BF protocol flow, or parts of it, is TBD

## Slide 4: Phase 1

## Slide 5: Phase 1 (SISO phase) overview
Assumption: there exists a control PHY link from the initiator to each of the intended responder
Goals:
  Collect feedback on one or more suitable antenna/sectors between an initiator and each responder
  Setup following MIMO phase
The SISO phase consists of:
  An optional (i.e., may not be present in every instantiation of the flow) I-TXSS using the Short SSW frame, if initiator hasn’t yet discovered all suitable links with responder(s)
    Definition of suitable is implementation dependent
  DMG SISO Setup/DMG SISO Setup Response frame exchanges between initiator and responder(s) to collect feedback and setup phase 2
Control PHY transmission and quasi-omni reception would typically be used during this phase

## Slide 6: Phase 1 (SISO phase) I-TXSS
Define two new fields defined in the Short SSW frame
The Addressing Mode field (1 bit) indicates whether the Addressing field in the Short SSW frame is individual/broadcast or group based
  SU-MIMO BF flow is used in case of individual address
  MU-MIMO BF flow is used in case of broadcast/group address
The Setup Duration field (10 bits) is defined to specify the duration, in microseconds, of the setup subphase which starts after the Short SSW frame with CDOWN=0
  Allows STAs that receive the Short SSW frame to determine the end of phase 1
  Maximum duration (1024usec) sufficient for up to 16 frame exchanges using MCS0
 | Packet Type | Addressing | CDOWN | RF Chain ID | Addressing Mode | Setup Duration | Direction | Reserved | FCS
Bits | 2 | 16 | 11 | 2 | 1 | 10 | 1 | 1 | 4
Short SSW frame format in an ISS
Move

## Slide 7: Phase 1 (SISO phase) addressing
The I-TXSS can span up to 2048 sectors (very long)
EDMG STAs should be able to determine as soon as possible whether or not they are part of BF training
  Allows a STA which is not a part of the MU-MIMO group to, e.g., decide to stay awake or doze
This should be done through the Addressing field
While it can be straightforward to identify a single STA, the question is: how do we identify a group of STAs in the Addressing field?

## Slide 8: Phase 1 (SISO phase) addressing
Addressing Mode field in Short SSW frame indicates whether the Addressing field should be interpreted as an individual/broadcast address or group address
If group address is used, a new EDMG Group ID Set element can be defined to associate a group ID with a group of STAs
  EDMG Group ID Set element can be transmitted in DMG Beacon and Announce frames
  AP responsible to ensure STAs have up to date info on groups
  All existent groups are included into EDMG Group ID Set element
By doing this, an EDMG STA that receives a group addressed Short SSW can determine whether they are part of the BF training
Element ID
Length
Number of EDMG Groups
EDMG Group 1
EDMG Group 2
EDMG Group ID
AID 0
AID 1
AID 7
Bits 8 8 8 5 69 69
Bits 5 8 8 8
Element ID Extension

## Slide 9: Phase 1 (SISO phase) setup exchange
Initiator and responder(s) exchange DMG SISO Setup and DMG SISO Setup Response frames to collect feedback and setup phase 2
  Polled approach is simpler and more robust, while at the same time being able to deal with DMG SISO Setup Response frames of different durations
If I-TXSS was present, the duration of the setup subphase shall not exceed the value of the Setup Duration field indicated in the Short SSW frame
  Enables any recipient STAs to determine the end of phase 1
The Duration field of each DMG SISO Setup/DMG SISO Setup Response frame shall point to the end of phase 1
A Channel Measurement Feedback element, or a modified version of it, is included in the DMG SISO Setup Response frame and includes list of received I-TXSS sectors/antennas and their corresponding SNR/RSSI per RX antenna (other fields TBD)
The AP may provide early notice on start of phase 1 for STAs in power save (either scheduled or unscheduled)

## Slide 10: Phase 2

## Slide 11: MIMO Phase
Design goal is to have a MU-MIMO scalable to many spatial streams (e.g., 16) and many users (8 to 16)
Proposed protocol flow comprises of 4 subphases

## Slide 12: MIMO Phase: steps
Initiator selects TX sectors for each antenna based on sector feedbacks from all responders in Phase 1, and other information
Initiator sends MU-MIMO BF Setup frame(s) to all responders to inform selected TX sectors for each antenna and order of antenna/sector sweep in MU-MIMO BF Training
  Initiator transmits this setup information in minimum set of frames in different antennas/sectors (sufficient to reach all responders)
  In option 2, MU-MIMO BF Setup is followed by poll and ack
Initiator transmits MU-MIMO BF training, which are BRP frames with RX training fields appended (described later)
Initiator polls MU-MIMO FBs (indicates FB formats and fields) and responder responds with MU-MIMO feedbacks
Initiator optionally polls some responders to perform responder sweep in fixed slots, in fixed channels. Polled responders sweep its TX sectors with FBs.
  This step is optional and not part of mandatory flow
Initiator transmit MU-MIMO selection for sets of MU transmission configuration to all responders in minimum set of frames (sufficient to reach all intended responders)
  In option 2, ack from responders is included

## Slide 13: MU-MIMO BF Setup frame
Use the same frame as MU-MIMO setup frame (TBD)
Content
  TA: BSSID
  RA: Group ID
  Purpose: MU-MIMO BF setup
  Sequence Number: identify which BF training
  TX-Antennas/Selected Sectors/No. RX TRN fields/Simultaneous TX antennas(Orthogonal Waveforms) training (detailed bit field TBD)
    Number RX TRN fields for each TX sector.
    BRP1: An (No of MUX ants in BRP frame 1), Ant index Xi, sector index S1, S2, …, Sn, Ant index Xj, sector index S1, S2, …, Sm, … ,
    ...
    BRPk: An (No of MUX ants in BRP frame 1), Ant index Xi, sector index S1, S2, …, Sn, Ant index Xj, sector index S1, S2, …, Sm, … ,

## Slide 14: MU-MIMO BF Training (1/2)
Initiator transmits BRP frame with TRN fields that sweep through TX antennas with training fields for selected TX sectors x max RX sectors in full bandwidth [1][2]
  One BRP frame for one TX antenna or multiple TX antennas (with orthogonal waveforms)
  Number RX TRN should be max of RX sectors from all intended STAs
In each training frame (BRP), initiator appends TRN-R training fields for all intended responder to perform RX sector training
  Already allowed in the SFD (section 3.2, para 2), which specifies that a BRP fame allows TX and RX training in the same packet
Propose to increase the limit to 256 TRN fields (rather than 64 used in 11ad)
  This enables testing combinations of TX and RX sectors in the same packet
  AP is aware of the maximum number of training fields each STA can process (capability)

## Slide 15: MU-MIMO BF Training: enhanced BRP packet format (2/2)
A control PHY packet with training fields (SC version possible)
Non-training parts transmitted through all antennas with small delay between antennas
Can be transmitted over a single channel or over a bonded channel
Training fields transmitted concurrently through all antennas using orthogonal TRN fields
  Orthogonal sequence identifies TX antenna
  Enables training multiple Tx antennas simultaneously using a normal BRP training protocol
Three possible modes:
  TX training: may be used by any EDMG STA who receives the frame
  RX training: several STAs can be trained concurrently
  Combined training: RX training for each TX training
AP configures the BRP frame according to STAs capabilities

## Slide 16: MU-MIMO FB Polling
AP polls each responder STA one by one for feedbacks of the MU-MIMO BF Training.
  Indicates feedback formats (RSSI feedback mandatory, others TBD)
Responder STAs feedback TX-RX sector pair combinations in indicated format when polled.
[Optional, not part of mandatory flow] AP may optionally engage individual R-TXSS by assigning fixed slots (in a fixed sub-channel number) for some STAs to re-establish responder link. AP may also assign fixed slots for contention. Polled responder shall perform R-TXSS in indicated fixed slots to establish responder link. AP can poll again after Responder link is established for MU-MIMO BF FBs.

## Slide 17: MU-MIMO FB Poll frame
Can define a new MU-MIMO Poll frame
Content of the frame
  TA: BSSID
  RA: STA MAC Address
  Purpose: MU-MIMO BF polling
  MU-MIMO BF Sequence Number
  FB format (TBD: RSSI, Time domain channel response, CSI, compressed/uncompressed, etc)
  [Optional, not part of mandatory flow] R-TXSS Indicator, Number of slots, channel number (Skip FB format field if R-TXSS indicator=yes). AP can poll again for MU-MIMO BF FB after responder link is established.

## Slide 18: MU-MIMO FB frame
Can define a new MU-MIMO FB frame
Content
  RA: BSSID
  TA: STA MAC Address
  Purpose: MU-MIMO Feedback
  MU-MIMO Sequence Number
  Feedbacks (all or only received ones) based on the requested format (and STA’s capabilities)
    RSSIs of TX-RX pair ID
    Time domain response of TX-RX pair ID
    CSI of TX-RX pair ID
  If STA and AP both have antenna reciprocity, STA optionally feedbacks responder link TX antenna /sector ID (for AP)
    Responder link feedback indicator
    TX antenna/sector selected (for responder link)

## Slide 19: MU-MIMO Selection
AP can select subset of users for different MU-MIMO transmission configurations based on feedbacks
  Selection is based on STA received signal strength and possible interference level.
  For non-beamformed case, each MIMO transmission configuration contains a subset of STAs (number of STAs in the subset ≤ number of TX antennas), each TX antenna/sector (Spatial stream) is assigned a RX antenna/sector (TX-RX pair) from a STA, and different STAs cannot be assigned the same TX antenna.
  For beamformed case, each MIMO transmission configuration contains a subset of STAs (number of STAs in the subset ≤ number of spatial stream), each spatial stream is assigned a RX antenna/sector from a STA

## Slide 20: MU-MIMO Selection frame
Can define a new MU-MIMO Selection frame
Content
  RA: Group ID
  TA: BSSID
  Purpose: MU-MIMO selection
  N: number of MU-MIMO Transmission Configurations
    MU-MIMO Config_ID 1: (BF1, TX Ant_Sec_ID1/SS_ID1, STA_ID1, RX Ant_Sec_ID1); (BF2, TX Ant_Sec_ID2/SS_ID2, STA_ID2, RX Ant_Sec_ID2), …
    MU-MIMO Config_ID 2: (BF1, TX Ant_Sec_ID1/SS_ID1, STA_ID1, RX Ant_Sec_ID1); (BF2, TX Ant_Sec_ID2/SS_ID2, STA_ID2, RX Ant_Sec_ID2), …,
    …
    MU-MIMO Config._N: (BF1, TX Ant_Sec_ID1/SS_ID1, STA_ID1, RX Ant_Sec_ID1); (BF2, TX Ant_Sec_ID2/SS_ID2, STA_ID2, RX Ant_Sec_ID2),…
    (Note: BFi bit indicates TX Ant_Sec_IDi (non-beamed) or SS_IDi (beamformed).
  AP transmits this setup information in minimum set of frames in different antennas/sectors (sufficient to reach all intended STAs).

## Slide 21: Summary
Proposed a MU MIMO beamforming protocol framework
Protocol is scalable to large number of users and streams

## Slide 22: References
IEEE 802.11-16/0405r1, 11ay DL MU-MIMO BF Training and User Selection, Mediatek

## Slide 23: Straw poll
Do you agree with inserting the following in section 3.4 of the SFD:
  “The 11ay MU MIMO beamforming protocol shall comprise the following phases:
  SISO phase
  MIMO phase
  The SISO phase is as specified in <slides 5-9>. The MIMO phase is as specified in <slides 11-20>.”