## Slide 1: MCS table for SC EDMG
Date: 2016-November-07
Authors:
Name | Company | Address | Phone | Email
Alecsander Eitan | Qualcomm |  |  | eitana@qti.qualcomm.com
Amichai Sanderovich | Qualcomm |  |  | amichais@qti.qualcomm.com

## Slide 2: Motivation
The current 802.11REVmc contains the MCS table for SC-DMG modem.
This table is divided into two tables, normal and extended mode.
This involves complex header signaling, reserve bits usage and limitation on the available length.

## Slide 3: Proposed MCS table
We suggest the following MCS table for SC.
MCS index | Modulation | NCBPS | Repetition | Code Rate | Data Rate (Mbps) CB=1 | Data Rate (Mbps) CB=2 | Data Rate (Mbps) CB=3 | Data Rate (Mbps) CB=4
1 | π/2-BPSK | 1 | 2 | 1/2 | 385 | 770 | 1155 | 1540
2 | π/2-BPSK | 1 | 1 | 1/2 | 770 | 1540 | 2310 | 3080
3 | π/2-BPSK | 1 | 1 | 5/8 | 962.5 | 1925 | 2887.5 | 3850
4 | π/2-BPSK | 1 | 1 | 3/4 | 1155 | 2310 | 3465 | 4620
5 | π/2-BPSK | 1 | 1 | 13/16 | 1251.25 | 2502.5 | 3753.75 | 5005
6 | π/2-BPSK | 1 | 1 | 7/8 | 1347.5 | 2695 | 4042.5 | 5390
7 | π/2-QPSK | 2 | 1 | 1/2 | 1540 | 3080 | 4620 | 6160
8 | π/2-QPSK | 2 | 1 | 5/8 | 1925 | 3850 | 5775 | 7700
9 | π/2-QPSK | 2 | 1 | 3/4 | 2310 | 4620 | 6930 | 9240
10 | π/2-QPSK | 2 | 1 | 13/16 | 2502.5 | 5005 | 7507.5 | 10010
11 | π/2-QPSK | 2 | 1 | 7/8 | 2695 | 5390 | 8085 | 10780
12 | π/2-16QAM | 4 | 1 | 1/2 | 3080 | 6160 | 9240 | 12320
13 | π/2-16QAM | 4 | 1 | 5/8 | 3850 | 7700 | 11550 | 15400
14 | π/2-16QAM | 4 | 1 | 3/4 | 4620 | 9240 | 13860 | 18480
15 | π/2-16QAM | 4 | 1 | 13/16 | 5005 | 10010 | 15015 | 20020
16 | π/2-16QAM | 4 | 1 | 7/8 | 5390 | 10780 | 16170 | 21560
17 | π/2-64QAM | 6 | 1 | 5/8 | 5775 | 11550 | 17325 | 23100
18 | π/2-64QAM | 6 | 1 | 3/4 | 6930 | 13860 | 20790 | 27720
19 | π/2-64QAM | 6 | 1 | 13/16 | 7507.5 | 15015 | 22522.5 | 30030
20 | π/2-64QAM | 6 | 1 | 7/8 | 8085 | 16170 | 24255 | 32340
Data Rate values are for Normal GI single stream. Other cases are scaled values.

## Slide 4: Performance of the proposed MCS table
(CR 7/8 not included)

## Slide 5: Proposed MCS table
Achieved rates

## Slide 6: Straw Poll
Do you agree to include in the SFD the MCS table for SC, as follows:
MCS index | Modulation | NCBPS | Repetition | Code Rate | Data Rate (Mbps) CB=1 | Data Rate (Mbps) CB=2 | Data Rate (Mbps) CB=3 | Data Rate (Mbps) CB=4
1 | π/2-BPSK | 1 | 2 | 1/2 | 385 | 770 | 1155 | 1540
2 | π/2-BPSK | 1 | 1 | 1/2 | 770 | 1540 | 2310 | 3080
3 | π/2-BPSK | 1 | 1 | 5/8 | 962.5 | 1925 | 2887.5 | 3850
4 | π/2-BPSK | 1 | 1 | 3/4 | 1155 | 2310 | 3465 | 4620
5 | π/2-BPSK | 1 | 1 | 13/16 | 1251.25 | 2502.5 | 3753.75 | 5005
6 | π/2-BPSK | 1 | 1 | 7/8 | 1347.5 | 2695 | 4042.5 | 5390
7 | π/2-QPSK | 2 | 1 | 1/2 | 1540 | 3080 | 4620 | 6160
8 | π/2-QPSK | 2 | 1 | 5/8 | 1925 | 3850 | 5775 | 7700
9 | π/2-QPSK | 2 | 1 | 3/4 | 2310 | 4620 | 6930 | 9240
10 | π/2-QPSK | 2 | 1 | 13/16 | 2502.5 | 5005 | 7507.5 | 10010
11 | π/2-QPSK | 2 | 1 | 7/8 | 2695 | 5390 | 8085 | 10780
12 | π/2-16QAM | 4 | 1 | 1/2 | 3080 | 6160 | 9240 | 12320
13 | π/2-16QAM | 4 | 1 | 5/8 | 3850 | 7700 | 11550 | 15400
14 | π/2-16QAM | 4 | 1 | 3/4 | 4620 | 9240 | 13860 | 18480
15 | π/2-16QAM | 4 | 1 | 13/16 | 5005 | 10010 | 15015 | 20020
16 | π/2-16QAM | 4 | 1 | 7/8 | 5390 | 10780 | 16170 | 21560
17 | π/2-64QAM | 6 | 1 | 5/8 | 5775 | 11550 | 17325 | 23100
18 | π/2-64QAM | 6 | 1 | 3/4 | 6930 | 13860 | 20790 | 27720
19 | π/2-64QAM | 6 | 1 | 13/16 | 7507.5 | 15015 | 22522.5 | 30030
20 | π/2-64QAM | 6 | 1 | 7/8 | 8085 | 16170 | 24255 | 32340