## Slide 1: MCS, NSS, BW and PPDU selection for 11ax
Date: 2016-11-05
Authors:

## Slide 2: Introduction
In this presentation we propose clarifying the selection rules for PPDU type, BW, and <MCS, NSS> for 11ax
  The topic is related, but not limited, to CR of CID 203
And more in general we propose to finalize all the normative behavior for the selection of these parameters for control response frames
  The proposal being to inherit rules from 11ac unless explicitly stated otherwise
CID | Commenter | P.L | Comment | Proposed Change | Resolution
203 | Alfred Asterjadhi | 63.24 | MCS selection rules for sending M-BA by a STA is not defined | As in comment. | Revised. Agree in principle. Proposed changes in this document account for comment resolution

## Slide 3: PPDU selection for control frames
Rules are conceptually inline with baseline, while accounting for 11ax concepts:
  AP may chose any format for sending control frames as a response to trigger-based PPDUs
An HE STA shall send control frames in a non-HT PPDU except when:
  The frame is a response to an ER SU, SU, or UL MU PPDU that uses STBC in which case:
    The control frame shall use the same PPDU format as the soliciting PPDU (as baseline)
  The frame is an Ack, BA, or M-BA sent as a response to a Trigger-based PPDU in which case:
    The control frame may be carried in any PPDU format that is supported by the intended receiver(s) (11ax motion)
  The Control frame is sent as a response to a PPDU containing a Trigger (non-MU RTS) or an UL MU Response Scheduling A-Control field in which case it shall be carried in HE Trigger-based PPDU format
  The Control frame is an Ack sent in response to ER SU, SU, or UL MU PPDU containing FTM
    In which case the Ack frame shall be sent in the same PPDU format as the soliciting PPDU
  Other exceptions for situations with reverse link imbalance are discussed in the next slides
(A-)MPDU
Ack/BA
SIFS
CTS
RTS
HE PPDU
SIFS
SIFS
TXOP
RTS
CTS
Ack/BA
Non-HT

## Slide 4: ER SU and reverse link imbalances (1)
ER SU PPDUs cover extended range and link imbalance use cases
  Both transmission and reception of ER SU PPDUs is optional
    There is a capability bit but normative behavior is yet to be specified in TGax D0.5
  Format of control response frames sent in response to ER SU PPDUs is undefined
    We propose that RX STA choses (and indicate to TX STA) which PPDU format to use
Benefits from
  ER SU PPDU selection when TX power is insufficient to close the reverse link,
  Non-HT PPDU selection (when TX power is sufficient to close the reverse link.
Probe Request
Probe Response
Ack
ER SU
ER SU
ER SU
Data
Ack
ER SU
SU
AP signals
switch to non-HT
Data
Ack
ER SU
Non-HT
Non-AP
AP
…
Data
Ack
ER SU
ER SU
Good: Closes the link
Bad: legacy EIFS issues
EIFS
Closes the link
No EIFS issues

## Slide 5: ER SU and reverse link imbalances (2)
Proposed rules for ER SU PPDU generation and reception:
  An HE STA may transmit an ER SU PPDU to a peer STA that supports its reception as indicated by the ER SU PPDU Payload field of the HE Capabilities element received from the peer STA. An HE STA shall not send an ER SU PPDU to a STA that does not support their reception.
  The responding STA shall send the control response using the eliciting PPDU format except when the responding HE STA has explicitly indicated an alternative PPDU format that it will be using to send the response (see next slide)
Probe Request
Probe Response
Ack
ER SU
ER SU
ER SU
Data
Ack
ER SU
SU
AP signals Control Resp.
PPDU format
to non-HT
Data
Ack
ER SU
Non-HT
Non-AP
AP
…
Data
Ack
ER SU
ER SU
Good: Closes the link
Bad: legacy EIFS issues
EIFS
Closes the link
No EIFS issues
ER SU
Data
Ack
Non-HT
Closes the link
No EIFS issues
Non-AP
AP
UL limited case
DL limited case
STA signals Control Resp.
PPDU format
to non-HT

## Slide 6: Explicit PPDU Type switching
The responding STA can explicitly indicate the PPDU type for Control Response frames by:
  Based on the most recent individually addressed PPDU sent to the transmitting STA
Switch takes effect similar to that of TOMI parameters
  E.g., after the end of the current TXOP
Transmitting STA accounts for expected response type when calculating Duration/ID and TXOP_DURATION field values.
  PPDU format for control response stays in effect until a new value is indicated

## Slide 7: BW selection for control frames
Rules below are conceptually inline with 11ac behavior and
  Could apply to both 2.4GHz & 5Ghz, though WFA does not allow >20MHz op. in 2.4GHz
Proposed rules for an HE STA:
  BW of control responses within a TXOP shall be same as the soliciting PPDU, except for:
    A CTS frame sent in response to RTS with Dynamic_BW or MU RTS in which case BW may be smaller
  Frames sent by TXOP holder may have smaller BW than previously TXed frames of that TXOP
    Note: This rule also applies to control responses sent by an AP as a response to a Trigger-based PPDU
  Bandwidth-signaling TA usage:
    An HE STA shall use BW-signaling TA for Control frames sent in >20MHz non-HT PPDUs
    An HE STA may use BW-signaling TA for Control frames sent in 20 MHz non-HT PPDUs
    An HE STA shall not use BW-signaling TA for other PPDU formats
  An HE STA should not transmit >20Mhz PPDUs in 2.4GHz
(A-)MPDU
Ack/BA
SIFS
CTS
RTS
PPDU
SIFS
SIFS
TXOP
RTS
40 MHz
20 MHz
(ED busy)
PIFS

## Slide 8: MCS, NSS selection for control frames
An HE STA shall follow the baseline <MCS, NSS> selection rules* except that:
  For Trigger-based PPDU it shall be determined by the soliciting Trigger or UL MU Response A-Control field
  For control frame sent in response to a Trigger-based PPDU it shall be a tuple supported by the intended RX(s)
  For a control frame sent in response to an ER SU PPDU it shall be equal to <MCS0, 1>
An HE STA that sends a control frame in an ER SU PPDU format shall use:
  DCM encoding if the most recent successfully received PPDU sent by the HE STA to the soliciting STA after association used DCM; otherwise the STA shall not use DCM for the control frame.
  106-tone ER SU PPDU if the most recent successfully received PPDU sent by the HE STA to the soliciting STA after association was a 106-tone ER SU PPDU.
*Accounting for the addition of the <HE-MCS, NSS> in the <MCS, NSS> selection set
(A-)MPDU
Ack/BA
SIFS
CTS
RTS
PPDU
SIFS
SIFS
RTS
CTS
Ack/BA
40 MHz