## Slide 1: TWT Information frames in 11ax
Date: 2016-11-05
Authors:

## Slide 2: Introduction
TWT modes defined in the latest TGax D0.5:
  Solicited TWT mode (individual TWT agreements):
    Non-AP STA and AP negotiate implicit TWT session(s)
    Non-AP STA follows the TWT schedule(s) of established TWT session(s)
      Renegotiations, terminations are performed via unicast MGMT frames; no need to read the Beacon
  Broadcast TWT mode:
    AP includes a broadcast TWT IE in the Beacon frame specifying one or more TWT sets
    Non-AP STAs that read the Beacon frame follow the provided broadcast TWT schedule(s)
Both modes inherit/use implicit TWT signaling provided by TWT IE, and:
  Trigger field in TWT IE indicates that Trigger frames are sent within each TWT SP
We propose to finalize the use of TWT Information frames in 11ax
  These rules are intended as resolution for CID 140
140 | Alfred Asterjadhi | 67.30 | The use of TWT Information frames for Implicit TWT is not complete. Clarify the use of these frames, especially their use to suspend/resume implicit TWT operation. | As in comment. | Revised – Agree in principle with the comment. Proposed resolution accounts for most of the suggested changes. TGax editor to make the changes shown in 11-16/1420r0 under all headings that include CID 140.

## Slide 3: Background: TWT Information frame
Currently the only normative behavior that is defined is:
  “A TWT requesting STA operating with an implicit TWT agreement with a TWT flow identifier that matches the TWT flow identifier of a received TWT Information frame from its TWT responding STA shall replace its next TWT SP start time value with the value from the Next TWT subfield of the TWT Information frame.“
Observations:
  It does not specify the settings of other fields in the TWT Information frame and expected behavior upon RX
    How are the fields set in transmission, and can the TWT requesting STA send the frame?
  It does not cover the case of Broadcast TWT
    i.e., can a TWT scheduling STA or a TWT scheduled STA send these frames?
    And when these frames are sent, what is the expected behavior?

## Slide 4: Rules for TWT Information frame
A STA may transmit TWT Information to its peer STA that contains:
  Response Requested subfield equal to 0
  A nonzero next TWT is contained when the frame is transmitted by TWT responding/scheduling STA,
  A next TWT subfield that is not present when the frame is transmitted by TWT requesting/scheduled STA and it
    Indicates a suspension of the TWT session the STA is following
  A next TWT subfield that is present when the frame is transmitted by the TWT requesting/scheduled STA and it
    Indicates resumption/skip of a previously suspended TWT
Advantages of specifying rules:
  Clarifies when TWT Information frames can be sent during TWT sessions
    Limiting the field settings only to a subset of options for simplifying the procedure.
  Specifies the frame’s subfield settings for this mode
    Specifies which settings of these fields enable a TWT suspension/resumption

## Slide 5: Examples: In individual TWT operation
Example 1 (as in baseline: AP indicates skip of some TWTs)
  TWT responding STA sends TWT Information frame to re-schedule the next TWT
    Next TWT indicates at which TWT the TWT session starts again.
Example 2 (STA indicates suspend, resume/skip of TWT)
  TWT requesting STA sends a TWT Information frame to suspend the TWT
    The TWT Information frame does not contain a Next TWT field.
  TWT responding STA assumes the TWT session suspended until TWT resumption is received
  TWT requesting STA sends a TWT Information frame to resume/skip the next TWT
    The TWT Information frame does contain the next TWT at which the resumption/skipping starts
    The next TWT is same as the one the TWT responding STA had advertised (simplifies schedule tracking)
TWT requesting STA
TWT responding STA
TWT
Setup
TWT Wake
Interval
TWT SP
TWT Information/Ack
Next TWT (skip)
(1)
TWT
Setup
TWT Wake
Interval
TWT SP
TWT Information/Ack
(2)
No Next TWT (suspension)
TWT Information/Ack
Next TWT (skip/resumption)
TWT requesting STA
TWT responding STA

## Slide 6: Examples: In broadcast TWT operation
Example 1 (as in baseline: AP indicates skip of some TWTs)
  TWT scheduling STA sends TWT Information to indicate which of the next TWTs
    Next TWT indicates at which TWT the TWT session starts again.
Example 2 (STA indicates suspend, resume, skip of TWT)
  TWT scheduled STA can send a TWT Information frame to suspend the broadcast TWT
    The TWT Information frame does not contain a Next TWT field.
    The TWT scheduling STA assumes that the STA suspended participating in broadcast TWT
  TWT scheduled STA sends a TWT Information to resume/indicate the next broadcast TWT
    The TWT information frame contain the next TWT (at which the resumption/or skipping starts)
    Next TWT is the same as the ones the TWT scheduling STA had advertised in the Beacon (simplifies schedule tracking)
TWT scheduled STA
TWT scheduling STA
TWT Wake
Interval
TWT SP
TWT Information/Ack
Next TWT (skip)
(1)
TWT Wake
Interval
TWT SP
TWT Information/Ack
(2)
Beacon
Beacon
No Next TWT (suspension)
TWT Information/Ack
Next TWT (skip/resumption)
TWT scheduled STA
TWT scheduling STA

## Slide 7: Flexible TWT (re)scheduling
Previous examples showed STAs changing the TWT schedule to fixed (i.e., pre-allocated) TWT slots.
  Keeps management of schedules simple at the AP
  Limits number of actions can be taken by these STAs
    Selection is performed from a pre-allocated set of TWTs
A STA could request change in TWT schedule (i.e., resume/skip) from an arbitrary time in the future
  This gives more flexibility – rather than being tied to a fixed schedule
  However, would require AP to have sufficient resources to keep track of all requests that it receives from various STAs
A STA can declare such capability (e.g., with a Flexible TWT Scheduler bit in the HE Capabilities)
  If the STA declared such capability then the peer STA(s) can send to the STA a TWT Information frame with Next TWT fields that contains a nonzero value

## Slide 8: Proposed text for resolving CID 140 (1)
TGax Editor: Insert the following subclause to D0.5 (CID #140):
25.7.4 Use of TWT Information frames(#140)
An HE STA may transmit a TWT Information frame to its peer STA during an individual TWT session, broadcast TWT session, or at any time if the peer STA has set the Flexible TWT Schedule Support of the HE Capabilities it transmits to 1.
The TWT Information frame shall have the Response Requested subfield equal to 0, the Next TWT Request subfield equal to 0, and one of the following:
A nonzero value in the Next TWT subfield when the frame is transmitted by a TWT responding STA, a TWT scheduling STA, or by any HE STA to a peer STA that supports TWT
  The value of the Next TWT shall be selected from existing TWT values for a TWT session if the Flexible TWT Schedule Support field of the peer STA is 0
  The Next TWT may contain any nonzero value if Flexible TWT Schedule Support field of the peer STA is 1
A Next TWT subfield that is present when the frame is transmitted by a TWT requesting STA, a TWT scheduled STA, or any HE STA to a peer STA that supports TWT
  The Next TWT indicates the TWT at which the TWT session is resumed and shall be selected from existing TWT values for that TWT session if the Flexible TWT Schedule Support field of the peer STA is 0
  The Next TWT may contain any nonzero value if Flexible TWT Schedule Support field of the peer STA is 1
  Note: In such case, the TWT requesting STA or TWT scheduled STA or peer STA that transmitted the TWT Information frame preserves the PM mode from the time it sent the TWT Information frame to the time it is expected to wake-up.
A Next TWT subfield that is not present when the frame is transmitted by a TWT requesting STA or a TWT scheduled STA to indicate suspension of the TWT session

## Slide 9: Proposed text for resolving CID 140 (2)
TGax Editor: Add the following text to the newly added subclause (CID #140):
A TWT requesting STA that receives a TWT Information frame follows the rules defined in 10.45.4 (Implicit TWT operation). A TWT requesting STA that receives an acknowledgment in response to a TWT Information frame that:
Does not contain a Next TWT field shall consider that TWT session suspended, and can follow the procedure in 25.7.3 (Broadcast TWT operation) until the TWT session is resumed.
Contains a Next TWT field shall consider the corresponding TWT session resumed, starting from the value indicated in the Next TWT field of the transmitted TWT Information frame.
A TWT scheduling STA that receives a TWT Information frame follows the rules defined in 25.3.2 (Rules for TWT scheduled STA), except that it shall use the Next TWT value contained in the received TWT Information frame. A TWT scheduling STA that receives an acknowledgment in response to a TWT Information frame that:
Does not contain a Next TWT field shall consider the TWT session suspended, and can follow the default PS procedure defined in 11.2 (Power management) until the TWT session is resumed.
Contains a Next TWT field shall consider the corresponding TWT session resumed, starting from the value indicated in the Next TWT field of the transmitted TWT Information frame.
An HE non-AP STA that transmits a TWT Information frame to a peer STA may go to doze state after receiving the acknowledgment and shall be in the awake state at the specified TWT indicated in the TWT Information frame. An HE non-AP STA that receives a TWT Information frame from a peer STA may go to doze state after transmitting the acknowledgment and shall be in the awake state at the specified TWT indicated in the TWT Information frame.
NOTE—The TWT Flow Identifier, together with the MAC addresses of the TWT requesting STA and TWT Responding STA identifies the TWT agreement for which the TWT Information frame is sent (see 10.43.1 (TWT overview)). The receiving STA that has not set up a TWT agreement with that TWT Flow Identifier with the transmitting STA interprets the TWT Information frame as part of a broadcast TWT session or as part of no TWT session.

## Slide 10: Proposed text for resolving CID 140 (3)
TGax Editor: Add a new subfield to the HE Capabilities information element “Flexible TWT Schedule Support”
TGax Editor: Add a new row to Table 9-262z as shown (ignore header row):
Subfield | Definition | Encoding
Flexible TWT Schedule Support | Indicates support for the reception of TWT Information frames with any nonzero value in the Next TWT field. | Set to 1 if the STA supports reception of a TWT Information frame with any nonzero value in the Next TWT field. Set to 0 otherwise.

## Slide 11: SP 1
Do you support the comment resolution text provided in the previous 3 slides for resolving CID 140?