## Slide 1: L-Header spoofing and bit reuse
Date: 2016-11-8
Authors:

## Slide 2: Background
Field name | Num. of bits | Start bit
Scrambler Initialization | 7 | 0
MCS | 5 | 7
Length | 18 | 12
Additional PPDU | 1 | 30
Packet Type | 1 | 31
Training Length | 5 | 32
Aggregation | 1 | 37
Beam Tracking Request | 1 | 38
Last RSSI | 4 | 39
Turnaround | 1 | 43
Reserved | 4 | 44
HCS | 16 | 48
4 reserved bits in L-Header are running out while more free bits in L-Header are desired for EDMG.
  2 bits in use
  1+ bit should be kept for future use
In this presentation we consider reuse of the Length field in L-Header for EDMG.
Extended SC MCS Indication | 1 | 44
Reserved | 1 | 45
EDMG (EDMG-Header-A) Indication | 1 | 46
Reserved | 1 | 47

## Slide 3: Spoofing overview
In an EDMG PPDU, actual MCS and length are included in the EDMG-Header-A/B [1].
The L-Header includes spoof MCS and length so that legacy STAs can compute the TXTIME of the EDMG PPDU.
L-STF
L-Header
EDMG-Header-A
L-CEF
Data
E-CEF
E-STF
TXTIME – calculated by spoof MCS and Length
spoof MCS, Length
EDMG PPDU
TXTIME
L-STF
L-Header
L-CEF
actual MCS, Length
DMG payload
Legacy STA sees:
[1] 11-16/1358r6 Specification Framework for TGay

## Slide 4: maximum TXTIME for EDMG
The maximum duration of a DMG PPDU (aPPDUMaxTime) is 2ms.
We suggest to specify that the maximum duration of an EDMG PPDU is 2 ms, as same as DMG.
  Significant efficiency improvement may not be expected with a longer PPDU.
    Overhead for preamble and BA could be less than 1% (20us) for 2ms PPDU.
  Potential risks of compatibility with 11ad are reduced.
  We haven’t seen any problems which encourage to reduce the maximum duration.

## Slide 5: How does legacy STA calculate TXTIME?
Example: DMG SCPHY MCS6 (see appendix for the details)
Data octets per
LDPC codeword
Data bits per
Symbol block

## Slide 6: How does legacy STA calculate TXTIME? (cont’d)
Since 11ad SC-PHY employs LDPC coding, and the packet consists of SC-FDE blocks, there are multiple length values which have the same TXTIME.
Symbol Block 512 sym
Data
448sym
GI
64sym
padding bits, padding symbols
Preamble/Header
Preamble/Header
MCS 6
Length=127
Length=168
the same TXTIME

## Slide 7: How does legacy STA calculate TXTIME? (cont’d)
In case of MCS6 for example, there are at least 42 length values which have the same TXTIME.
  Length = 42n+1 ~ 42n+42 have the same TXTIME
This means the lower bits of the Length field in L-Header are not important for TXTIME calculation.

## Slide 8: Reuse of Length field in L-Header
We suggest to reuse LSBs of the Length field in the L-Header for EDMG purpose.
  Bandwidth preview will be proposed[2]
L-STF
L-Header
EDMG-Header-A
L-CEF
Data
E-CEF
E-STF
spoof MCS, Length
EDMG PPDU
TXTIME
actual MCS, Length
MSBs:
used for TXTIME indication
(spoofing)
LSBs:
reused for EDMG purpose
[2]11-16/1395r0 EDMG Header-A Fields preview in L-Header

## Slide 9: How many bits can be reused?
The number of reusable bits depends on the spoof MCS in the L-Header. (see appendix for the details)
5 bits will be available if we use MCS 2 or above for spoof MCS.
MCS in L-Header | Reusable bits
1 | 4
2 | 5
3 | 5
4 | 5
5 | 6
6 | 5
MCS in L-Header | Reusable bits
7 | 5
8 | 5
9 | 6
10 | 6
11 | 6
12 | 6

## Slide 10: Consideration for spoof MCS
By using MCS 2 or 3, spoofing is properly performed for up to 2ms PPDUs.
We suggest to rule out use of MCS1 for spoofing, while use MCS2 or above.
5.46
TXTIME of DMG PPDUs when Length=262143 (max. in 11ad)

## Slide 11: Summary of Length bits reuse
We suggest to use 5 LSBs of Length field in L-Header for EDMG purpose.
L-STF
L-Header
EDMG-Header-A
L-CEF
Data
E-CEF
E-STF
spoof MCS, Length
EDMG PPDU
TXTIME : no grater than 2ms
actual MCS, Length
13 MSBs:
used for TXTIME indication
(spoofing)
5 LSBs:
reused for EDMG purpose
set to MCS2 or above

## Slide 12: Conclusion
We propose to define the maximum PPDU duration of EDMG PPDU as 2ms.
We show that 5 LSBs of Length field in L-Header can be reused for EDMG purpose.

## Slide 13: References
[1] 11-16/1358r6 Specification Framework for TGay
[2] 11-16/1395r0 EDMG Header-A Fields preview in L-Header

## Slide 14: Straw poll
Do you agree to add the following to the SFD
“The maximum PPDU duration of EDMG PPDU is 2ms."

## Slide 15: Appendix

## Slide 16: TXTIME calculation in DMG SC
TXTIME of DMG PPDU is computed as follows TXTIME[us] = ((2176+1152+64) + (2+NBLKS) * 512)) / 1760 MHz = (NBLKS*512+4416)/1760
NBLKS is calculated as follows
Thus, TXTIME is:
  parameters α (dependent of modulation) and β (dependent of coding rate) are shown in the table.
STF
CEF
GI followed by Header
Header
Payload
Symbols/Block
MCS | α | β
1 | 672/448 = 3/2 | 21
2 | 672/448 = 3/2 | 42
3 | 672/448 = 3/2 | 52.5
4 | 672/448 = 3/2 | 63
5 | 672/448 = 3/2 | 68.25
6 | 672/896 = 3/4 | 42
7 | 672/896 = 3/4 | 52.5
8 | 672/896 = 3/4 | 63
9 | 672/896 = 3/4 | 68.25
10 | 672/1792 = 3/8 | 42
11 | 672/1792 = 3/8 | 52.5
12 | 672/1792 = 3/8 | 63

## Slide 17: The number of reusable bits
There are at least w choices of the length value in L-Header for the given TXTIME.
b LSBs of the Length field in L-Header can be reused, where
MCS | α | β | w | b
1 | 3/2 | 21 | 21 | 4
2 | 3/2 | 42 | 42 | 5
3 | 3/2 | 52.5 | 52 | 5
4 | 3/2 | 63 | 63 | 5
5 | 3/2 | 68.25 | 68 | 6
6 | 3/4 | 42 | 42 | 5
7 | 3/4 | 52.5 | 52 | 5
8 | 3/4 | 63 | 63 | 5
9 | 3/4 | 68.25 | 68 | 6
10 | 3/8 | 42 | 84 | 6
11 | 3/8 | 52.5 | 104 | 6
12 | 3/8 | 63 | 126 | 6

## Slide 18: Example of spoof Length calculation
Without reuse of 5 LSBs
With reuse of 5 LSBs (r : the value in reused 5 bits)
MCS | α | β | w | b
1 | 3/2 | 21 | 21 | 4
2 | 3/2 | 42 | 42 | 5
3 | 3/2 | 52.5 | 52 | 5
4 | 3/2 | 63 | 63 | 5
5 | 3/2 | 68.25 | 68 | 6
6 | 3/4 | 42 | 42 | 5
7 | 3/4 | 52.5 | 52 | 5
8 | 3/4 | 63 | 63 | 5
9 | 3/4 | 68.25 | 68 | 6
10 | 3/8 | 42 | 84 | 6
11 | 3/8 | 52.5 | 104 | 6
12 | 3/8 | 63 | 126 | 6
replace the 5 LSBs of L with r
correction for keeping
the desired TXTIME