## Slide 1: Ack and Block Ack in bonded channels
Date: 2016-11-07
Authors:
Name | Affiliation | Address | Phone | email
Solomon Trainin | Intel |  | 972547885738 | solomon.trainin@intel.com
Oren Kedem | Intel |  |  | Oren.Kedem@intel.com
Carlos Cordeiro | Intel |  |  | carlos.cordeiro@intel.com
Gal Basson | Qualcomm |  |  | bgal@qti.qualcomm.com
Amichai Sanderovich | Qualcomm |  |  | amichais@qti.qualcomm.com

## Slide 2
Purpose and definitions
Purpose of this presentation is to provide Ack and BA rules for bonded channels

## Slide 3
Tx Sequence in multiple channels BW allocation from 2016-TECH-Intel-0031-01-NG60 channel bonding more details r1
Tx Sequence in multiple channels and NAV setup
Duplicated RTS/CTS allows STA C to set up NAV
ACK/BA in duplicated mode allows STA C to set up NAV

## Slide 4
Tx Sequence in multiple channels BW allocation from 2016-TECH-Intel-0031-01-NG60 channel bonding more details r1
ACK and BA wideband vs duplicated
Format | Pros | Cons | Consequences | Comments
Wideband | BA is shorter for MCS 1 and bitmap size of 1024 bits | Duration field is not available for NAV assertion of legacy STA, non multichannel capable STA, and STA that are not open for same BW |  | Duration field can be received by any EDMG STA opened to equal or wider BW with any primary channel
Duplicated | NAV can be set by legacy and non multichannel capable STA Ack is shorter BA is shorter in most cases | MCS1 and 1024 bitmap is not shorter | Support of duplicate Tx mode for mandatory MCS’s | Same as above

## Slide 5
Duplicated mode vs. wide bonded channel link budget
Trade off between using duplicated (D) or wide (W) bonded mode
  In D, only half the power is useful
  In W, receiver integrates twice as much noise
1) and 2) above more or less cancel each other
However, in D a larger BO will be needed due to larger PAPR
Considering all of the above, the duplicated mode leads to a worse link budget

## Slide 6
Wideband vs duplicated, response decision making
Data frame BW=2channels |  |  |  |  | 
 | Data frame MCS | ACK/BA by mandatory MCS |  |  | 
 |  | 1 | 2 | 3 | 4
Mandatory MCS | 1 | W | NA | NA | NA
 | 2 | W | W | NA | NA
 | 3 | W | W | W | NA
 | 4 | D | D | W | W
 | 5 | D | D | D | W
 | 6 | D | D | D | D
 | 7 |  |  |  | 
 | 8 |  |  |  | 
 | 9 |  |  |  | 
Data frame BW=3channels |  |  |  |  | 
 | Data frame MCS | ACK/BA by mandatory MCS |  |  | 
 |  | 1 | 2 | 3 | 4
Mandatory MCS | 1 | W | NA | NA | NA
 | 2 | W | W | NA | NA
 | 3 | W | W | W | NA
 | 4 | D | W | W | W
 | 5 | D | D | W | W
 | 6 | D | D | D | W
 | 7 | D | D | D | D
 | 8 |  |  |  | 
 | 9 |  |  |  | 
Data frame BW=4channels |  |  |  |  | 
 | Data frame MCS | ACK/BA by mandatory MCS |  |  | 
 |  | 1 | 2 | 3 | 4
Mandatory MCS | 1 | W | NA | NA | NA
 | 2 | W | W | NA | NA
 | 3 | W | W | W | NA
 | 4 | W | W | W | W
 | 5 | D | W | W | W
 | 6 | D | D | W | W
 | 7 | D | D | D | W
 | 8 | D | D | D | D
 | 9 |  |  |  | 

## Slide 7: Comparing MCS5 (bonded) vs MCS1 (duplicated)
Summary: when responding in duplicated mode to bonded frame sent by an MCS that is higher or equal to 5, sending the response frame with MCS1 compensates the link budget deficiency.
 | mcs1, duplicate link budget advantage | 
SNR at sensitivity | 5.6 | MCS1 requires a lower SNR
Noise BW | 3 | MCS1 receiver integrates noise only over half the BW
Useful power | -3 | MCS1 – only half of the signal power is used by receiver
BO advantage | -4 | Both are BPSK MCS1 duplicate PAPR is approx. 6 dB larger, but 6 dB larger EVM is allowed, so assume need larger BO of approx. 4 dB
Total | 1.6 | 

## Slide 8: Straw Poll
An ACK or BA frame shall be sent over a bandwidth equal to the bandwidth of the frame the ACK or BA are sent in response to.
An ACK or BA frame sent in duplicated mode in response to a 4.32 GHz, 6.48 GHz, or 8.64 GHz PPDU received with an MCS higher than MCS4 shall be sent with MCS1
An ACK or BA frame transmitted in response to a 4.32 GHz, 6.48 GHz or 8.64 GHz PPDU received with an MCS lower than or equal to MCS4 may be sent in non-duplicated mode with the same bandwidth of the PPDU the frame is sent in response to, and with an MCS that is equal or lower than the MCS of the PPDU that the ACK and BA are sent in response to and that provides the shortest response frame length

## Slide 9: BACKUP

## Slide 10: BA length wideband vs duplicated
MCS1 | Bitmap size (bit) | BA size (byte) | BA length (us) Duplicate Bonded (BW=2) |  | Capacity in BW=2(byte)
 | 64 | 33 | 3.382 | 4.591 | 47
 | 128 | 41 | 3.382 | 4.591 | 
 | 256 | 67 | 4.255 | 4.882 | 99
 | 512 | 89 | 4.838 | 4.882 | 
 | 1024 | 153 | 6.000 | 5.464 | 154
MCS1 | Bitmap size (bit) | BA size (byte) | BA length (us) Duplicate Bonded (BW=3) |  | Capacity in BW=3(byte)
 | 64 | 33 | 3.382 | 4.591 | 73
 | 128 | 41 | 3.382 | 4.591 | 
 | 256 | 67 | 4.255 | 4.591 | 
 | 512 | 89 | 4.838 | 4.882 | 161
 | 1024 | 153 | 6.000 | 4.882 | 

## Slide 11: BA length wideband vs duplicated (cont.)
MCS1 | Bitmap size (bit) | BA size (byte) | BA length (us) Duplicate Bonded (BW=4) |  | Capacity in BW=4(byte)
 | 64 | 33 | 3.382 | 4.591 | 99
 | 128 | 41 | 3.382 | 4.591 | 
 | 256 | 67 | 4.255 | 4.591 | 
 | 512 | 89 | 4.838 | 4.591 | 
 | 1024 | 153 | 6.000 | 4.882 | 203