## Slide 1: Symbol Blocking and Guard Interval Definition for SC MIMO in 11ay
Date: 2016-11-09
Authors:

## Slide 2: Introduction
This presentation proposes symbol blocking and Guard Interval (GI) definition for MIMO SC PHY in 11ay.
It extends the QCOM’s proposal of symbol blocking definition for SISO presented in [1].

## Slide 3: MIMO EDMG PPDU Format
Figure 1 below shows an EDMG PPDU frame format defined in the SFD, [2].
There are two basic cases for MIMO format:
  SU-MIMO: EDMG-Header-B is not present;
  MU-MIMO: EDMG-Header-B is present;
EDMG-Header-B has a constant symbol block and GI time duration as it is defined in [2].
L-STF | L-CEF | L-Header | EDMG-Header-A | EDMG-STF | EDMG-CEF | EDMG-Header-B | Data | AGC | TRN
Figure 1: EDMG PPDU general frame format definition.

## Slide 4: Proposed Guard Interval Types
Guard Interval (GI) types (values are provided for CB = 1):
  Short: N = 32;
  Normal: N = 64;
  Long: N = 128;
GI lengths for different channel bonding factors are provided in Table 1 below.
Note that the GI sequences are defined at the NCB*1.76 GHz rate, where NCB = 1, 2, 3, and 4. The DFT size is kept unchanged equal to 512*NCB.
Table 1: Guard interval lengths for different channel bonding factors.
 | CB = 1 | CB = 2 | CB = 3 | CB = 4
Short | 32 | 64 | 96 | 128
Normal | 64 | 128 | 192 | 256
Long | 128 | 256 | 384 | 512

## Slide 5: Single Channel SU-MIMO
SU-MIMO frame structure:
  EDMG-Header-B is not present and data part starts after the EDMG-CEF field;
  Different streams have different GIiN sequences, i=1:8, N = 32, 64, and 128;

## Slide 6: Single Channel MU-MIMO
MU-MIMO frame structure:
  EDMG-Header-B is present and data part follows after the Header-B;
  Header-B has constant normal GI length of 64 chips regardless the GI data type;
  “Seamless” Header-B to data transition is achieved by using of the “nested” property:
    Right side “nesting”: GIi64 = [X, GIi32];
    Left side “nesting”: GIi128 = [GIi64, X];
  NOTE: different users in MU-MIMO should have the same GI type;

## Slide 7: GI Definition for SISO Single Channel
SISO Golay sequences:
  As proposed in [1], the GI for SISO is defined as follows:
    Short: GI32 = -Ga32, Dk = [2 1 4 8 16], Wk = [+1 +1 -1 -1 +1];
    Normal: GI64 = Ga64, Dk = [2 1 4 8 16 32], Wk = [+1 +1 -1 -1 +1 -1];
    Long: GI128 = -Ga128, Dk = [2 1 4 8 16 32 64], Wk = [+1 +1 -1 -1 +1 +1 +1];
MIMO Golay Sequence Set (GSS):
  The GSS is constructed based on the SISO sequences presented above;
  The delay vector Dk is kept constant over the set and weight vector Wk is changed only;
  Next slide defines the GSS by setting the Wk vectors;
  GI is defined as GIiN = ±GaiN, i = 1:8, N = 32, 64, and 128, proper Ga signs selection guarantees the GI “nested” property considered above;

## Slide 8: GSS for Single Channel
GSS definition:
  Ga32: Dk = [2 1 4 8 16];
  Ga64: Dk = [2 1 4 8 16 32];
  Ga128: Dk = [2 1 4 8 16 32 64];
  Weight vectors Wk are provided in the Table 2 below.
Stream # | Wk vector for Ga32 | Wk vector for Ga64 | Wk vector for Ga128
1 | [+1,+1,-1,-1,+1] | [+1,+1,-1,-1,+1,-1] | [+1,+1,-1,-1,+1,+1,+1]
2 | [-1,+1,-1,-1,+1] | [-1,+1,-1,-1,+1,-1] | [-1,+1,-1,-1,+1,+1,+1]
3 | [-1,-1,-1,-1,-1] | [-1,-1,-1,-1,-1,-1] | [-1,-1,-1,-1,-1,+1,+1]
4 | [+1,-1,-1,-1,-1] | [+1,-1,-1,-1,-1,-1] | [+1,-1,-1,-1,-1,+1,+1]
5 | [-1,-1,-1,-1,+1] | [-1,-1,-1,-1,+1,-1] | [-1,-1,-1,-1,+1,+1,+1]
6 | [+1,-1,-1,-1,+1] | [+1,-1,-1,-1,+1,-1] | [+1,-1,-1,-1,+1,+1,+1]
7 | [-1,-1,-1,+1,-1] | [-1,-1,-1,+1,-1,-1] | [-1,-1,-1,+1,-1,+1,+1]
8 | [+1,-1,-1,+1,-1] | [+1,-1,-1,+1,-1,-1] | [+1,-1,-1,+1,-1,+1,+1]
Table 2: GSS weight vectors definition for different sequence lengths and stream number for CB = 1.

## Slide 9: GI Definition for MIMO Single Channel
Tables 3 below provides a summary of the GI definition for MIMO using Ga sequences for CB = 1.
Stream # | Short GI | Normal GI | Long GI
1 | GI132 = -Ga132 | GI164 = +Ga164 | GI1128 = -Ga1128
2 | GI232 = -Ga232 | GI264 = +Ga264 | GI2128 = -Ga2128
3 | GI332 = -Ga332 | GI364 = +Ga364 | GI3128 = -Ga3128
4 | GI432 = -Ga432 | GI464 = +Ga464 | GI4128 = -Ga4128
5 | GI532 = -Ga532 | GI564 = +Ga564 | GI5128 = -Ga5128
6 | GI632 = -Ga632 | GI664 = +Ga664 | GI6128 = -Ga6128
7 | GI732 = -Ga732 | GI764 = +Ga764 | GI7128 = -Ga7128
8 | GI832 = -Ga832 | GI864 = +Ga864 | GI8128 = -Ga8128
Table 3: GI definition for different types of GI and number of streams for CB = 1.

## Slide 10: Channel Bonding SU-MIMO
SU-MIMO frame structure:
  EDMG-Header-B is not present and data part starts after the EDMG-CEF field;
  Different streams have different GIiN sequences, i=1:8, N = 32*NCB, 64*NCB, 128*NCB, where NCB = 2, 3, and 4;

## Slide 11: Channel Bonding MU-MIMO
MU-MIMO frame structure:
  EDMG-Header-B is present and data part follows after the Header-B;
  Header-B has constant normal GI length of 64*NCB regardless the GI data type;
  “Seamless” Header-B to data transition is achieved by using of the Header-B GI definition as follows:
    Short data GI: GIBi = GIi64*NCB – normal GI length;
    Normal data GI: GIBi = GIi64*NCB – normal GI length;
    Long data GI: GIBi = GIi128*NCB(1:64*NCB) – normal GI length, just first half of long GI;

## Slide 12: GSS for Channel Bonding x2, x4
  GSS definition - weight vectors Wk are provided in the Table 4 below.
  Ga64: Dk = [1 8 2 4 16 32];
  Ga128: Dk = [1 8 2 4 16 32 64];
  Ga256: Dk = [1 8 2 4 16 32 64 128];
  Ga512: Dk = [1 8 2 4 16 32 64 128 256];
  Ga128, Ga256, Ga512 – are used for EDMG-STF/CEF and already defined in SFD, [2];
Table 4: GSS weight vectors definition for different sequence lengths and stream number for CB = 2, 4.
Stream # | Wk vector for Ga64 | Wk vector for Ga128 | Wk vector for Ga256 | Wk vector for Ga512
1 | [-1,-1,-1,-1,+1,-1] | [-1,-1,-1,-1,+1,-1,-1] | [-1,-1,-1,-1,+1,-1,-1,+1] | [-1,-1,-1,-1,+1,-1,-1,+1,+1]
2 | [+1,-1,-1,-1,+1,-1] | [+1,-1,-1,-1,+1,-1,-1] | [+1,-1,-1,-1,+1,-1,-1,+1] | [+1,-1,-1,-1,+1,-1,-1,+1,+1]
3 | [-1,-1,-1,+1,-1,-1] | [-1,-1,-1,+1,-1,-1,+1] | [-1,-1,-1,+1,-1,-1,+1,-1] | [-1,-1,-1,+1,-1,-1,+1,-1,+1]
4 | [+1,-1,-1,+1,-1,-1] | [+1,-1,-1,+1,-1,-1,+1] | [+1,-1,-1,+1,-1,-1,+1,-1] | [+1,-1,-1,+1,-1,-1,+1,-1,+1]
5 | [-1,-1,-1,+1,-1,+1] | [-1,-1,-1,+1,-1,+1,+1] | [-1,-1,-1,+1,-1,+1,+1,-1] | [-1,-1,-1,+1,-1,+1,+1,-1,+1]
6 | [+1,-1,-1,+1,-1,+1] | [+1,-1,-1,+1,-1,+1,+1] | [+1,-1,-1,+1,-1,+1,+1,-1] | [+1,-1,-1,+1,-1,+1,+1,-1,+1]
7 | [-1,-1,-1,+1,+1,+1] | [-1,-1,-1,+1,+1,+1,-1] | [-1,-1,-1,+1,+1,+1,-1,-1] | [-1,-1,-1,+1,+1,+1,-1,-1,+1]
8 | [+1,-1,-1,+1,+1,+1] | [+1,-1,-1,+1,+1,+1,-1] | [+1,-1,-1,+1,+1,+1,-1,-1] | [+1,-1,-1,+1,+1,+1,-1,-1,+1]

## Slide 13: GI Definition for MIMO x2
Tables 5 below provides a summary of the GI definition for MIMO using Ga sequences for CB = 2.
Table 5: GI definition for different types of GI and number of streams for CB = 2.
Stream # | Short GI | Normal GI | Long GI
1 | GI164 = -Ga164 | GI1128 = +Ga1128 | GI1256 = +Ga1256
2 | GI264 = -Ga264 | GI2128 = +Ga2128 | GI2256 = +Ga2256
3 | GI364 = +Ga364 | GI3128 = +Ga3128 | GI3256 = +Ga3256
4 | GI464 = +Ga464 | GI4128 = +Ga4128 | GI4256 = +Ga4256
5 | GI564 = +Ga564 | GI5128 = +Ga5128 | GI5256 = +Ga5256
6 | GI664 = +Ga664 | GI6128 = +Ga6128 | GI6256 = +Ga6256
7 | GI764 = -Ga764 | GI7128 = +Ga7128 | GI7256 = +Ga7256
8 | GI864 = -Ga864 | GI8128 = +Ga8128 | GI8256 = +Ga8256

## Slide 14: GI Definition for MIMO x4
Tables 6 below provides a summary of the GI definition for MIMO using Ga sequences for CB = 4.
Table 6: GI definition for different types of GI and number of streams for CB = 4.
Stream # | Short GI | Normal GI | Long GI
1 | GI1128 = +Ga1128 | GI1256 = +Ga1256 | GI1512 = +Ga1512
2 | GI2128 = +Ga2128 | GI2256 = +Ga2256 | GI2512 = +Ga2512
3 | GI3128 = -Ga3128 | GI3256 = +Ga3256 | GI3512 = +Ga3512
4 | GI4128 = -Ga4128 | GI4256 = +Ga4256 | GI4512 = +Ga4512
5 | GI5128 = -Ga5128 | GI5256 = +Ga5256 | GI5512 = +Ga5512
6 | GI6128 = -Ga6128 | GI6256 = +Ga6256 | GI6512 = +Ga6512
7 | GI7128 = -Ga7128 | GI7256 = +Ga7256 | GI7512 = +Ga7512
8 | GI8128 = -Ga8128 | GI8256 = +Ga8256 | GI8512 = +Ga8512

## Slide 15: GSS for Channel Bonding x3
GSS definition:
  Ga96: Dk = [3, 24, 6, 12, 48];
  Ga192: Dk = [3, 24, 6, 12, 48, 96];
  Ga384: Dk = [3, 24, 6, 12, 48, 96, 192] – was proposed for CEF x3 and defined in [3];
  Weight vectors Wk are provided in the Table 7 below.
Stream # | Wk vector for Ga96 | Wk vector for Ga192 | Wk vector for Ga384
1 | [-1,-1,-1,-1,+1] | [-1,-1,-1,-1,+1,+1] | [-1,-1,-1,-1,+1,-1,-1]
2 |  |  | 
3 | [-1,-1,-1,+1,-1] | [-1,-1,-1,+1,-1,+1] | [-1,-1,-1,+1,-1,-1,+1]
4 |  |  | 
5 | [-1,-1,+1,-1,-1] | [-1,-1,+1,-1,-1,+1] | [-1,-1,-1,+1,-1,+1,+1]
6 |  |  | 
7 | [-1,-1,+1,+1,-1] | [-1,-1,+1,+1,-1,+1] | [-1,-1,-1,+1,+1,+1,-1]
8 |  |  | 
Table 7: GSS weight vectors definition for different sequence lengths and stream number for CB = 3.

## Slide 16: GSS for Channel Bonding x3 (Cont’d)
GSS x3 sequences generation:
  In order to get a required length of 96, 192, and 384 for Ga/Gb sequences, one needs to apply the following recursive operation:
    Ga3 = [+1, +1, -1];
    Gb3 = [+1, +j, +1];
    Streams 1, 3, 5, 7: (A0(n), B0(n)) = (+Ga3(2-n), +Gb3(2-n));
    Streams 2, 4, 6, 8: (A0(n), B0(n)) = (+conj(Gb3(n)), -conj(Ga3(n)));
    Ak(n) = Wk*Ak-1(n) + Bk-1(n-Dk);
    Bk(n) = Wk*Ak-1(n) – Bk-1(n-Dk);
  NOTE: the difference from the standard definition is that A0(n) and B0(n) sequences at the zero iteration are not Dirac delta functions, but rather Ga3(n) and Gb3(n) or Ga3(2-n) and Gb3(2-n) introduced above, (2-n) defines inverted order of samples;
  Starting from the length N = 3 and making 5, 6, and 7 iterations, one will get length of 96, 192, and 384 accordingly;

## Slide 17: GI Definition for MIMO x3
Tables 8 below provides a summary of the GI definition for MIMO using Ga sequences for CB = 3.
Table 8: GI definition for different types of GI and number of streams for CB = 3.
Stream # | Short GI | Normal GI | Long GI
1 | GI196 = +Ga196 | GI1192 = +Ga1192 | GI1384 = +Ga1384
2 | GI296 = +Ga296 | GI2192 = +Ga2192 | GI2384 = +Ga2384
3 | GI396 = +Ga396 | GI3192 = +Ga3192 | GI3384 = +Ga3384
4 | GI496 = +Ga496 | GI4192 = +Ga4192 | GI4384 = +Ga4384
5 | GI596 = +Ga596 | GI5192 = +Ga5192 | GI5384 = +Ga5384
6 | GI696 = +Ga696 | GI6192 = +Ga6192 | GI6384 = +Ga6384
7 | GI796 = +Ga796 | GI7192 = +Ga7192 | GI7384 = +Ga7384
8 | GI896 = +Ga896 | GI8192 = +Ga8192 | GI8384 = +Ga8384

## Slide 18: SP/M
Do you agree to add the following to the SFD:
  The 11ay specification should define the symbol blocking structure and GI definition for SU-MIMO, MU-MIMO, CB = 1, 2, 3, 4 for SC PHY provided on slides 5 – 17 of this presentation.

## Slide 19: References
11-16-1394-00-00ay Packet structure for SC EDMG PPDU for each GI length
11-15-1358-06-00ay-11ay Spec Framework
11-16-1207-00-00ay-SC-PHY-EDMG-CEF-design-for-channel-bonding-x3
Draft P802.11REVmc_D5.4