## Slide 1: Consideration on Internal Contention Between Data and Trigger Frame
Date: 2016-11-08
Authors:

## Slide 2: Background
To improve HE STAs UL performance, 2 set EDCA feature is present in the TGax D0.5[1] to lowers HE non-AP STAs’ EDCA channel access probability when they are scheduled by the AP.
  (MAC Motion #91)In addition, an HE AP may temporarily change the EDCA access parameters for HE non-AP STAs that are UL MU capable, by including an MU EDCA Parameter Set element in the Beacon frame, Probe Response frame, and (Re-)Association Response frame. An HE non-AP STA that receives an MU EDCA Parameter Set element from its associated AP follows the rules defined in 25.2.3 (Obtaining an EDCA TXOP for UL MU capable STAs).

## Slide 3: Motivation
How to avoid the unexpected access delay for trigger frame transmissions due to internal contention should be considered.
The following is present in the TGax D0.5
  An AP may send the Trigger frame using any access category and follows the rules defined in 10.22.2 (HCF contention based channel access (EDCA)) for obtaining and sharing the TXOP.(MAC Motion #90)

## Slide 4: Proposal – option 1
(current D0.5) An AP may send the Trigger frame using any access category and follows the rules defined in 10.22.2 (HCF contention based channel access (EDCA)) for obtaining and sharing the TXOP.(MAC Motion #90)
  (proposal) Note:
    The chosen AC for sending the trigger frame should be the same AC as the data which is being solicited by the trigger frame.
    The trigger frame should access channel with higher priority compared with the data in same AC.

## Slide 5: Proposal – option 2
(current D0.5) An AP may send the Trigger frame using any access category and follows the rules defined in 10.22.2 (HCF contention based channel access (EDCA)) for obtaining and sharing the TXOP.(MAC Motion #90)
  (proposal) Note:
    The AP should choose the highest AC for sending a trigger frame regardless of the AC of the data that the trigger is soliciting.
    The trigger frame may access channel with higher priority compared with the data in same AC.

## Slide 6: Proposal – option 3
The spec should define a new AC dedicated for trigger frame transmission. The EDCA parameter for the new AC shall be broadcasted in a BEACON frame, Probe Response frame, and (Re-)Association Response frame.

## Slide 7: SP
Which option do you prefer to
  Option 1: As described in page 4
  Option 2: As described in page 5
  Option 3: As described in page 6

## Slide 8: References
11-16/0024r1, Draft Specifications, D0.5