## Slide 1: EDMG PHY Headers for Open Loop Spatial Multiplexing in SU-MIMO
Date: 2016-11-7
Authors:

## Slide 2: Introduction
  Several MIMO scenarios for 11ay have been proposed [1], and the contribution of [2] proposed open loop spatial multiplexing (OLSM) + PH(Phase Hopping) as OLSM and showed PER(Packet Error Rate) performance. The contributions of [3] proposed OLSM + PH with precoding as OLSM and evaluated PER performance.
This contribution discusses the necessity of including related bits for OLSM in SU-MIMO EDMG-header-A [4].

## Slide 3: Necessity of including related bits for OLSM in SU-MIMO EDMG-header-A
    The contributions of [3] proposed OLSM + PH with precoding as OLSM and the following motion has been passed.
  Do you agree to modify the following in clause 6.1 of the SFD:
  “For EDMG OFDM mode, the 11ay specification shall define SU EDMG PPDU transmission with and without phase hopping. An EDMG STA may support transmission and reception of SU EDMG PPDU with phase hopping. In this mechanism, the following apply:
  - Precoding may be used
  - The period of phase hopping is TBD.”
    The contribution of [4] proposed a definition for SU-MIMO EDMG-header-A and we consider that including related bits for OLSM in SU-MIMO EDMG-header-A is necessary.

## Slide 4: Additional SU-MIMO EDMG-Header-A fields
To indicate whether PH and precoding are applied or not, “Phase hopping field (1bit)” and “Precoding field (1 bit)” are needed in the SU-MIMO EDMG-Header-A.
“Precoding field” requires 1 bit for PH.
Field name | Number of bits | Description
Phase hopping | 1 | A value of 1 indicates that phase hopping is applied. A value of 0 indicates that phase hopping is not applied.
Precoding | 1 | e.g.: a value of 0 indicates that precoding is not applied, and value of 1 indicates that precoding is applied.

## Slide 5: Summary
Regarding SU-MIMO EDMG-Header-A, the following motion of the contribution [4] has been passed.
  Do you agree to add to the SFD the following fields in the EDMG-header A of an EDMG SU PPDU: SU/MU field (1 bit), BW (TBD), primary channel (TBD bits), MCS (TBD), GI/CP length field (2 bits), PSDU length field (22 bits), Beamformed field (1 bit), Short/Long LDPC (1 bit), number of SS (TBD)?
In this contribution, additional SU-MIMO EDMG-Header-A fields are proposed.
  Phase hopping field (1 bit)
  Precoding field (1 bits)

## Slide 6: Straw poll
  Do you agree to add the following fields in the EDMG-header-A of an OFDM EDMG SU PPDU to the SFD:
  - Phase hopping field (1 bit): Reserved if either TX or RX does not
  support phase hopping.
  - Open loop precoding field (1 bit): Reserved if phase hopping field is
  “0”. Reserved if either TX or RX does
  not support phase hopping.

## Slide 7
References
11-15-0334-01-ng60-mimo-framework
11-16-0669-01-00ay-open-loop-spatial-multiplexing-with-phase-hopping-for-11ay
11-16-0959-00-00ay-open-loop-spatial-multiplexing-with-phase-hopping-for-11ay
11-16-1046-00-00ay-preliminary-design-ok-edmg-headers