## Slide 1: Multiple BSSID and MU
Date: 2016-11-06
Authors:
Name | Affiliation | Address | Phone | Email
Liwen Chu | Marvell |  |  | 
Abhishek Patil | Qualcomm |  |  | 
Po-kai Huang | Intel |  |  | 

## Slide 2: Recap of Multiple BSSID in 802.11ax
  In order to support legacy STA, multiple virtual APs belonging to a multi-BSS AP may need to broadcast beacons.
    AID of virtual AP per TIM element in Beacon are not fixed..
    Multicast AID bit position in a TIM element for a virtual AP is not fixed (i.e., depends on which one of the VAP is transmitting a beacon carrying the Multiple BSSID element)
  In one DL MU and UL MU transmission, frames from multiple BSSs or to multiple BSSs can be transmitted.
  It is not clear how to define TA of group-addressed frames in broadcast RU.
  It is not clear how to define the TA of a Trigger frame that destined to STAs associated with single virtual AP or the TA of a Trigger frame that destined to STAs associated with multiple virtual APs.
  The RA of frames in UL MU PPDU is not clearly defined.
Liwen Chu, Marvell, et. al.

## Slide 3: Transmitted BSSID in 11ax
  An HE AP device that operates in multi-BSSID mode shall designate one BSSID as the one that that takes the primary role to transmit Multiple BSSID element in Beacon and Probe Response frames
    Frames carry Multiple BSSID element which contains information about all the nontransmitted BSSs that the AP device supports.
  As per 802.11 baseline, an HE AP device that supports multiple BSS includes two types of virtual APs:
    AP with transmitted BSSID: the single virtual AP with transmitted BSSID will broadcast Beacon with Multiple BSSID element.
    AP with nontransmitted BSSID: other virtual APs shall not broadcast Beacon with Multiple BSSID element, however they may broadcast Beacons without Multiple BSSID element when the virtual APs assume that legacy STAs will associate with them.
      For each nontransmitted BSSID there is a unique transmitted BSSID. Therefore, the relative index for deriving the nontransmitted BSSID and group-addressed AID is always fixed.
  MaxBSSID Indicator field and Tx BSSID Indicator field are added to HE Operation element.
    With MaxBSSID Indicator value n, a HE STA associated with a virtual AP which owns nontransmitted BSSID figure out transmitted BSSID 48-n MSB.
    The Tx BSSID Indicator indicates whether an HE AP corresponds to transmitted BSSID.
Liwen Chu, Marvell, et. al.

## Slide 4: Multi-BSSID Control Frame Support
802.11 Baseline spec states that for the STA that supports Multi-BSSID functionality, the STA shall support frame filtering for up to two BSSIDs (one for the transmitted BSSID and one for the nontransmitted BSSID) for Beacon, Probe Response, and TIM broadcast frames.
To extend Multi-BSSID functionality to control frames, we expect that the STA then needs to support frame filtering for up to two BSSIDs (one for the transmitted BSSID and one for the nontransmitted BSSID) for control frame as well. This adds more requirement to 11ax implementation.
Due to this reason, we propose that
  It is optional for non-AP STA associated with a BSS corresponding to a nontransmitted BSSID to support reception of control frame with TA equal to transmitted BSSID
  Designate a bit in HE Capabilities element to indicate support for multi-BSSID extension of control frames
  An HE AP shall only address a STA associated with a BSS corresponding to a nontransmitted BSSID with a control frame with TA equal to transmitted BSSID if the STAs indicate support for multi-BSSID extension of control frames
Liwen Chu, Marvell, et. al.

## Slide 5: HE STA’s Behavior
An HE STAs upon receiving such an element may scan the medium to identify the transmitting BSSID and identify the index and multicast AID mapping for its nontransmitted BSSID with respect to the transmitting BSSID
  This can be done via the Multiple BSSID element carried in the transmitting BSSID’s Beacon/Probe Response frames.
Upon identifying the transmitting BSSID, an HE STA that announces the support for multi-BSSID extension of control frames shall not discard control frames (specifically Trigger, Multi-STA BA, NDPA) transmitted by the transmitting BSSID.
In addition, an HE STA may attempt to associate with the transmitted BSSID if it finds it to be suitable.
Liwen Chu, Marvell, et. al.

## Slide 6: MU Transmission with Multiple BSSID
For group-addressed frames , e.g. Basic Trigger frame, destined to STAs associated with multiple virtual APs,
  Transmitted BSSID is used as TA of such frames.
  STAID field value of 2047 identifies RU allocated to all BSSID in MBSS.
For group-addressed frames , e.g. Basic Trigger frame, destined to STAs associated with single virtual AP,
  Virtual AP’s BSSID is used as TA of such frames.
  STAID field value of the virtual AP identifies RU allocated to the virtual AP’s BSSID.
For both case, the following rules apply:
  RA fields of all frames in an A-MPDU are same, and TA fields of all frames in an A-MPDU are same.
  If a frame solicited by Trigger frame is control frame, the RA selection of the control frame uses the TA of the soliciting frame or associated AP’s MAC address.
  If a frame solicited by Trigger frame is data/management frame, the RA of the solicited frame is set to the intended recipient.
Liwen Chu, Marvell, et. al.

## Slide 7: Summary
We propose
  an HE AP device that operates in multi-BSSID mode shall assign one BSSID as the one that that takes the primary role to transmit Multiple BSSID element in Beacon and Probe Response frames.
  it is optional for non-AP STA associated with a BSS corresponding to a nontransmitted BSSID to support reception of control frame with TA equal to transmitted BSSID.
  TA and RA rules with multiple BSSID element.
Liwen Chu, Marvell, et. al.

## Slide 8: Backup Slides
Liwen Chu, Marvell, et. al.

## Slide 9: AID of Broadcast RU in DL MU
When multiple virtual APs transmit Beacons, broadcast RU for STAs associated with single virtual AP in DL MU is difficult to identify.
  The reason is that each virtual AP doesn’t have a fixed AID for broadcast transmission in a DL broadcast RU.
    The AID calculation of each virtual AP has different reference BSSID.
      STAs may miss some Beacon,
      STAs may have inaccurate TSF time.
      An AP may change its beacon interval.
Beacon from Virtual AP0
Beacon from Virtual AP1
Beacon from Virtual AP2
AP0 has AID 0, AP1 has AID1 etc.
AP0 has AID 2n-1, AP1 has AID0 etc.
AP0 has AID 2n-2, AP2 has AID0 etc.
DL MU
RU control info
TA Info
Liwen Chu, Marvell, et. al.

## Slide 10: Spec Texts Related to Beacon, Probe Response, TIM Broadcast
A non-AP STA in which dot11MultiBSSIDActivated is true shall support frame filtering for up to two BSSIDs; one for the transmitted BSSID and one for the nontransmitted BSSID. The STA, when associated with a BSS corresponding to a nontransmitted BSSID, shall discard all Data and Management frames that use the transmitted BSSID as the transmit address, except for Beacon, Probe Response, and TIM broadcast frames. (See 11.1.3.7 Beacon reception)
Liwen Chu, Marvell, et. al.