## Slide 1
Considerations on Quiet Time Period
Date: 2016-11-06
Authors:

## Slide 2: Introduction
HE AP could receive QTP(Quiet Time Period) Request and transmit QTP Response and QTP Setup to set QTP[1][2]
  STA-2-STA STAs could transmit QTP request in order to request protection on STA-2-STA TXOP
Specific protection or quiet mechanism is not considered yet[2]
  A new type of mechanism to prohibit STAs’ channel access could be defined for QTP procedure
  Conventional NAV procedure could be reused for QTP setting

## Slide 3: QTP Scenario
An HE STA-2-STA STA could be a QTP request STA
An HE AP should be a QTP response STA
HE STAs could decode QTP setup frame
HE STA which receive QTP setup shall not transmit its frame except immediate response frame

## Slide 4: QTP Scenario
Why only HE STAs shall not transmit during QTP?
  For legacy protection?
  Or because legacy STAs cannot decode QTP Setup frame?

## Slide 5: QTP setup mechanism
QTP is a mechanism to set a Quiet Period to non QTP request STAs in HE BSS
STAs which received QTP Setup frame shall not access channel during Quiet Period Duration except a QTP Request STA
  We already have similar procedure, so-called NAV procedure
  Without defining any other new procedure, NAV could be a good QTP setup mechanism for QTP setup STAs
Therefore, recipients of QTP Setup frame except QTP requestor shall set a NAV after receiving QTP Setup frame
  A QTP Requestor STA shall not set NAV timer even QTP Setup frame is received

## Slide 6: QTP setup mechanism
If HE AP wants to set QTP for all 802.11 STAs, HE AP could set NAV by transmitting non-HT PPDU format QTP Setup frame whose value of Duration field is Quiet Period Duration

## Slide 7: QTP setup mechanism
If HE AP wants to set QTP for HE STAs only, then HE AP shall transmit HE PPDU format QTP Setup frame
  Recipients of QTP Setup frame set a NAV based on the value of Duration field or the value of Quiet Period Duration field in QTP setup element

## Slide 8: Conclusions
QTP is a mechanism for enhancing STA-2-STA transmission performance and it could be enabled by setting NAV for other STAs
NAV based QTP and supporting legacy STAs’ QTP using non-HT PPDU format need to be considered
  If an AP wants to provide a powerful protection, QTP shall be set to legacy STAs also
  If legacy STA’s QTP is an implementation issue, then just specify NAV setting procedure for QTP (Do not limit QTP setting to HE STAs.)

## Slide 9: References
[1] 11-16/1237r1 “setting-quiet-time-period”
[2] 11-16/1238r1 “Setting Quiet time period – text”