## Slide 1: New Amendment Style
Date: 2016-11-07
Authors:

## Slide 2: Background
The 802.11 specification defines a large set of MAC features and the set increases with each amendment
With each amendment:
  We need to identify the features in the baseline that apply to devices implementing the amended specification
  If we modify an existing feature, we need to make sure the modification only applies to the devices implementing the amended specification
  We need to make sure we don’t apply a new requirements to a legacy device
These issues are becoming more complicated as we define behavior for new bands (900 MHz, TV whitespace, 45 GHz, 60 GHz)
  In a new band there is no legacy and thus no backward compatibility requirement
  As a result, we pick and choose the features supported in these bands
  And, of course, add a bunch of new features

## Slide 3: The proliferation of STA types and their requirement inheritance
HT
VHT
DMG
S1G
EDMG
45MG
HE
QoS
Mesh
FILS
GLK
CDMG
S1G relay
TVHT
One technique we use to define feature set applicability is the STA type
STA
(unadorned)

## Slide 4: STA types and requirement applicability
A STA type is defined by the set of requirements associated with it
  I.e., A VHT STA shall…
A STA type may also inherit a set of requirements from another STA type
  An HT STA is also a QoS STA. [REVmc/D8.0 P77L13]
  A VHT STA is an HT STA that, in addition to features supported as an HT STA, supports VHT features identified in … [REVmc/D8.0 P77L40]
  A DMG STA is also a QoS STA. [REVmc/D8.0 P91L50]
Normative statements that apply to the parent thus apply to the child (and its children)
All STA types inherit requirements that apply to the generic (unadorned) STA
  A STA that receives an RTS frame addressed to it considers the NAV in determining whether to respond with CTS… [REVmc/D8.0 P1277L22]

## Slide 5: The inverse set: “non-” prefixes
To apply a requirement to a set of STA types that excludes a specific STA type we often use a “non-” prefix
We often use this to deal with legacy compatibility
Examples:
  A non-DMG QoS STA receiving a QoS Data frame sent under a BA agreement… [REVmc/D8.0 P1286L25]
    Requirement applies to a QoS STA that is not a DMG STA and the children that are not DMG STAs (mesh STA, HT STA, VHT STA, HE STA, TVHT STA and S1G STA)
  When a block ack agreement is set up between a non-HT non-DMG STA and another STA, …[REVmc/D8.0 P1384L16]
    Requirement applies to a QoS STA but not its DMG and HT decedents. It applies to an S1G STA.
However, to determine if a requirement applies to a particular STA type, the reader needs to understand the inheritance map

## Slide 6: Additional notes
STA types are not mutually exclusive
  A VHT STA might also be a mesh STA, FILS STA and GLK STA
Some STA types have specific PHYs associated with them (requirements on both the MAC and PHY)
  E.g., S1G, DMG, HT, VHT, TVHT, CDMG, 45MG
And some do not (requirements on the MAC only)
  E.g., mesh, QoS, FILS, GLK
Some STA combinations are ambiguous (expected behavior is not well defined)
  E.g., DMG mesh STA or DMG FILS STA

## Slide 7: Difficulties with large numbers of STA types
Managing requirements by STA type is proving difficult
As we apply different sets of features to different STA types and tailor existing features to each STA type we end up with procedures adorned with STA specific requirements
To decipher these procedures, the reader needs understand the relationships between the various STA types
The standard does not clearly convey these relationships

## Slide 8: Example
10.3.2.7 CTS and DMG CTS procedure A STA that receives an RTS frame addressed to it considers the NAV in determining whether to respond with CTS unless the NAV was set by a frame originating from the STA sending the RTS frame (see 10.22.2.2 (EDCA backoff procedure)). In this subclause for a non-S1G STA, “NAV indicates idle” means that the NAV count is 0 or that the NAV count is nonzero but the nonbandwidth signaling TA obtained from the TA field of the RTS frame matches the saved TXOP holder address. In an S1G STA, “NAV indicates idle” means that both NAV and RID counters are 0 or that either NAV or RID counter is nonzero but the TA field of the RTS frame matches the saved TXOP holder address.
A VHT STA that is addressed by an RTS frame in a non-HT or non-HT duplicate PPDU that has a bandwidth signaling TA and that has the RXVECTOR parameter DYN_BANDWIDTH_IN_NON_HT equal to Static behaves as follows …
A VHT STA that is addressed by an RTS frame in a non-HT or non-HT duplicate PPDU that has a bandwidth signaling TA and that has the RXVECTOR parameter DYN_BANDWIDTH_IN_NON_HT equal to Dynamic behaves as follows …
An S1G STA that is addressed by an RTS frame that has the Dynamic Indication field in the Frame Control field equal to 0 (Static) behaves as follows …
An S1G STA that is addressed by an RTS carried in a 2 MHz duplicate frame that has the Dynamic Indication field in the Frame Control field equal to 1 (Dynamic) behaves as follows …
A non-VHT and non-S1G STA that is addressed by an RTS frame or a VHT STA that is addressed by an RTS frame carried in a non-HT or non-HT duplicate PPDU that has a nonbandwidth signaling TA or a VHT STA that is addressed by an RTS frame in a format other than non-HT or non-HT duplicate behaves as follows …
A DMG STA follows the procedure defined in this subclause, except … Bunch of statements about S1G STA
Statements about DMG STA

## Slide 9: Proposed solution
Have a separate MAC clause for a new set of features and include specific legacy behavior by reference:
  Clause 24 – XSTA MAC
    24.1 General
    An XSTA does not conform to the requirements of clause 4-11, except where specifically referenced from this Clause.
    24.5.6.7 MAC CRC field
    The CRC field is defined in 9.2.1.4.
In the January 2016 Editor’s meeting we discussed introducing a new amendment style (see 16/0035r0)
TGax’s draft amendment was identified as a good vehicle to try this out

## Slide 10: P802.11ax/D0.5 Contents
3. Definitions, acronyms, and abbreviations
4. General description
6. Layer management
8. PHY service specification
9. Frame formats
10. MAC sublayer functional description
11. MLME
17. Orthogonal frequency division multiplexing (OFDM) PHY specification
25. High Efficiency (HE) MAC specification
26. High Efficiency (HE) PHY specification
Main change is addition of an HE MAC specification clause

## Slide 11: P802.11ax/D0.5 Clause 25 contents
25. High Efficiency (HE) MAC specification
  25.1 Introduction
  25.2 Channel Access
  25.3 Fragmentation
  25.4 Block acknowledgement
  25.5 MU operation
  25.6 HE sounding protocol
  25.7 TWT operation
  25.8 Operating mode indication
  25.9 Spatial reuse operation
  25.10 A-MPDU operation
  25.11 TXVECTOR parameters STA_ID_LIST, UPLINK_FLAG, BEAM_CHANGE and BSS_COLOR for an HE PPDU(#2517)
  …
New procedures that apply to HE STAs are concentrated in this new clause rather than spread throughout the other clauses

## Slide 12: Defining an HE STA is easy
4.3.14a High efficiency (HE) STA The IEEE 802.11 HE STA operates in frequency bands between 1 GHz and 6 GHz. An HE STA is VHT STA or HT non-AP STA that, in addition to the features supported as a VHT STA or HT non-AP STA respectively, supports the MAC features defined in Clause 25 and the PHY features defined in Clause 26.
4.3.14 Very high throughput (VHT) STA The IEEE Std 802.11 VHT STA operates in frequency bands below 6 GHz excluding the 2.4 GHz band. A VHT STA is an HT STA that, in addition to features supported as an HT STA, supports VHT features identified in Clause 9 (Frame formats), Clause 10 (MAC sublayer functional description), Clause 11 (MLME), Clause 14 (MLME mesh procedures), Clause 17 (Orthogonal frequency division multiplexing (OFDM) PHY specification), and Clause 21 (Very High Throughput (VHT) PHY specification).
Vs
All new MAC features are in one place; reader goes there first

## Slide 13: Example: Fragmentation
25.3 Fragmentation 25.3.1 General An HE STA supports the static fragmentation procedure defined in 10.2.7 (Fragmentation/defragmentation overview), 10.5 (Fragmentation), and 10.6 (Defragmentation). In addition, an HE STA can support the dynamic fragmentation procedure defined in this subclause. …
An HE STA supports the existing fragmentation procedure plus a new procedure.
  Reference the old procedure explicitly
  Add the new procedure to Clause 25
We don’t have to say anything about non-HE STAs not supporting this procedure since nothing in Clause 25 applies to pre-HE devices

## Slide 14: Example: A-MPDU operation
25.10 A-MPDU operation … 25.10.2 A-MPDU padding for an HE SU PPDU, HE extended range SU PPDU and HE MU PPDU An HE STA that transmits an HE SU PPDU, HE extended range SU PPDU or UL HE MU PPDU that contains one A-MPDU, shall construct the A-MPDU(s) as described in 10.13.6 (A-MPDU padding for VHT PPDU). … 25.10.3 A-MPDU padding for an HE trigger-based PPDU A non-AP STA that transmits an HE trigger-based PPDU shall construct the PSDU carried in the HE trigger-based PPDU as described in this subclause.
The procedure for an HE SU PPDU, HE extended range SU PPDU and HE MU PPDU is the same as the VHT procedure (apply by reference)
The procedure for an HE trigger-based PPDU is different since the payload size is defined by the Trigger frame and not by the amount of data the STA has to send (define new procedure)

## Slide 15: Summary
The new amendment style is not a radical departure from how we amend the 802.11 specification
It concentrates MAC changes into one clause which helps with a number issues:
  Helps the reader identify when a new feature was introduced
  Reduces the change needed to existing procedures when a new procedures are introduced
  Keeps the procedure as it applies to legacy devices unchanged, but allows the procedure to be modified for new devices
The inheritance hierarchy is clear in the structure of the document