## Slide 1: On the Implementation of Dynamic Load Balancing for A-BFT Channel
Date: 2016-11-07
Authors:
Name | Company | Address | Phone | Email
Sang G. Kim | LG Electronics |  |  | sanggook.kim@lge.com
Kyungtae Jo |  |  |  | kyungtae.jo@lge.com
SungJin Park |  |  |  | allean.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
JinMin Kim |  |  |  | jinmin1230.kim@lge.com
Saehee Bang |  |  |  | saehee.bang@lge.com

## Slide 2: Introduction (1/2)
Dynamic load balancing over A-BFT channel was proposed to alleviate overload situation due to inherent 11ad design and new use cases envisioned in 11ay [1]
Motion was approved and the following text was incorporated into SFD [2]:
  “11ay shall support dynamic load balancing in A-BFT by providing means to adjust necessary parameters (e.g. RSSBackoff or/and RSSRetryLimit). The ranges of new parameters (e.g. RSSBackoff or/and RSSRetryLimit) are determined by the reserved bits in Beacon Interval Control field. The exact bits are TBD.”
Since the reserved bits in Beacon Interval Control field are limited (4 bits) and a new Information Element can contribute heavier Beacon content, it is better to add a field into existing element.

## Slide 3: Introduction (2/2)
In this contribution, we propose the method to implement dynamic load balancing specified in SFD by introducing a field into EDMG Operation element already defined.

## Slide 4: EDMG Operation Element and Proposal (1/2)
  EDMG Operation element is already included in SFD
  PCP/AP provides EDMG Operation element and it determines operational parameters of an EDMG BSS
  Proposal:
    1 octet of a field (“OverloadControl”) is included in EDMG Operation element
    The first half (4 bits) denotes the values of RSSBackoff and RSSRetryLimit
    The second half (4 bits) is reserved

## Slide 5: EDMG Operation Element and Proposal (2/2)
Bit Values (B0 B1) | RSSBackoff
00 | 8 (No change with 11 ad)
01 | 16
10 | 24
11 | 32
Bit Values (B2 B3) | RSSRetryLimit
00 | 2
01 | 4
10 | 6
11 | 8 (No change with 11 ad)

## Slide 6: Summary
Method to implement dynamic load balancing to address overload situation in A-BFT channel is proposed
1 octet of the field (“OverloadControl”) is newly defined with description and values as in slide 4 - 5
Since it uses already defined EDMG Operation element, no need to introduce a new element and this is well suited without incurring much complexity

## Slide 7: Reference
[1] 11-16-0948-00-00ay-on-random-access-in-a-bft
[2] 11-15-1358-09-00ay-11ay Spec Framework

## Slide 8: Straw poll
Do you agree to add the following text into SFD?
  “The EDMG Operation element includes signaling of RSSBackoff and RSSRetryLimit”
  Y/N/A

## Slide 9: Straw poll
Do you agree to add the following text into SFD?
  “EDMG operation element shall define signaling for dynamic load balancing for A-BFT channel as shown and described in slides 4 - 5”
  Y/N/A

## Slide 10: Motion
Do you agree to add the following text into SFD?
  “The EDMG Operation element includes signaling of RSSBackoff and RSSRetryLimit”
  Y/N/A

## Slide 11: Motion
Do you agree to add the following text into SFD?
  “EDMG operation element shall define signaling for dynamic load balancing for A-BFT channel as shown and described in slides 4 - 5”
  Y/N/A