## Slide 1: EDMG-Header-A contests
Date: 2016-11-08
Authors:
Name | Company | Address | Phone | Email
Jinmin Kim | LG Electronics |  |  | jinmin1230.kim@lge.com
Kyungtae Jo |  |  |  | kyungtae.jo@lge.com
SungJin Park |  |  |  | allean.park@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com
Sang G. Kim |  |  |  | sanggook.kim@lge.com
Saehee Bang |  |  |  | saehee.bang@lge.com

## Slide 2: Introduction
In this contribution, we propose the contents of EDMG-Header-A for SU&MU.
First, we detail more how to design MCS field of SU considering HW complexity & link adaptation gain
Next, we will deal with the contents of EDMG-Header-A for FDMA.

## Slide 3: EDMG-Header-A for SU

## Slide 4: 1st Topic: MCS - Criterion of the number of MCS -
We have to consider some issues when we decide the number of MCS for spatial streams
  HW complexity
  Flexibility of indicating MCS for spatial stream
  Signaling overhead in EDMG-Header-A
Based on above, we can consider 2 methods for the number of MCS
  Method 1:
    Independent MCS field for each spatial stream
  Method 2:
    Define a Base MCS field and 8 differential MCS fields

## Slide 5: 1st Topic: MCS - Proposed MCS field(1/2) -
Considering flexibility & signaling overhead & real channel environments, method 1 is reasonable for 4 or less spatial streams and method 2 is preferred for above 4 spatial streams
So, we propose MCS field in different way by NSS. For example,
  If NSS <= 4, the MCS field would be defined as:
    {MCS1, MCS2, MCS3, MCS4}, i.e. 5 * 4 = 20 bits
  If NSS > 4, the MCS field would be defined as:
    {Base MCS, diffMcs1, diffMcs2, diffMcs3, diffMcs4, diffMcs5, diffMcs6, diffMcs7, diffMcs8}, i.e. 5 + 8 * 2 = 21 bits
In method 2, the step size in differential MCS field have to be defined considering HW complexity & MIMO channel environment
  11n already defined UEP(unequal error protection) for spatial streams. And it only supports different modulation order not code rate for HW simplicity

## Slide 6: 1st Topic: MCS - Proposed MCS field(2/2) -
So, we propose that the step size is modulation order for above 4 spatial streams
  Base MCS: the lowest MCS index across all spatial streams (5bits)
  Diff. MCS: the different modulation order compared to base MCS (2bits)
    ‘00’ indicates the same MCS with the base MCS
    ‘01’ indicates the one-step higher order modulation than the base MCS with the same code rate
    ‘10’ indicates the two-step higher order modulation than the base MCS with the same code rate
    ‘11’ indicates the three-step higher order modulation than the base MCS with the same code rate
  For example, if Base MCS is QPSK ½ code rate,
    ‘00’ is QPSK ½ code rate. ‘01’ is 16QAM ½ code rate
    ‘10’ is 64QAM ½ code rate.‘11’ is 256QAM ½ code rate

## Slide 7: 2nd Topic: Channel Aggregation - The number of MCS -
There are 2 options in channel aggregation
  1st option: total number of MCS is N regardless of channel aggregation
    In channel aggregation, N/2 MCSs are used for spatial stream per aggregated channel
  2nd option: total number of MCS is 2xN when channel aggregation is used
    In channel aggregation, N MCSs can be used for spatial stream in each aggregated channel
We prefer option 1 for low signaling overhead in EDMG-Header-A.

## Slide 8: 2nd Topic: Channel Aggregation - The number of spatial stream(NSS) -
There are 2 options for how to assign NSS in each aggregated channel
  Option 1: same NSS between each aggregated channel
  Option 2: independent NSS in each aggregated channel
We prefer option 2 since each aggregated channel can have different channel characteristics.

## Slide 9: EDMG-Header-A for MU

## Slide 10: MU-MIMO / FDMA indication
We propose to add 1 bit to EDMG-Header-A for MU PPDU to indicate whether current PPDU is for MU-MIMO or FDMA

## Slide 11: EDMG Header-A contents for FDMA
The contents for FDMA can be simply designed in a similar way to MU-MIMO
The maximum number of STAs to be allocated in FDMA is four since the maximum number of channels in CB/CA is four
  We define 4 channel descriptors like SS descriptor in MU-MIMO
  We limit the maximum NSS per STA to 2 streams (1bits)
    Maximum number of spatial streams per AP would be 8 (with four users)
  Beamformed field(1 bit) is independently defined per STA in EDMG Header-A
    Because each EDMG Header-B and data for STAs can be pre-coded differently in frequency domain
Channel Descriptor 0 |  |  | Channel Descriptor 1 |  |  | Channel Descriptor 2 |  |  | Channel Descriptor 3 |  | 
AID | NSS | BF | AID | NSS | BF | AID | NSS | BF | AID | NSS | BF
8bits | 1bits | 1bit | 8bits | 1bits | 1bit | 8bits | 1bits | 1bit | 8bits | 1bits | 1bit

## Slide 12: Conclusion
We propose to define MCS field in EDMG-Header-A for SU
  Also, how to assign the number of spatial streams in channel aggregation
We propose to add MU-MIMO/FDMA indication bit to EDMG-Header-A for MU
  Also, EDMG-Header-A contents for FDMA

## Slide 13: SP/M #1
Do you agree to insert the following text into the SFD
  If NSS <= 4, the MCS field in EDMG-Header-A for SU is defined as:
    4 MCS fields (20bits)
      Each MCS field (5 bits) is for each spatial stream
  If NSS > 4, the MCS field in EDMG-Header-A for SU is defined as:
    Base MCS field (5bits)
      this indicates the lowest MCS index across all spatial streams
    8 differential MCS fields (16bits)
      Each MCS field (2bits) for each spatial stream is interpreted as follows:
        ‘00’ indicates the same MCS with the base MCS
        ‘01’ indicates the one-step higher order modulation than the base MCS with the same code rate
        ‘10’ indicates the two-step higher order modulation than the base MCS with the same code rate
        ‘11’ indicates the three-step higher order modulation than the base MCS with the same code rate

## Slide 14: SP/M #2
Do you agree to insert the following text into the SFD
  The total number of MCS subfields in the EDMG-Header-A field shall be constant whether or not channel aggregation is used. Therefore, if channel aggregation is used, the number of MCSs assigned to each channel in the aggregate shall be N/2, where N is the total number of MCS subfields.

## Slide 15: SP/M #3
Do you agree to insert the following text into the SFD
  The maximum number of spatial stream in each aggregated channel is four in channel aggregation
  The different number of spatial stream can be allocated to each aggregated channel in channel aggregation

## Slide 16: SP/M #4
Do you agree to add the following field to the EDMG-Header A for MU:
  MU-MIMO / FDMA indication (1bit)

## Slide 17: SP/M #5
Do you agree to add the following fields to the EDMG Header-A when the PPDU is for FDMA
  4 Channel Descriptors, each of which has
    AID (8bits)
    NSS (1 bits)
    Beamformed (1bit)