## Slide 1: Location Measurement Protocol for 11ax
Date: 2016-11-08
Authors:

## Slide 2: Abstract
In this presentation we describe how an 11ax scheduling protocol may be used for performing the negotiation phase

## Slide 3: Recap: Accepted Functional Requirements
Addressed by this submission:
The location protocol shall support positioning measurement of unassociated and associated STAs in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent positioning measurements of multiple STAs, in both associated and (unassociated) states in the HE MU mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of an AP in HE operation mode. The same requirement shall also apply to VHT operation mode.
The 11az amendment shall have a mode supporting concurrent measurement from several transmit chains of each non-AP STA in the HE operation mode. The same requirement shall also apply to the VHT operation mode.

## Slide 4: 802.11ax UL MU Operation using Trigger Frame
AP transmits a Trigger frame to initiate UL MU transmission
  Resource allocation (RUs and spatial streams) signaled in Trigger frame
  Mixed UL transmission in frequency and spatial domains, i.e., UL-OFDMA or UL MU-MIMO
STAs transmit UL MU frames simultaneously after SIFS of Trigger frame transmission
AP transmits ACK/BA/M-BA frame to STAs
  Multi-STA BA (M-BA) is a new MU DL BA defined in 11ax as an extension of baseline Multi-TID BA for ACK/BA of multiple TIDs per STA

## Slide 5: Frame exchange flow description
Similar to FTM, the proposed mechanism is composed of 3 stages:
  Measurement negotiation
  Measurement exchange
  Termination (can be implicit or explicit, to be discussed at a later time)

## Slide 6: Proposed Service Negotiation Phase
TF Service Request
FTM Request
AP
STA
FTM Response
Propose to define a new Trigger frame type (currently there are 5 types of Trigger frames in 11ax
  The Trigger type is for service negotiation / request
  The frame format of the TF Service Request is TBD
  Proposed mechanism is adaptable for both scheduled and random-access based STAs
Propose that the TF Service Request frame solicits an FTM Request from STAs allowing capability exchange
The AP sends an FTM Response to complete the service negotiation phase
  Reuse legacy and add 11az IEs
  Legacy STAs skip the 11az IEs
SIFS
M-BA
SIFS
Same as REV\mc
SIFS
Ack

## Slide 7: Summary
We have proposed an 802.11ax-based FTM negotiation phase for both associated and unassociated STAs

## Slide 8: Straw Poll 1
Do you agree that 11az negotiation phase should support enhanced FTM Request in both SU and MU modes for both associated and unassociated states?