## Slide 1: Recommendation from PDED Ad Hoc in San Antonio in Nov 2016 wrt ED threshold
9 Nov 2016
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 2 84461010 +61 418 656587 | amyles@cisco.com

## Slide 2: IEEE 802.11 PDED ad hoc has been considering a request related to ED from 3GPP RAN1
  In R1-166040 (June 2016), 3GPP RAN1 further suggested that 802.11 be redefined to also use an ED of -72dBm in the future ...
  … rather than the currently defined ED of -62dBm (and PD of -82dBm)
RAN1 respectfully requests future IEEE 802.11 technologies to align the energy detection threshold used with other technologies operating in the same unlicensed band, e.g., -72 dBm.
An energy detection threshold of -72 dBm has been chosen by 3GPP for Rel-13 LAA also with an interest in aligning with other technologies in the future.

## Slide 3: The IEEE 802.11 PDED ad hoc considered various inputs over three teleconferences and one session
Pre-PDED ad hoc material
  19-16-0110-00 described issue & possible responses in 802.19 WG
  11-16-1263-00 summarised issue for 802.11 WG; led to ad hoc
PDED ad hoc teleconference material
  27 Sep – agenda, minutes – including proposal for simulation evidence
  11 Oct – agenda, minutes – mainly brainstorming
  25 Oct – agenda, minutes – including agreed direction in 11-16-1344-00
PDED ad hoc session material
  Agenda, minutes
  Simulation (11-16-1451-00) showing ED = -72 dBm produces poor results in mixed legacy/802.11ax environment

## Slide 4: The IEEE 802.11 PDED ad hoc recommends that the 3GPP RAN1 request be rejected
Motion
  The IEEE 802.11 PDED ad hoc recommends to the IEEE 802.11 WG that 11-16-1493-01 be sent to 3GPP RAN1 in response to their request that IEEE 802.11 adopt an ED of -72dBm. The Chair of the IEEE 802.11 PDED ad hoc has editorial license.
  Moved:
  Seconded:
  Result: 13/0/4
  Note: subsequent editorial changes resulted in 11-16-1493-03
    Main change was addition of text from actual 3GPP RAN1 request

## Slide 5: The IEEE 802.11 PDED ad hoc recommends that the 3GPP RAN1 request be rejected
Summary (1/3)
  Introduction
    Thanks 3GPP and reproduces request
  Interpretation of the request
    Notes that we understand request for ED of -72dBm to actually be a request for scaled ED between -72dB and -62dB depending on tx power
    Notes we understand request applies to 802.11ax in 5GHz band
  Background to 802.11 coexistence
    Notes PD is the key mechanism for co-existence for multiple generations, and such coexistence is required by 802.11ax PAR
    Notes that while 802.11ax is considering refinements to PD the default PD remains at -82dBmIn summary, both current and future 802.11 devices in 5 GHz band will continue to rely primarily on PD for coexistence.
  …

## Slide 6: The IEEE 802.11 PDED ad hoc recommends that the 3GPP RAN1 request be rejected
Summary (2/3)
  …
  Discussion
    Notes it is of primary importance that all devices operating in the 5 GHz band are able to detect each other with high sensitivity, and this is provided by PD
    Asserts it would be undesirable to introduce a lower ED threshold requirement because 802.11ax devices would be significantly disadvantaged
  Summary
    Notes there would be significant system harm in modifying the ED threshold used by 802.11ax devices
    Suggests continuing dialog and cooperation with RAN1 would be beneficial towards agreeing a future framework for efficient sharing of 5 GHz band
  …

## Slide 7: The IEEE 802.11 PDED ad hoc recommends that the 3GPP RAN1 request be rejected
Summary (3/3)
  …
  Actions
    Asks 3GPP RAN1 if they want to continue discussions on topic
    Asks 3GPP RAN1 to consider support for PD-based channel access in a future release of LAA specification
  Date
    Note dates of future IEEE 802 LMSC and 802.11 WG meetings

## Slide 8: It is now proposed that the LS be written to come from IEEE 802.11 WG rather than IEEE 802
  The IEEE 802.11 PDED ad hoc wrote the proposed LS as coming from IEEE 802
    It is natural for IEEE 802 to respond because the LS interaction so far has been from IEEE 802
    No one proposed an alternative approach
  The IEEE 802.11 WG Chair has now proposed that the LS be written as coming from IEEE 802.11 WG
    It would not need IEEE 802 EC approval
    The topic is aligned with IEEE 802.11 WG work
  The IEEE 802.11 PDED ad hoc has no view on this proposal and it is up to the WG

## Slide 9: The IEEE 802.11 WG may consider a recommendation to IEEE 802 EC wrt 3GPP RAN1 ED request (original)
Proposed motion for IEEE 802.11 WG
  The IEEE 802.11 WG recommends to the IEEE 802 EC that 11-16-1493-04 be sent to 3GPP RAN1 in response to their request that IEEE 802.11 adopt an ED of -72dBm. The Chair of the IEEE 802.11 WG has editorial license.
  Moved:
  Seconded:
  Result:

## Slide 10: The IEEE 802.11 WG may consider a recommendation to IEEE 802 EC wrt 3GPP RAN1 ED request (alternative)
Proposed motion for IEEE 802.11 WG
  The IEEE 802.11 WG recommends to the IEEE 802 EC that 11-16-1493-04 be sent to 3GPP RAN1 in response to their request that IEEE 802.11 adopt an ED of -72dBm. The Chair of the IEEE 802.11 WG is authorised to adjust the LS to come from IEEE 802.11 WG rather than IEEE 802, and has editorial license.
  Moved:
  Seconded:
  Result: