## Slide 1: Scheduling Allocations Over Multiple Channels
Date: 2017-01-16
Authors:

## Slide 2: Background: Channel Access over Multiple Channels
In a EDMG BSS the BTI, A-BFT and ATI is always present on the primary channel of the BSS.
IEEE 802.11ay shall support allocation of SP(s) and CBAP(s) over more than one channel and over a bonded channel through DMG Beacon frame, Announce frame and Grant frame. An allocation may not have the primary channel.
CH
1
(
Primary)
CH2
CH
3
Data
Data
Data
Allocation #1
Allocation #3
Data
Allocation #2
Beacon/
Announce
Data
Allocation #4

## Slide 3: Background: EDMG Extended Schedule element
The EDMG Extended Schedule element (ESE) defines incremental signaling to the ESE, including channel allocation indications if allocations are scheduled over more than one channel.
  The Channel Allocation field specifies the allocation and the bandwidth that the allocation occupies.
    The contents of the Allocation Key subfield are used to identify the allocation. This is done by correlating the contents of this subfield with the information obtained from the ESE transmitted in the same frame.
    The Channel Aggregation and BW subfields specify the properties of the allocation identified by the Allocation Key subfield.

## Slide 4: Problem Statement
For an allocation which does not include the primary channel (e.g., Allocation #2), a DMG STA cannot decode EDMG ESE, it will wrongly treat the allocation as it is over the primary channel.
As a result, the DMG STA may make confusion on that there exist overlapping allocations over the primary channel (e.g., Allocations #2 and #4).
  Note that spatial sharing mechanism is applicable to SP allocation only and is not implemented in any WiGig device.
EDMG ESE
ESE
CH
1
(
Primary)
CH2
CH
3
Data
Data
Data
Allocation #1
Allocation #3
Data
Allocation #2
Beacon/
Announce
Data
Allocation #4

## Slide 5: Proposal
For an allocation that does not include the primary channel, its allocation information shall be completely and only included in the EDMG ESE.
  ESE includes the allocation information only for the allocations that include the primary channel.
The size of the Channel Allocation field of EDMG ESE for an allocation depends on whether the allocation is based on incremental signaling or complete signaling.
An Scheduling Allocation subfield shall be added into each Allocation field of EDMG ESE to indicate whether an allocation is based on incremental signaling or complete signaling.
Example format of complete Channel Allocation field
Example format of incremental Channel Allocation field
EDMG ESE format

## Slide 6: Proposal (cont.)
A DMG STA can detect Allocation #4 but cannot detect allocation #2. Thus it will not make any confusion.
CH
1
(
Primary)
CH2
CH
3
Data
Data
Data
Allocation #1
Allocation #3
Data
Allocation #2
Beacon/
Announce
Data
Allocation #4
EDMG ESE
ESE

## Slide 7: Reference
11-15-1358-06-00ay-specification-framework-for-tgay
11-16-1208-00-00ay-scheduling-allocation-on-multi-channels-in-11ay
IEEE Std. 802.11-2016

## Slide 8: SP #1
Do you agree to add the following text into SFD?
  For an allocation that does not include the primary channel, its allocation information shall be completely and only included in the EDMG Extended Schedule element.
  Y/N/A

## Slide 9: SP #2
Do you agree to add the following text into SFD?
  A Scheduling Type subfield shall be added into each Channel Allocation field of the EDMG Extended Schedule element to indicate whether an allocation is based on incremental signaling or complete signaling.
  Y/N/A