## Slide 1: Fast BSS Discovery
Date: 2017-01-04
Authors:

## Slide 2: Abstract
Use of quasi-omni TX can enable fast BSS discovery in some expected 11ay scenarios
In this presentation, we propose solutions to enable fast BSS discovery using quasi-omni TX for 11ay.

## Slide 3: Introduction
Generally, quasi-omni transmission (TX) in 60 GHz is avoided due to the reduced communication range
However, employing quasi-omni transmission can reduce delays due to beamforming training during discovery and facilitate fast link setup
  Fast link setup is important for some TGay usage models [1]
First, let us consider the quasi-omni communication range

## Slide 4: Quasi-omni for AP vs STA
Friis:
General assumptions:
  AP has higher transmit power,
  AP has higher antenna gain, (= ), with more elements
  Sensitivity, , is equivalent
A potential scenario:
  AP (16 elements)
  STA (4 elements)
[AP] | Beamed (16 elements) | Quasi-Omni (single element)
(TxPower) | +10dBm | -2dBm ()
(TxAntGain) | +15dBi | +3dBi ()
 | +25dBm | +1dBm
[AP] | Beamed (16 elements) | Quasi-Omni (single element)
 | +10dBm | 
 | +15dBi | 
 | +25dBm | +1dBm
[STA] | Beamed (4 elements) | Quasi-Omni (single element)
 | +3dBm | -3dBm ()
 | +7dBi | +1dBi ()
 | +10dBm | -2dBm
[STA] | Beamed (4 elements) | Quasi-Omni (single element)
 | +3dBm | 
 | +7dBi | 
 | +10dBm | -2dBm

## Slide 5: Quasi-omni MCS0 vs Beamed MCS12
APSTA (downlink):
  vs :
    (based on Friis)
    
TxAntGainAP (16 elements)
TxPowerAP (16 elements)
RxAntGainSTA (4 elements)
Q-O MCS0:
Beamed MCS12:
Sensitivity difference (MCS0MCS12)
EIRPqomni_AP
+1dBm
+12dB
+12dB
+6dB
EIRPbeamed _AP
-25dB
+6dBm (= +1dBm +12dB +12dB +6dB -25dB)
+5dB difference

## Slide 6: Quasi-omni MCS0 vs Beamed MCS12
STAAP (uplink):
  vs :
    (based on Friis)
    
TxAntGainSTA (4 elements)
TxPowerSTA (4 elements)
RxAntGainAP (16 elements)
Q-O MCS0:
Beamed MCS12:
Sensitivity difference (MCS0MCS12)
EIRPqomni_STA
-2dBm
+6dB
+6dB
+12dB
EIRPbeamed _STA
-25dB
-3dBm (= -2dBm +6dB +6dB +12dB -25dB)
-1dB difference

## Slide 7: Quasi-omni MCS0 vs Beamed MCS12
STASTA (P2P/PBSS):
  vs :
    (based on Friis)
    
TxAntGainSTA (4 elements)
TxPowerSTA (4 elements)
RxAntGainSTA (4 elements)
Q-O MCS0:
Beamed MCS12:
Sensitivity difference (MCS0MCS12)
EIRPqomni_STA
-2dBm
+6dB
+6dB
+6dB
EIRPbeamed _STA
-25dB
-9dBm (= -2dBm +6dB +6dB +6dB -25dB)
-7dB difference

## Slide 8: Observations: quasi-omni communication range
Actual quasi-omni range depends on implementation
Considering the general relationship between quasi-omni and data MCS range, discovery based on quasi-omni TX may be effective for:
  Scenarios that require high MCS (e.g. a temporary high-speed link)
  Scenarios that feature short-range communication
  Scenarios that may include devices within a short range

## Slide 9: Quasi-omni TX based discovery proposal
We propose that the 11ay specification should include support for fast BSS discovery based on quasi-omni TX
Two ideas:
  Quasi-omni TX during the BTI
  Quasi-omni TX of probe request

## Slide 10: 1. Quasi-omni TX during the BTI
Proposal:
  Optionally include quasi-omni TX of DMG Beacon during the BTI
    New ‘Quasi-omni TX’ field indicates if the TX is quasi-omni
    TRN-R subfields may be appended for reciprocal antenna training
  If DMG Beacon with QO=1 is received and SLS is not completed during A-BFT (e.g. collision or no A-BFT), frame exchanges may proceed using quasi-omni TX
Spec changes:
  Add ‘Quasi-omni TX’ field to DMG Beacon
  Allow appending of TRN-R subfields to DMG Beacon
  Describe use of TRN-R fields appended to DMG Beacon

## Slide 11: 1. Quasi-omni TX during the BTI
Discovery Mode=1 (Active Scanning)
Discovery Mode=0 (AP/PCP)
DBcn
…
AP
STA
Discovery Mode=1
BTI
DTI
E.g. Collision or conflict
A-BFT
Quasi-Omni TX=1
AP
STA
BTI
TRN-R subfields present
DBcn
…
DBcn
TRN-R
Probe Rsp
ACK
DBcn
DBcn
DBcn
…
E.g. Collision, conflict or no A-BFT
(A-BFT)
DTI
Probe/Assoc Req
TRN-R
Quasi-Omni TX=1
ACK
Probe/Assoc Rsp
ACK
…
If antenna reciprocity is available
If antenna reciprocity is available
If antenna reciprocity is available
TRN-R subfields present
Quasi-Omni TX=1
May additionally include SSID, DMG Capabilities, etc

## Slide 12: 1. Quasi-omni TX during the BTI
Proposed new ‘Quasi-omni TX’ field:
  DMG Beacon::SSW field:
Direction
CDOWN
Sector ID
DMG Antenna ID
RXSS Length
1 bit
9 bits
6 bits
2 bits
6 bits
The RXSS Length subfield is valid only when transmitted in a CBAP and is reserved otherwise.
Quasi-omni TX
Reserved
1 bit
5 bits
RXSS Length
6 bits
In DMG Beacon

## Slide 13: 1. Quasi-omni TX during the BTI
Benefits:
  Allows discovery sequence to proceed when A-BFT SLS is not completed
    E.g. Due to conflict in schedule, collision with other STAs or absence of A-BFT
Drawbacks:
  Slight overhead to the BTI

## Slide 14: 2. Quasi-omni TX of probe request
Solution:
  Optionally transmit Probe Request by quasi-omni TX
  TRN-R subfields may be appended for reciprocal antenna training
  Probe Response is transmitted based on reciprocal antenna training or quasi-omni TX
Spec changes:
  Describe use of TRN-R fields appended to Probe Request to enable Probe Response transmission
    E.g. “A DMG STA that receives a probe request with TRN-R subfields appended to it should train its receiver antenna and subsequently select a transmit sector for transmission of the Probe Response frame based on antenna or antenna pattern reciprocity.”

## Slide 15: 2. Quasi-omni TX of probe request
Probe Req
Example sequence
AP
STA
DTI
Probe Rsp
ACK
TRN-R
If antenna reciprocity is available
…
TRN-R subfields present

## Slide 16: 2. Quasi-omni TX of probe request
Benefits:
  Enables faster and more efficient discovery of multiple STAs without overhead of sector sweep for STAs within the quasi-omni MCS0 range
Drawbacks:
  Not effective if target is outside the quasi-omni MCS0 range
  Does not provide beamforming training if antenna reciprocity is not supported

## Slide 17: Conclusion
Use of quasi-omni TX can enable fast BSS discovery in some expected 11ay scenarios
We propose to include the following solutions in 11ay:
  Quasi-omni TX during the BTI
  Quasi-omni TX of probe request

## Slide 18: References
[1] 11-15-0625-03-00ay-ieee-802-11-tgay-usage-scenarios

## Slide 19: Straw poll 1
Do you agree to insert the following in section 4 of the SFD: “The 11ay specification shall enable BSS discovery through transmitted DMG Beacon frames based on:
  Setting the Quasi-omni TX subfield to one in transmitted DMG Beacon frames to indicate the potential for discovery based on quasi-omni transmission
  Appending TRN-R subfields to transmitted DMG Beacon frames
  Transmit antenna training by an EDMG STA based on TRN-R subfields appended to a received DMG Beacon frame that has the Quasi-omni TX subfield equal to one”

## Slide 20: Straw poll 2
Do you agree to insert the following in section 4 of the SFD: “The 11ay specification shall enable BSS discovery through Probe Request based on:
  Appending TRN-R subfields to a Probe Request frame transmitted with quasi-omni antenna pattern
  Transmit antenna training by an EDMG STA based on TRN-R subfields appended to a received Probe Request frame transmitted with a quasi-omni antenna pattern”

## Slide 21: Motion 1
Instruct the editor to insert the following in section 4 of the SFD: “The 11ay specification shall enable BSS discovery through transmitted DMG Beacon frames based on:
  Setting the Quasi-omni TX subfield to one in transmitted DMG Beacon frames to indicate the potential for discovery based on quasi-omni transmission
  Appending TRN-R subfields to transmitted DMG Beacon frames
  Transmit antenna training by an EDMG STA based on TRN-R subfields appended to a received DMG Beacon frame that has the Quasi-omni TX subfield equal to one”

## Slide 22: Motion 2
Instruct the editor to insert the following in section 4 of the SFD: “The 11ay specification shall enable BSS discovery through Probe Request based on:
  Appending TRN-R subfields to a Probe Request frame transmitted with quasi-omni antenna pattern
  Transmit antenna training by an EDMG STA based on TRN-R subfields appended to a received Probe Request frame transmitted with a quasi-omni antenna pattern”