## Slide 1: PAR Verification Single BSS Simulation
Date: 2016-12-15
Authors:

## Slide 2: Summary
In this presentation, we show several UL system throughput simulation results comparing 11ac and 11ax OFDMA
As the number of STAs increases, in UL, 11ax OFDMA has more system throughput gain over 11ac
The single BSS scenario is the first step to verify 11ax’s performance. We will continue to work on multiple BSS scenario definition and simulation, and make contribution to TGax Simulation scenario and EVM documents

## Slide 3: Single BSS Simulation Setup (1/3)
Topologies
  10m x 10m area with 20 STAs
  20m x 20m area with 80 STAs
  30m x 30m area with 180 STAs
AP is at the center in the space
STAs are randomly dropped in the area
  STA density is the same of the 3 topologies

## Slide 4: Single BSS Simulation Setup (2/3)
PHY abstraction and SINR calculation
  Follow 11ax evaluation methodology [1]
MAC protocols, such as CCA, back-off, trigger frame, and etc.
  Based on 11ax draft D1.0 [2]
General settings
Parameters | Default Value
Traffic type | Full buffer UDP UL traffic
UDP packet size | 100 Bytes
AP/STA # of TX/TX antenna | 1
Access Protocol parameters | EDCA with default parameters
Bandwidth | 80 MHz
Aggregation | 64 MPDU per AMPDU
RTS/CTS | No

## Slide 5: Single BSS Simulation Setup (3/3)
Access category setting
  1/3 STAs are AC_VI (15, 31)
  1/3 STAs are AC_VO (7, 15)
  1/3 STAs are AC_BE (31, 1023)
MCS setting
  11ac: Genie helped, best MCS to reach just under 10% PER (distance dependent)
  11ax OFDMA: MCS9
OFDMA (80MHz)
  8 106-tone RU users
  5 26-tone RU users
OFDMA scheduling
  For each RU, AP selects a STA randomly

## Slide 6: Topology 1: 20 STAs
UL System throughput
  11ac 70.14 Mbps
  11ax OFDMA 198.74 Mbps
  11ax OFDMA has 2.83 times gain over 11ac
Throughput Histogram
  11ac
    Three groups’ throughputs
      VO (Mean: 6.8 Mbps)
      VI (Mean: 2.45 Mbps)
      BE (Mean: 0.17 Mbps)
  11ax
    All STAs have similar throughputs because of no priority scheduling
    Mean throughput 9.93 Mbps
Throughput Histogram 20 STAs
VO
VI
BE
11ac
11ax
10m
10m

## Slide 7: Throughput CDF of 20 STAs
CDF
5% percentile throughput
  11ac 0.017 Mbps
  11ax OFDMA 9.87 Mbps

## Slide 8: Topology 2: 80 STAs
UL System throughput
  11ac 39.3 Mbps
  11ax OFDMA 180.0 Mbps
  11ax OFDMA has 4.58 times gain over 11ac
Throughput Histogram
  11ac
    Three groups’ throughputs
      VO (Mean: 0.95 Mbps)
      VI (Mean: 0.41 Mbps)
      BE (Mean: 0.04 Mbps)
  11ax
    Most STAs have similar throughputs because of no priority scheduling
    Some STAs have a little worse throughputs due to their longer distance to AP
    Mean throughput 2.25 Mbps
Throughput Histogram 80 STAs
11ac
11ax
20m
20m

## Slide 9: Throughput CDF of 80 STAs
CDF
5% percentile throughput
  11ac 0.02 Mbps
  11ax OFDMA 2.09 Mbps

## Slide 10: Topology 3: 180 STAs
UL System throughput
  11ac 12.51 Mbps
  11ax OFDMA 138.95 Mbps
  11ax OFDMA has 11.1 times gain over 11ac
Throughput Histogram
  11ac
    Three groups’ throughputs
      VO (Mean: 0.14 Mbps)
      VI (Mean: 0.058 Mbps)
      BE (Mean: 0.001 Mbps)
    BE STAs has almost zero throughput
  11ax
    Most STAs have similar throughputs because of no priority scheduling
    Some STAs have a little worse throughputs due to their longer distance to AP
    Mean throughput 0.77 Mbps
Throughput Histogram 180 STAs
11ac
11ax
30m
30m

## Slide 11: Throughput CDF of 180 STAs
CDF
5% percentile throughput
  11ac 0 Mbps
  11ax OFDMA 0.67 Mbps

## Slide 12: Discussion
For 11ac
  Contention and collision determine the system throughput
  As the number of STA increases, high priority AC STAs grab all UL opportunities with serious collisions
    Overall throughput drops a lot (70.14 -> 39.3 -> 12.51)
    AC BE STAs almost cannot transmit. 5% percentile throughput is closed to zero
For 11ax OFDMA
  No collision
  As the number of STA increases,
    OFDMA can maintain a stable UL system throughput
    The system throughput drops because there are more distant STAs and their PERs are higher
  AP may determine STA’s UL throughput by scheduling
  5% percentile throughput is determined by AP’s scheduling

## Slide 13: Next Step
11ax shall not only improve system throughputs of single BSS scenarios
We will continue working on multiple BSS scenario definition and simulation, and make contribution to TGax Simulation scenario and EVM documents

## Slide 14: References
11-14-0571-12-00ax-evaluation-methodology.docx
Draft P802.11ax_D1.0.pdf