## Slide 1: Pre-Association Negotiation of Management Frame Protection (PANMFP)
Date: 2017-03-01
Authors:

## Slide 2: Background
Motivation for FTM Security
  Integrity of measurement and location
    Requires management and control frame protection
  Location and ranging privacy
    Management frame protection
Earlier Contributions (See references)
  FTM Security Enhancements (16/1020r0)
  Security Requirements (16/1256r1)
  FTM Security in Associated and Un-associated States (16/1498r1)
Group interest in more detail
  Protection in Un-associated state
  Mechanism allows any management frame to be protected
  Using standard MFP after key derivation whether associated or not
Slide 2

## Slide 3: Introduction
We believe
  Standard Management Frame Protection (MFP) i.e. using AES-xCMP should be leveraged to protect management frames pre and post association
    Protect FTM/Location
    Protect additional discovery mechanisms (e.g. Service Discovery)
    Additional privacy pre-association
  Possible in Un-associated state with extensions to key negotiation protocol(s)
PANMFP protocol is presented here
  Not discussed in this presentation
    Control frame protection, but it can leverage MFP
    Mechanisms to protect against physical layer attacks
Slide 3

## Slide 4: PANMFP Authentication Protocol
Slide 4
non-AP STA
AP
Beacon(RSNIE(PANMFP))
Auth(1, PANMFP, PMKID(s), DH-S(FCG, FFE) or SNonce, RSNIE, Wrapped Data)
Auth(3, PANMFP, MIC)
Auth(2, PANMFP, PMKID, DH-A(FCG, FFE) or ANonce, Wrapped Data, MIC)

## Slide 5: PANMFP Authentication Protocol
RSN IE advertises PANMFP AKM
PANMFP 802.11 authentication protocol establishes a PTK
  Mutual authentication
  Includes key confirmation
  Optional support for PFS
  Use existing elements - FCG, FFE, Wrapped Data, MIC
Management frame protection using the PTK
  Unicast frame protection only
  Protect robust action frames and de-authentication frame
Slide 5

## Slide 6: PANMFP Authentication Protocol
Authentication Frame 1
  PMKID(s) identifying possible PMK(s)
    from initial Security Association to another AP in ESS
      can use any AKM for initial SA
      identified in RSN IE
  Allow for DH or Nonces to derive PTK
  Optionally allow Wrapped Data - can carry EAP-rp as in FILS
Slide 6

## Slide 7: PANMFP Authentication Protocol
Authentication Frame 2
  PMKID identifying the PMK
  Optionally allow Wrapped Data - can carry EAP-rp as in FILS
  MIC protects the frame
    AP derives PTK before sending the frame
    DH public values or nonces are integrity protected using PTK (KCK)
    KCK used with CMAC or HMAC-SHA-xxx where xxx is 384 or 256 as determined by RSNIE
  Example key derivation(s)
PTK without PFS = KDF-Hash-Length(PMK, “PANMFP-PTK”, SNonce||ANonce||BSSID||STA-Addr)
PTK with PFS = KDF-Hash-Length(PMK, “PANMFP-PTK”, DH-shared-secret||BSSID||STA-Addr)
    MIC lengths of 16 or 24 octets as in [1]
    KCK length is per AKM in the RSNIE
    KEK not used
Slide 7

## Slide 8: PANMFP Authentication Protocol
Authentication Frame 3
  Completes key confirmation with MIC
  Keys installed on AP after the frame is ACK’d
  Keys installed on non-AP STA after the frame ACK is received
Slide 8

## Slide 9: Expected changes to 802.11 Spec
AKM selector for PANMFP AKM (Table 9-133)
Algorithm Assigned Number for PANMFP
PANMFP Key derivation and hierarchy (12.7.1.x)
PANMFP Authentication Protocol (12.x)
  frame generation and processing on STA and AP
Frame filtering
  Robust action frames are class 2 when SA established by PANMFP is present
FTM negotiation
  Advertise secure FTM capabilities (Extended Capabilities IE)
  Negotiate secure FTM use (FTM parameters)
  Secure FTM relies on PANMFP and standard MFP
FTM Security Considerations
Slide 9

## Slide 10: Questions & Discussion
Can we use SAE
  No, since SAE derives PMK only
What about FILS
  Used for initial authentication only
  Key confirmation part of association
  Wrapped data can be used to execute EAP-rp protocol to derive PMK
What about FBT
  PMK-r1 can be used as PMK in PANMFP
How is PMK distributed
  No new mechanisms for PMK distribution.
Can we work with no PMK
  Possibly, similar to OWE
Changes to 802.11 state machine
  Not required, but filtering rules change
Slide 10

## Slide 11: Questions & Discussion
Do we need replay protection for negotiation
  No, renegotiate with new Nonces or FFEs
Can association follow PANMFP authentication and data frame protection using keys derived via PANMFP
  No, must 802.11 re-authenticate, re-associate and establish an RSN SA that is not from PANMFP
Can Authentication happen with Public Keys and Certificates instead of a PMK
  Yes, but not in the scope of this proposal
Can the key be negotiated in two messages
  No, since the first message may not be protected and needs to be confirmed
Slide 11

## Slide 12: Summary
FTM/11az needs security
FTM frame protection should use standard MFP
Presented a pre-association protocol
  To establish keys to protect FTM and other frames prior to association
  Independent of FTM
    Can possibly protect other frames
Slide 12

## Slide 13: Straw Poll
The 802.11 authentication method described here should be used for negotiating pre-association security (Keys, SA) used to secure FTM
  Agree:
  Disagree:
  Abstain:
Slide 13

## Slide 14: References
[1] IEEE Std 802.11 REVmc_D8.0, IEEE Standard for Information Technology – Telecommunications and information exchange between systems, local and metropolitan area networks – Specific requirements, Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications
[2] “Proposed 802.11az Functional Requirements”, IEEE 802.11-16/424r3
[3] IEEE 802.11-16/1020r0, Q. Wang, et. al., “Security Enhancement to FTM”, July 2016
[4] IEEE 802.11-16/1256-01-00az, Qi Wang et. al., Functional Requirement for Secure Ranging
[5] IEEE 802.11-16/1498-01-00az, Qi Wang et. al., FTM Security in Associated and Un-sssociated States
Slide 14