## Slide 1: NDP Short Feedback Design
Date: 2017-03-13
Authors:

## Slide 2: Background (1)
It is well accepted that being able to get a very short simultaneous feedback from a high number of STAs (all STAs) improve the 11ax system and power efficiencies [1], [3]
  Many feedbacks require 1 bit: PS-Poll (power efficiency), Channel Availability (collisions avoidance)
  Other feedbacks could be 2 bit. For example: “How many buffered Bytes for transmission: 0, 1 to 1000, 1000 to 5000, > 5000 ?”
  A short simultaneous resource request feedback (1 or several bits) capable of supporting a high number of STAs is needed for an efficient UL MU simultaneous scheduling in addition to the existing (or enhanced) piggybacked buffer information
  Less overhead for resource request feedback than polling method
  Low and stable latency for resource request feedback, compared to possibly high and unpredictable latency with CSMA-CA in dense environments

## Slide 3: Background (2)
In Nov. 2016, added subclause 25.5.2.7 to the spec: 25.5.2.7 NDP feedback report procedure The NDP feedback report is a mechanism for an HE AP to collect short feedbacks from a very high number of HE STAs, in an efficient manner. The feedbacks (e.g. resource requests) are sent without data payloads in response to a Trigger frame. The feedbacks are not for channel sounding. This mechanism is optional for non-AP STA.
But details of the NDP feedback mechanism are TBD
This contribution propose a signaling technique for the NDP feedback mechanism that can handle a high number of STAs and is power and air time efficient

## Slide 4: How to define the NDP feedback mechanism?
UL MU transmission in response to a trigger frame
Use frequency dimension for many small orthogonal allocations
To avoid collisions, assign orthogonal allocations to users
No data payload (NDP), STAs transmit energy on one orthogonal allocation for feedback
  with spreading gain in time domain for PHY robustness
For minimal changes to the current PHY, we propose
  to use UL MU NDP simultaneous transmissions in response to a trigger frame; and
  define orthogonal allocations tone sets to multiplex different STAs’ feedbacks

## Slide 5: Overview of proposed signaling for Short Feedback (1 of 3)
Define tone sets that spread a 242RU  provides diversity and enables the AP to estimate AGC value based on HE-STF spread over a 242RU
For compatibility with 20 MHz only STAs, to minimize degradation from DC offset and CFO, signaling use tones in each 20 MHz with indices: [-113:-6, 6:113]
To minimize change, use HE-LTF sequence [2]
  20 MHz only STA: 20 MHz 12.8 us 4x HE-LTF
  40 MHz STA: 40 MHz 12.8 us 4x HE-LTF
  80 MHz STA: 80 MHz 12.8 us 4x HE-LTF
Two sets of 6 tones are used to transmit 1 bit
  b0 = 1  Send energy on first 6 tones set
  b0 = 0  Send energy on complementary 6 tones set
Four sets of 6 tones are used to transmit 2 bits

## Slide 6: Overview of proposed signaling for Short Feedback (2 of 3)
High power mode - four sets of tones can also be used to transmit one bit to enable higher transmit power by 3dB in PSD limited regions by duplicating the response on b1 and b0: STAs send b0=b1=1 or b0=b1=0
Puncture HE-LTF sequence except for tones at indices IULf
For same power between HE-STF and tone sets, boost per tone power relative to the target RSSI
  1 bit (6 tones): 10*log10(242/6) = 16.06 dB above target RSSI
  2 bit (12 tones): 10*log10(242/12) = 13.05 dB above target RSSI
Multiply punctured HE-LTF sequence by the P-matrix row corresponding to a specific spatial stream (SS)
  Allow multiplexing of multiple users
  Use 1x1, 2x2 or 4x4 P-matrix, 1 ≤ Nss ≤ 4
    Corresponding to 1, 2 or 4 time-domain symbols

## Slide 7: Overview of proposed signaling for Short Feedback (3 of 3)
AP and STAs have a prior agreement on tone sets and P-matrix spreading to use for a given response
Complementary tone set are adjacent
  Noise like interference will add power in both bins, biasing RX decision toward a “No Response” instead of a “1” or “0”
  Non-coherent CW interference (not aligned to tone grid) will bias RX decision toward a “No Response” instead of a “1” or “0
Detection at RX does not need a Channel Estimate
  RX does not care about sequence in tone set
  RX detect energy in one tone set and compare to energy in complementary tone set

## Slide 8: Proposed feedback schemes
Multiplex different users with P-matrix code (and potentially different tone sets);
Separate different states of the same user with different tone sets.
Two sets of 6 tones are used to transmit 1 bit:
  If bx = 1, send energy on first tone set and quiet on second tone set
  If bx = 0, send energy on second tone set and quiet on first tone set

## Slide 9: Tone set indices for each 20 MHz: IULf
P-Matrix 1x1 | P-Matrix 2x2 | P-Matrix 4x4 | 2 bit or 1 bit high power |  |  |  | 
 |  |  | 1 bit |  |  |  | 
Tone sets | Tone sets | Tone sets | b0 = 1 | b0 = 0 |  | b1 = 1 | b1 = 0
1 | 1,2 | 1,2,3,4 | -113,-77,-41,6,42,78 | -112,-76,-40,7,43,79 |  | -95,-59,-23,24,60,96 | -94,-58,-22,25,61,97
2 | : | : | -111,-75,-39,8,44,80 | -110,-74,-38,9,45,81 |  | -93,-57,-21,26,62,98 | -92,-56,-20,27,63,99
3 | : | : | -109,-73,-37,10,46,82 | -108,-72,-36,11,47,83 |  | -91,-55,-19,28,64,100 | -90,-54,-18,29,65,101
4 | : | : | -107,-71,-35,12,48,84 | -106,-70,-34,13,49,85 |  | -89,-53,-17,30,66,102 | -88,-52,-16,31,67,103
5 | : | : | -105,-69,-33,14,50,86 | -104,-68,-32,15,51,87 |  | -87,-51,-15,32,68,104 | -86,-50,-14,33,69,105
6 | : | : | -103,-67,-31,16,52,88 | -102,-66,-30,17,53,89 |  | -85,-49,-13,34,70,106 | -84,-48,-12,35,71,107
7 | : | : | -101,-65,-29,18,54,90 | -100,-64,-28,19,55,91 |  | -83,-47,-11,36,72,108 | -82,-46,-10,37,73,109
8 | : | : | -99,-63,-27,20,56,92 | -98,-62,-26,21,57,93 |  | -81,-45,-9,38,74,110 | -80,-44,-8,39,75,111
9 | 17,18 | 33,34,35,36 | -97,-61,-25,22,58,94 | -96,-60,-24,23,59,95 |  | -79,-43,-7,40,76,112 | -78,-42,-6,41,77,113
10 | 19,20 | 37,38,39,40 | -95,-59,-23,24,60,96 | -94,-58,-22,25,61,97 |  |  | 
11 | : | : | -93,-57,-21,26,62,98 | -92,-56,-20,27,63,99 |  |  | 
12 | : | : | -91,-55,-19,28,64,100 | -90,-54,-18,29,65,101 |  |  | 
13 | : | : | -89,-53,-17,30,66,102 | -88,-52,-16,31,67,103 |  |  | 
14 | : | : | -87,-51,-15,32,68,104 | -86,-50,-14,33,69,105 |  |  | 
15 | : | : | -85,-49,-13,34,70,106 | -84,-48,-12,35,71,107 |  |  | 
16 | : | : | -83,-47,-11,36,72,108 | -82,-46,-10,37,73,109 |  |  | 
17 | : | : | -81,-45,-9,38,74,110 | -80,-44,-8,39,75,111 |  |  | 
18 | 35,36 | 69,70,71,72 | -79,-43,-7,40,76,112 | -78,-42,-6,41,77,113 |  |  | 

## Slide 10: Tone set indices for 20, 40, 80 and 160 MHz
20 MHz tones used for UL feedback (up to 216 tones)
  IULf
40 MHz tones used for UL feedback (up to 432 tones)
  IULf - 128, IULf + 128
80 MHz tones used for UL feedback (864 tones)
  IULf - 384, IULf - 128, IULf + 128, IULf + 384
80+80 MHz, 160 MHz tones used for UL feedback (up to 1728 tones)
  Same as 80 MHz on lower and upper 80 MHz

## Slide 11: Max # of STAs that can simultaneously send the UL Short Feedback
BW | Response = 1 bit |  |  | Response = 2 bit |  | 
 | Nss = 1 | Nss = 2 | Nss = 4 | Nss = 1 | Nss = 2 | Nss = 4
20 MHz | 18 | 36 | 72 | 9 | 18 | 36
40 MHz | 36 | 72 | 144 | 18 | 36 | 72
80 MHz | 74 | 148 | 296 | 37 | 74 | 148
160 MHz | 148 | 296 | 592 | 74 | 148 | 296

## Slide 12: Further discussion on the proposed feedback mechanism
Spreading gain from SS improve performance and reliability:
    One symbol, Nss = 1  0 dB 1x1 P-matrix
    Two symbols, Nss = 2  3.01 dB 2x2 P-matrix
    Four symbols, Nss = 3, 4  6.02 dB 4x4 P-matrix
No collisions between STAs
  AP assign to each STA:
    a unique SS and sets of 6 tones
      For 1 bit response, assign 2 sets of 6 tones
      For 2 bit response, assign 4 sets of 6 tones
      For PSD limited 1 bit response, assign 4 sets of 6 tones

## Slide 13: Feedback Signal Properties
Channel estimation is not required for detection
Detection performance is independent of sequence
  AP is not required to have prior knowledge of feedback sequence
Signal is robust to interference and channel response
Trivial detection, no adaptive threshold adjustment
  Compare sum of power between sets of complementary 6 tones
Detection in unaffected by timing offset
  With the +/-400 ns timing accuracy and a 120 m radius, there is up to 1.6 us of timing offset.
A “No response” from STA can be easily detected
  A “No response” from a STA could mean STA did not received the query, is out of range or the AP did not decode properly the feedback response.
  In interference prone environments, responses from STAs could be missed. AP can identify STAs with “No response” and treats them accordingly

## Slide 14: Example of Detection Algorithm
Processing for each P-matrix row:
  De-spreading
  Sum power per set of 6 tones
  Compare powers between complementary tone sets for decision
Detection algorithm for b0 (3 outcomes)
  P1 = sum(power in b0 = 1 tone locations)
  P0 = sum(power in b0 = 0 tone locations)
  K = 3; % Suggested decision scaling factor
  ( P1 > K∙P0 )  b0 = 1
  ( P0 > K∙P1 )  b0 = 0
  not( P1 > K∙P0 ) & not( P0 > K∙P1 )  No response

## Slide 15: Simulations

## Slide 16: Flat channel, 1 TX and 1 RX, Nss = 4
P(NoResp  YES/NO) = 2.29e-2
1 bit, 6 tones: Boost = +16.06 dB, K = 3
2 bits 12 tones: Boost = +13.05 dB, K = 3
Probability of Error CFO=0
6 tones with 1 bit
12 tones with 2 bits
If tones are not boosted,
this is SNR = 0 dB

## Slide 17: 6 tones sequence Channel Sims
1x4 (TX antennas x RX antennas)
Nss = 4
Channel D: SNR is for the ensemble of channel realizations
Timing offset added
  +400 ns of timing error plus round trip delay for 100 m
CFO and Power imbalance added
4 RX signals are equally combined
  With flat channel and MIS=10-2, gain of 4 RX vs. 1 RX is around 1.8 dB
  With channel D and MIS=10-2, gain of 4 RX vs. 1 RX is around 4.5 dB
Worst case analysis;
  STA #1 reply b0 = 1 and STA #2 to #4 replies b0 = 0
  Select tone locations that maximize crosstalk
    b0 = 1  Tones locations: -113,-77,-41,6,42,78
    b0 = 0  Tones locations: -112,-76,-40,7,43,79

## Slide 18: STA #1 Probability Mis & False, Nss = 4, Channel D with CFO & Time Offset
4 STAs with 1 TX antenna
AP with 4 RX antennas
CP: 1.6 us, Time offset: 1.0667 us
#1 send b0 = 1, #2 to #4 send b0 = 0
#1 to #4 power: [0, +5, +10, +15] dB
#1 to #4 CFO: [-400, +400, -400, +400] Hz
Signal power normalized for the realization ensemble
Time offset is 400ns of timing error plus 100m round-trip
6 tones: Boost = +16.06 dB, K = 3
If tones are not boosted,
this is SNR = 0 dB

## Slide 19: Summary
Define an NDP short feedback report mechanism based on 6 tone sets per 20 MHz
One bit of response requires 2 or 4 sets
Two bits of response requires 4 sets.
Users are multiplexed in the frequency and time using P matrix.
The design has the following attributes:
  Frequency spreading of tone set and complementary tone set are adjacent; makes the RX detection insensitive to the Channel frequency response
  Detection algorithm is independent of RX level, P-Matrix size (i.e. number of symbols), number of RX antennas and Sequence
  Detection is robust to interference
  Feedback response is an affirmative bn = 1 or bn = 0
  For SNR ≥ -24 dB, False detection rate is very small (< 10-6)
  6 tones sequence PAPR is between 4.26 to 7.78 dB. Median is 4.60 dB
  12 tones sequence PAPR is between 4.36 to 10.78 dB. Median is 5.88 dB

## Slide 20: References
[1] IEEE 802.11-16/1367r0: NDP feedback report
[2] IEEE 802.11-15/1334r1: HE-LTF sequence design
[3] IEEE 11-16-0xxx-00-00ax-Proposed spec text for NDP feedback report

## Slide 21: Straw poll #1
Do you agree to add to the spec: The NDP short feedback report is based on STA populating sets of 6 tones as defined below. Time domain P matrix spreading (2x2 and 4x4) is used to enhance reliability and/or multiplex users
????Add more details here????

## Slide 22: Appendix

## Slide 23: Tones alignment between 20 MHz only STAs and 40/80 MHz STAs
Four 20 MHz only STAs
80 MHz
40 MHz
Tones at [-116:-2, 2:116]
are common to 20 MHz only, 40 and 80 MHz tone plan