## Slide 1: EDMG A-PPDU for 11ay SC mode
Date: 2017-01-17
Authors:

## Slide 2: Abstract
11ad supports DMG A-PPDU [1].
In this presentation, we propose EDMG A-PPDU for 11ay SC mode.

## Slide 3: Overview of EDMG A-PPDU Aggregation
EDMG A-PPDU aggregation is constructed in a similar manner to DMG A-PPDU.
  An EDMG A-PPDU is a sequence of two or more EDMG PPDUs transmitted without IFS, legacy preamble, and with a PHY-dependent separation between EDMG PPDU transmissions.
    The L-STF, the L-CEF, the L-Header, the EDMG-STF and the EDMG-CEF exist in the 1st PPDU only.
  All MPDUs within A-MPDUs within an EDMG A-PPDU shall have the same values for the TA field and RA fields.
    EDMG A-PPDU is used in SU transmission only.
  The transmission duration of an EDMG A-PPDU shall be no greater than aPPDUMaxTime.

## Slide 4: Necessity of EDMG A-PPDU aggregation
Increase flexibility
  11ay supports Multi-TID A-MPDU [2]. Different TID implies a demand for use of different MCS. Multi-TID A-MPDU can’t change MCS during a packet. On the other hand A-PPDU may use different MCS for different TID.
    Since the transmitter can not receive feedback from the receiver during A-PPDU transmission, the transmitter autonomously change MCS.
Increase Data rate of A-PPDU
  The data rate of 11ad is up to 6.7Gbps. 11ay may support ~100Gbps.

## Slide 5: EDMG A-PPDU Aggregation for CB
In channel bonding case, the EDMG-Header-A is transmitted with same bandwidth as corresponding data field except the 1st EDMG-Header-A.
  Since PPDUs except the 1st PPDU within the EDMG A-PPDU don’t compose L-STF and EDMG-STF, wideband transmission of EDMG Header-A is reasonable.

## Slide 6: Additional EDMG PPDU field
L-Header based EDMG A-PPDU aggregation shall be prohibited.
  Even if the L-Header is used to indicate the EDMG A-PPDU aggregation, the legacy device can’t receive the 2nd L-Header in the EDMG A-PPDU. The legacy device might malfunction.
To indicate the EDMG A-PPDU aggregation, “Additional EDMG PPDU field (1bit)” is needed in the EDMG-Header-A.
Field Name | Number of bits | Description
Additional EDMG PPDU | 1 | A value of 1 indicates that this EDMG PPDU is immediately followed by another EDMG PPDU. A value of 0 indicates that no additional EDMG PPDU follows this EDMG PPDU.

## Slide 7: EDMG-Header-A Encoding and Modulation for EDMG A-PPDU in SC mode
The encoding and modulation method for EDMG-Header-A in the EDMG A-PPDU is almost same as the one for the single EDMG PPDU transmission.
The difference is repetition after BPSK mapping. The BPSK symbol block blk is repeated NCB (NCB : channel bonding factor) times to support different channel bonding factors [3].
  NCB =2: [Ga128, blk, blk]
  NCB =3: [Ga192, blk, blk, blk]
  NCB =4: [Ga256, blk, blk, blk, blk]
The repetition is applied to the EDMG-Header-A except the 1st EDMG-Header-A.

## Slide 8: Conclusion
We propose the frame format, the additional fields in EDMG Header-A, and EDMG Header-A encoding and the modulation method for EDMG A-PPDU in 11ay SC mode.

## Slide 9: References
[1] 802.11-2016
[2] 11-16/0932r0 Multi-TID Aggregation for 11ay
[3] 11-16/0989r0 EDMG Header-B Encoding and Modulation for SC PHY in 11ay

## Slide 10: SP #1
Do you agree to insert the following in the 11ay SFD? "11ay specification shall define EDMG SU PPDU aggregation."

## Slide 11: SP #2
Do you agree with the EDMG A-PPDU formats shown in slide 3 and 5 of 11-17/0051r3 for 11ay SC mode?
  For single 2.16 GHz channel and channel aggregation
  For channel bonding

## Slide 12: SP #3
Do you agree to add “Additional EDMG PPDU field” to the EDMG-Header-A?
Field Name | Number of bits | Description
Additional EDMG PPDU | 1 | A value of 1 indicates that this EDMG PPDU is immediately followed by another EDMG PPDU. A value of 0 indicates that no additional EDMG PPDU follows this EDMG PPDU.

## Slide 13: SP #4
Do you agree with the coding and modulation method shown in slide 7 of 11-17/0051r3 for EDMG-Header-A within the EDMG A-PPDU transmitted with the same bandwidth as the corresponding data field in 11ay SC mode?