## Slide 1: WUR MAC issues
Date: 2017-01-15
Authors:
Name | Affiliation | Address | Phone | Email
Jeongki Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | jeongki.kim@lge.com
Kiseon Ryu |  |  |  | kiseon.ryu@lge.com
Jayh Park |  |  |  | hyunh.park@lge.com
Suhwook Kim |  |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Abstract
The overall MAC procedure for WUR was introduced at the last meeting [1]
This discusses the details of some WUR MAC issues
  Broadcast Wake-up
  Group Wake-up and Multi-User Wake-up
  WUP (Wake Up Packet) contents design

## Slide 3: Broadcast Wake-up (1/2)
Broadcast WUP can be sent before sending group address BU
  To wake up all WUR mode STAs
In legacy WLAN, group addressed BU is generally sent after DTIM
Broadcast WUP should be sent early with enough time for WUR mode STAs to receive DTIM/GA BU correctly after its wake up delay because Broadcast WUP TX can be delayed if channel is busy
Each STA’s wake up delay could be different according to each STA capability or environment (e.g., temperature, humidity, etc.)
Broadcast Wakeup
AP
STA1
STA2
STA3
STA4
Wakeup delay
DTIM
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on
Waiting time

## Slide 4: Broadcast Wake-up (2/2)
AP (or WUR Transmitter) includes Wake up Completion Time (WCT) in Broadcast WUP
  WCT: Indicates the time which WUR mode STA should finish its wake up procedure (e.g., TBTT or Group addressed BU TX start time)
Each WUR mode STA decides its WLAN-On start time based on the received WCT value and its wake up delay
Wake up start time of STA 3, 4
Wake up start time of STA 1, 2
Broadcast Wakeup
(WCT)
AP
STA1
STA2
STA3
STA4
Wakeup delay
DTIM
Group addressed BU
WLAN on
WLAN on
WLAN on
WLAN on

## Slide 5: Group wake up and MU wake up (1/2)
Group wake up
  Group wake up can be used for waking up all STAs belonging to a group
    E.g., Group ID or multicast address
  May not be efficient if it is used for waking up a part of STAs in a group
WUP
(GID =1)
AP
STA1
STA2
STA3
STA4
WLAN on
Wakeup delay
MU PPDU (STA 1, 2, 3)
STA1, 2, 3, 4, 5 belong to Group 1 (GID=1)
STA5
PS-Polls from STA 1~5
Unnecessary power consumption
Unnecessary power consumption

## Slide 6: Group wake up and MU wake up (2/2)
Multi-User (MU) wake up
  WUR need to support MU wake-up mode for waking up a part of STAs in a group
  Example 1) WUP may contain multiple receiver IDs  the WU packet size is increased according to the number of STAs
  Example 2) WUP may contain TIM
    TIM size should be optimized (e.g., like 11ah hierarchical TIM, using WUR ID1) instead of AID)
WUP (TIM :STA 1, 2, 3)
AP
STA1
STA2
STA3
STA4
WLAN on
Wakeup delay
MU PPDU (STA 1, 2, 3)
1) WUR ID can be allocated when entering WUR mode
STA5
PS-Polls from STA 1~3

## Slide 7: Wakeup Packet contents design (1/3)
Considerations on Wakeup Packet (WUP) design
  WUP TX frequency as small as possible to minimize the contention with other WLANs/WUPs  Broadcast/Group/MU wake up
  WUP content size should be minimized (e.g., if OOK is used, 1 symbol (4us) is used for delivering 1 bit)  WUP optimization
  Avoid unnecessary false alarm of wake-up  MU wake-up
  Including WUR operation mode (WOM) information which indicates whether the STA wakes up after receiving the WUP or not
    WUP may be sent for just keep alive check or synchronization
      In this case STA does not need to wake up

## Slide 8: Wakeup Packet contents design (2/3)
Option 1
  Transmitter ID (e.g., BSS Color or BSSID)
  Receiver ID (e.g., AID)
    Individual ID, Broadcast ID, Group ID, TIM indication (Special value)
    WUR ID can be used to identify a WUR mode STA instead of AID
      e.g., WUR ID is allocated when entering WUR mode
  WOM(WUR Operation Mode): 0- No wake-up, 1-Wake-up
  Other information can be present optionally
    E.g., TIM
WUR Preamble (e.g., sequence)
WUP contents
L-Part (e.g., L-STF/LTF/SIG)
Receiver ID
(e.g., AID)
Transmitter ID
(e.g., BSS Color)
WOM
Other information (optional)

## Slide 9: Wakeup Packet contents design (3/3)
Option 2
  Frame Type
    0: Broadcast wake-up
    1: Individual wake-up, Individual ID is included as receiver ID
    2: Group wake-up, Group ID is included as receiver ID
    3: MU wake-up, TIM or multiple IDs set are included
Frame Type
Transmitter ID
WOM1)
Other information (optional)
Receiver ID
(optional)
WUR Preamble (e.g., sequence)
WUP contents
L-Part (e.g., L-STF/LTF/SIG)
FT=0
Transmitter ID
WOM
Other information (optional)
FT=1
Transmitter ID
WOM
Other information (optional)
FT=2
Transmitter ID
FT=3
Transmitter ID
WOM
Other information (optional)
Individual ID
WOM
Other information (optional)
Group ID
TIM
Not including receiver ID
1) WOM can be delivered implicitly (e.g., by Frame Type)

## Slide 10: Conclusion
To avoid inefficient WUR packet transmission, WUR needs to consider Broadcast/Group/Multi-user wake-up
  In this case, need to minimize power consumption of WUR mode STAs by avoiding false alarm of wake-up (MU wake-up)
Need to consider the followings in WU packet design
  Less frequent WUR packet TXs
  Optimized WUR packet
  Less false alarm
  WUR operation mode (Wake-up or No wake-up) indication

## Slide 11: References
[1]11-16/1445r1, Overall MAC Procedure for WUR
[2]11-16/0036r2, WUR Frame Structure

## Slide 12: Straw Poll 1
Do you agree that the wake-up packet to wake up all WUR mode STAs need to be considered in 11ba TG?
Result: Y/N/A: 24/1/12

## Slide 13: Straw Poll 2
Do you agree that multicast wake-up need to be considered in 11ba TG?
Result: Y/N/A: 23/3/10.

## Slide 14: Motion 1
Move to add to SFD
  802.11ba spec shall define a mechanism to wake up all WUR mode STAs (i.e., broadcast wake-up frame)
Mover: Jeongki Kim
Second: Jinsoo Choi

## Slide 15: Motion 2
Move to adopt the following to SFD
  802.11ba spec shall define a mechanism to wake up multiple WUR mode STAs (e.g., multi-user wake-up frame)
Mover: Jeongki Kim
Second: Jinsoo Choi